IEEE P802.11
Wireless LANs

Proposed Baseline Text for the Interleaving of MAC Level FEC

Date:  	March 14, 2001

Author:	Christopher Hansen

Raju Gubbi
	Broadcom
	Address: 400 E. Caribbean Drive, Sunnyvale, CA 94089
	Phone: (408) 543-3378
	Fax: (408) 543-3399
	e-Mail:  chansen@broadcom.com

Abstract

This document contains proposed text for the addition of interleaving to the MAC Level FEC

## 7.5.x Interleaving within FEC Frames

- The Reed-Solomon encoded Frame Body will be interleaved on a with a block interleaver. The width of the interleaver (row size) is N = 224 octets (112 words) and the depth (column size), M, is equal to the length of the frame body in words divided by 112. If the calculated depth, M, is not an integer then it is rounded up to the next higher integer.  The encoded Frame Body is written into the interleaver in words on a row-by-row basis.  It is read out of the interleaver in words on a column-by-column basis.

Figure XXX – MAC Body FEC Interleaver

# Text boxes

c0(0) c1(0) ,c0(1) c1(1), … ,cN-2(M-1) cN-1(M-1)

c0(M) c1(M)

cN-2(M) cN-1(M)

c0(M) c1(M)

c2(1) c3(1)

c2(0) c3(0)

cN-2(1) cN-1(1)

c0(1) c1(1)

cN-2(0) cN-1(0)

c0(0) c1(0)

c0(0) c1(0) ,c2(0) c3(0), … ,cN-2(M-1) cN-1(M-1)

Read out octets as columns

Write in octets as rows