IEEE P802.11
Wireless LANs

# Normative Text for TXOP Ending rule

Date:                                         November 13, 2001

Author:          S. Kandala1, S. Choi2, K. Nakashima1, Y. Ohtani1, S. Terada1, J. del Prado2

1Sharp Corporation, 2Philips
 
                       e-Mail: srini@sharplabs.com & sunghyun.choi@philips.com

# Abstract

This document contains the material proposed to Tge for inclusion in the draft in the form of insertions into and replacements for material in of IEEE std 802.11-1999, as updated by IEEE STd 802.11e/D1.3, October 2001.

Editorial notes appear in bold italic Times New Roman font, informative notes appear in normal Arial font, and normative text appears in normal Times New Roman font.  Open issues are highlighted using red text in normal Arial font, and begin with "OPEN ISSUE:".  Changes to existing text in current standard are shown underlined and in red for additions and red with strikethrough for deletions.

# Insert the following paragraph at the end of Clause 9.10.2 (after the Note) immediately above clause 9.10.2.1 as follows:

Within a polled TXOP, if there will be potentially any time left in the TXOP after the transmission of the final frame and its expected ACK response, then the recipient of this final frame shall be HC. If there are no frames to be sent to the HC, then the WSTA shall send a QoS Null with No Ack bit set to 0 to the HC.  If the beginning of the reception of an expected ACK response, as detected by the occurrence of PHY-CCA.indication(busy) at the ESTA which is expecting the ACK response during the first slot time following SIFS, it shall retransmit the frame or transmit a QoS Null frame, with Non-Final bit set to 0 and No Ack bit set to 0, after PIFS from the end of last transmission, until such time that it receives an acknowledgement or when there is not enough duration remaining in the TXOP for sending such a frame. This is to avoid the situation where the HC may not receive the frame and may result in an inefficient use of the channel. If the HC does not have any more ESTAs to be polled, it shall send a QoS CF-Poll with the RA matching the HC MACaddress and Duration/ID equal to zero.

Delete the third paragraph of clause 9.10.2.1 as the conditions that cause the behavior described therein will not occur.