## Slide 1: Temporary MAC Addresses for Anonymity
Jon Edney, Henry Haverinen, J-P Honkanen, Pekko Orava

## Slide 2: Introduction
This presentation proposes a method to separate the MAC address of a station from its identity
It means that you can’t find out who a station is by looking at the MAC address.

## Slide 3: Problem
WLAN MAC address is visible in all WLAN packets
=> This enables an observer to trace the movements of users and to collect history and profile data
This is a serious privacy breach especially in public access networks.
  Similar problems have caused bad press for cellular operators.

## Slide 4: Solution Requirements
Minimal changes to IEEE802.11.
  Works as normal after the address selection phase.
Station MAC address only need to be locally unique.
“Local” is defined to be within the ESS and distribution system.
Should also work where DS from multiple ESSs share same wiring plant.
Station MAC address is openly visible once chosen – no special security provisions

## Slide 5: Basic Approach to Solution
Station requests the MAC address from network
Network delivers the address to the station
Network guarantees unique MAC addresses
Initial requests use a random address
MAC address can be different for each new association
“Static” MAC address never used nor revealed

## Slide 6: Basic Concept of the Proposed Approach
AP advertises the feature using a capability bit in beacons and probe responses.
Station must confirm AP has capability before trying to Associate
A random address is used before obtaining a network assigned temporary station MAC address.
Information Elements are added to association request / response frames to indicate address related actions
A temporary station MAC address is selected during initial association procedure from locally administered IEEE MAC addresses.
Access Point delivers unique MAC address to STA
The scheme supports expiry, renewal and reclaim of the addresses.

## Slide 7: Temporary MAC Address Format
Locally administered unicast MAC addresses are used as temporary addresses.
Main part of the temporary address is divided into two parts: temporary address prefix and station specific part.
The address prefix differentiates temporary address types and multiple ESS’s that share one DS or WM.
ESS prefix: Address prefix for temporary station defined in each ESS. To prevent temporary MAC address collisions, the ESS prefix shall be unique for each ESS sharing one DS or WM.

## Slide 8: Definitions
Temporary Probe Address (TPA): Temporary MAC address used for communication with the access point before station has been assigned a Temporary Station Address.
  TPA may only be used by the station for issuing Probe and Assoc Reqs and may only be used by the access point to issue Probe and Assoc Resp.
  All TPAs have temporary address prefix 255.
  Station specific part of the address is randomly chosen by STA.
Temporary Station Address (TSA): Temporary MAC address assigned by the network to a station for a limited period of time.
  Network uses its own ESS prefix as the temporary address prefix for all TSAs it assigns. Station specific part of the address is unique to ESS and is chosen by a method out of the scope of the standard.

## Slide 9: Temporary Address Lifecycle
State 1 - Unallocated: The station has no valid temporary MAC address allocated by the access point. Station uses Temporary Probe Address.
State 2 - Allocated: The station has valid Temporary Station Address allocated by the network.
State 3 - Unallocated: The address allocated for the station has expired. Station uses Temporary Probe Address for attempting to reclaim the previously allocated address.

## Slide 10: Temporary MAC Address IE
One new information element, Temporary MAC Address IE, is defined.
Information elements required are implemented as subtypes to the Temporary MAC Address IE saving IEEE802.11 information element IDs.

## Slide 11
Use passive scanning to learn which networks support the temporary MAC addresses based on Beacons that have the "MAC Anonymity" capability bit set.
Procedure for active scanning when the station does not have valid temporary station address:
  1) Station selects a temporary probe address (TPA).
  2) Station sends Probe Request(s) using the TPA.
  3) Access points send Probe Response frames as a response to received Probe Requests. The "MAC Anonymity" capability bit shall be set if the access point and the network supports temporary MAC addresses.
  4) Station sends Acknowledgement control frames for correctly received Probe Responses using the TPA.
Access points that support temporary MAC addresses shall advertise the feature in Beacon and Probe Response management frames by setting the "MAC Anonymity" capability bit to 1.
Discovery of Temporary Address Support

## Slide 12: Allocation of Temporary MAC Address
Following procedure is used for allocating a new temporary station address:
  STA selects a TPA and a random Request ID.
  STA sends an Assoc Req containing Temporary MAC Address IE of subtype New Address Request to the target AP. The information element indicates that the station is requesting a new temporary MAC address.
  AP allocates a temporary MAC address that is unique within the ESS and DS.
  AP sends an Assoc Resp to the STA using TPA. The response includes the IE of subtype Address Grant containing the new TSA and the Lease period. The Request ID value of the request is copied to the response.
  STA compares the Request ID value of the response with the ID selected at the step 1. If the values match the station continues to the next step. If not, the station has detected a TPA collision and proceeds to step 1.
  STA starts to use new TSA after sending Acknowledgement frame (sent with the TPA) as a response to the Association Response frame.

## Slide 13: Renewal of Temporary MAC Address
The temporary station address remains allocated to a station only for the duration of the lease time.
If the station wants to hold the address for a longer period, following renewal procedure is to be used:
  1) Before the lease period expires, the STA transmits Assoc or Reassoc Req frame that contains Temporary MAC address IE of subtype Renew Request to an AP.
  2) On reception of a renewal request, the AP shall transmit Assoc or Reassoc Resp frame with Temporary MAC address IE of subtype Address Grant in case of successful renewal of an allocated TSA. The information element carries the TSA and the new lease period.
Failure of renewal is indicated in the Association/Reassociation Response frame. Reasons: unallocated or invalid address.
If the AP response does not include correct IE, the STA will disassociate due to AP not supporting the feature.

## Slide 14: Reclaiming of Temporary MAC Address
If the station has been unable to renew the lease for some reason and the lease has expired, the station may use the following procedure for attempting to reclaim the same TSA:
  STA selects a TPA for use during the reclaim process.
  STA sends an Assoc Req carrying IE of subtype Reclaim Request. The information element contains the TSA to be reclaimed.
  AP checks that the requested TSA is unallocated and that the temporary address is valid. Validness check shall at least include the checking of the temporary address prefix against the ESS prefix.
  AP sends Assoc Resp frame with IE of subtype Address Grant containing the TSA and the new lease period.
Failure of renewal is indicated in the Association/Reassociation Response frame. Reasons: allocated or invalid address.
If the AP response does not include correct IE, the STA will disassociate due to AP not supporting the feature.

## Slide 15: Roaming
Station keeps same MAC address when roaming
Station assumes same SSID is on same DS
Station does not send “address” element
Re-association handled as for normal address

## Slide 16: Conclusions
Static MAC addresses impose a serious privacy breach on public access WLAN networks
This proposal presents a way to use temporary MAC addresses to improve privacy
Deliberate "stealing" of MAC addresses is equally easy with static and temporary MAC addresses. The current level of security in "MAC address ownership" is maintained
Support is entirely optional and no implementation changes are needed for systems that do not use temporary MAC address