IEEE P802.11
Wireless LANs

TGe AP Mobility Ad-hoc Teleconference Minutes (Cumulative)

Date:	Feb 27, 2002

Original AP Mobility Author and Chair:	Adrian P Stephens
	Mobilian Corporation
	NW Evergreen Pkwy, Hillsboro, OR 97124
	Phone: +44 771 276 3448 (mobile)
	e-Mail: Adrian.Stephens@mobilian.com

Notes Author:	David Hunter
	Vetronix Corporation
	2030 Alameda Padre Serra, Santa Barbara, California 93103-1716, USA
	Phone: International +1 805 966 2000 x3145 (immobile)
	e-Mail: hunter@timefactor.com

Abstract

This document contains cumulative minutes of meetings of the TGe AP-Mobility Ad-hoc group.

# 6 February 2002

Adrian Stephens, Chair

Opened the meeting at 10:10 AM PST.

Attendees:

Adrian Stephens		(AS)	adrian.stephens@mobilian.com

Rajugopal Gubbi	(RG)	rgubbi@broadcom.com

David Hunter		(DH)	hunter@timefactor.com

John Kowalski		(JK)	kowalskj@sharplabs.com

Mike Moreton		(MM)	mike.moreton@synad.com

Susan Tsao		(ST)	susan@woodsidenet.com

Khaled Turki		(KT)	khaled@ti.com

Chao-Chun Wang	(CW)	ccwang@tvia.com

David Hunter took these notes.

(Note from Chair - Many thanks, David for these excellent notes)

Reviewed proposed agenda

(from 020204 announcement email by Adrian Stephens):

1.  Roll call

2.  Secretary assignment

3.  Review and approval of the proposed agenda

4.  Bring comments on AP-mobility from all sources and create a list of issues

5.  Discuss means to resolve those issues

7.  Agree, if possible, recommended changes

8.  Assign responsibility for updating document

## 6 February Agenda Review

RJ:  Suggest that Adrian give brief rundown of the 02/66r3 document distributed by AS on the TGe website.

## AS presented the highlights of 02/66r3.

Aside:  AS pronounces QAPCS as "capsis".

### Section 1.4

JK:  General ballot comment (which might as well be made against TGf as TGe):  what interactions does this have with TGf?

AS:  In the general case only one device will provide access to your infrastructure.

JK:  But don't want to preclude that might have access provided by more than one AP.  May need to provide AP redundancy that is invisible to the user.  This may cause a race condition with respect to TGf.  That's why this issue could be a ballot comment on TGf's current letter ballot.

AS:  A station may roam to a new AP.

JK:  But, then, is the TGf "context" preserved?

RG:  Context can't be preserved when the AP changes.

AS:  This can amount to an unsubtle hint that the STAs need to reassociate to a better AP.   There is no context to hand over to the new AP, so have to create whole new associations.  TGf copes with that case.

RG:  If a more capable AP comes in, is any association list transferred?

AS:  There's no handover at all from the previous AP.

RG:  Then bullet number 4 under Section 1.4 [which states:  "If the most capable QAPCS becomes inactive, the next most capable QAPCS will take over as the AP."].  Because APs may change anytime.

AS:  But typically the most capable QAPCS is a settop box, which has line power.  If it is disconnected, then the next most (say a camcorder) becomes AP.  Now, if this QAP is involved in a stream, it can set its InhibitAPMobility bit to prevent the current streaming from being disrupted if the most capable QAPCS returns.  This state will be temporary, only as long as the stream is ongoing.

RG:  We really need a complete list of requirements for the "taking over" action (as opposed to the ranking process).  You aren't expecting the Inhibit bit to be present in legacy APs, are you?

AS:  No.  The idea is that the Inhibit bit makes the current AP the highest ranking QAPCS, for a while.

### Section 3

DH:  Suggest avoiding the "Mobile Unit" term.  I can point out two other, distinct, uses of the term "mobile" in this document, and having a third is just confusing.

AS:  Here we're just using a general TGe term.

DH:  Will take the ACTION to create a rewrite of the document that avoids the "Mobile Unit" term.  Will later suggest ways to pull that term out of the TGe draft altogether.

### Section 5.9

AS:  Suggest that we need more text here with respect to JK's inclusion "In order to protect against the possibility of hidden nodes, QAPCS may use one of a plurality of SSIDs, identifying different wireless networks."

JK:  Will take an ACTION to expand that text later -- but it won't happen until next week at the earliest.

AS:  We don't need to create all the solutions right away; the key is just finding the issues now.

AS:  Will take an ACTION to add information with respect to a new Section 4 bullet here.

MM:  Is it worth excluding the hidden node?

AS:  Would like to see all QSTAs to be QAPCS devices.

DH:  Agree with that goal, but am worried about the requirement of a QAPCS device to function as a legacy AP when nothing but legacy STAs are around it.  That would seem to be a heavy burden on many CE devices.

AS:  But the AP is not required to support contention free periods.

MM:  Believe that being an HC is much more complicated than being a PC, anyway, and the QAPCS is required to support that functionality.

AS:  Hopefully the HC capabilities will not be so burdensome that small devices can't support them.

### Section 5.9.1

AS:  The current text doesn't clarify the relative timing of these events.  They could happen in either order.  We need to make sure that TGf is able to cope with both orders.

### Section 7

AS:  The Infrastructure Bandwidth field contains a coarse mapping of connections to infrastructures.

JK:  Bits 4 and 5 should each be ranges [see their Descriptions].  They currently are overlapping.

RG:  Suggest it would be better to put the bandwidth there.

CW:  Wouldn't it be better to have separate upstream and downstream numbers.

AS:  In separate Tx/Rx protocols, you double the numbers [to state overall throughput], while in Ethernet you don't.  The customer will be more interested in the receive rate.  We should include a note that these values apply to the receive field.

(ACTION on AS?)

MM:  Suggest using bits 2-3 as a user defined priority that can fit into the ranking.

AS:  Would like to hold that discussion until we get most of the issues listed.

MM:  The main goal here is to reduce the number of general ranking discussions.

RG:  We'll have those discussions anyway.

AS:  We can expect a lot of variability in the usages of just two user-proscribed bits.

MM:  The idea would be to use the two bits as a user override -- set by the user or, in larger institutions, a network administrator.

AS:  See your point -- could be a way of passing the buck.

JK:  How could this be set by the user -- a management utility?

MM:  I'd suggest that on a PC it would be user level functionality.

JK:  In a PC you would want to mandate such a capability, but not in an HDTV.  In general I agree with the intent, but definitely don't want the average user to have to even think about this.

MM:  Definitely need to have a default value set.

AS:  Can we get rid of the line power field?  [Do need an indicator of] "AP desirability" -- how much you want to be an AP.

JK:  We have the same problem here as with prioritised QoS.  Would be nice to make them tri-state values -- 1, 0 and "don't care". But I believe line power is a very important discriminator.

AS:  Say we have 4 overall values -- don't want, don't care, want, and really want -- to be an AP.

JK:  As long as we have the Inhibit bit, it doesn't matter that much.  But do want to give enough power to the designer to allow specific usage.

KT:  Why is line power so important?  You might want your laptop to be the AP for certain applications – for instance, streaming to a display device.

RG:  But still need a good reason why another AP couldn't do as good a job.

CW:  The user can decide which is the more reliable.

JK:  In fact, could have a line power AP that is even more capable than the others, because it is connected to an UPS.

AS:  So it seems that having just one bit for line power is not sufficient.  I suggest making this a priority field.

JK:  But now we've gotten back into the correct metric rathole again. It might be best to bring this up to the general group via a message on the reflector.

AS:  I'll take the ACTION to send an email (on the issues with ranking and the parameters to be used in the ranking) on the reflector.

===========

RG:  AP Mobility question:  where are the rules for the AP to give controls?  When to set / reset the Inhibit bit.

AS:  The general rule is that the highest ranked devices will set/reset the Inhibit bit dynamically.

RG:  Still need to set the rule exactly so implementations can follow the same procedure.

AS:  At root this needs to be a local decision.

RG:  Can still have a minimum set.  For instance, it shouldn't be conformant behaviour for an AP to go down in the middle of a stream.

AS:  Hopefully this behaviour is not highly dynamic.  It should be a very rare circumstance.  Take the case in which a settop box [has paid, monthly, access on cable], and the user has an emergency backup dialup modem which costs money for access.  [The user doesn't mind paying as an emergency backup, but wants the "free" connection to take over the moment the settop box comes back on line.]  Now a brief glitch in the settop causes the backup to take over.  Since the settop is streaming, it sets its Inhibit bit.  So when the settop comes back, it is shut out [from being the AP].

RG:  I'll take the ACTION to write a normative behaviour section for this [to start discussion on normative rules for setting the Inhibit bit].

===========

Consensus was to end the review of 02/066r3 at this point, and for it to be taken up from this point at the next teleconference (probably next week at the same day and time).

### Section 11.4.1

JK:  I need to mention two questions from Japan-side about QAPCS scanning:

(1) About the requirement that a QAPCS shall periodically scan for APs with higher QAPCS priority:  we should make it clear that if the InhibitAPMobility bit is set, the QAP need *not* do this.

(2) If the QAPCS is scanning other channels, what is the scan rate?  Anyway, does this limit the QoS capabilities [of the system]?

AS:  The 10 percent number was just picked out of the hat.  We need much more justification of useful numbers.

## 6 February End

Meeting adjourned 11:40 AM PST.

# 13 February 2002

Adrian Stephens, Chair

Opened the meeting at 10:00 AM PST.

Attendees:

Attendees:

Adrian Stephens		(AS)	adrian.stephens@mobilian.com

Toshihiro Fujita		(TF)	sukechan@sm.sony.co.jp

Rajugopal Gubbi	(RG)	rgubbi@broadcom.com

David Hunter		(DH)	hunter@timefactor.com

Ho-In Jeon		(HJ)	hoinjeon@netsgo.com

John Kowalski		(JK)	kowalskj@sharplabs.com

Mike Moreton		(MM)	mike.moreton@synad.com

Susan Tsao		(ST)	susan@woodsidenet.com

Khaled Turki		(KT)	khaled@ti.com

Chao-Chun Wang	(CW)	ccwang@tvia.com

** If I missed anyone, please email me at hunter@timefactor.com and I’ll correct this list, David Hunter.

David Hunter took these notes.

Reviewed proposed agenda

(Agenda was re-announced by Adrian Stephens on the stds-802-11@ieee.org reflector 11 February 2002.)

1.  Roll call

2.  Review and approval of the proposed agenda

3.  Bring comments on AP-mobility from all sources and create a list of issues

4.  Discuss means to resolve those issues

5.  Agree, if possible, recommended changes

6.  Assign responsibility for updating document

## Agenda Review

Approved without comment.

AS noted that, because some of the participants in this meeting have to attend other teleconference meetings within an hour, this meeting will be limited to 1 hour.

### Issues about 7.3.2, Parameter Set

In an email to the stds-802-11@ieee.org reflector on 7 February 2002, AS described known issues about the Parameter Sets.  The discussion of this is deferred until we take up rankings, in general.

Current status:  AS has received, so far, three responses to this email.  The main thing they show is that JK and AS disagree in rankings.

JK:  we need to include in that later discussion the email by one of my colleagues about assigning ranks to multiple categories.  This is a different formula [than has been presented so far].

## AS continued presentation of the highlights of 02/66r3.

### Section 7.4.3

JK:  This is a management frame – are all required fields included here?

AS:  Its an action frame, so there is less variety.  But, because for a management frame you have to be a member of a BSS, there is a question whether these are Class 3 or Class 1 frames.

JS:  Imagine you’d also have to be associated and authenticated.

AS:  There’s an ordering problem here.  If a new QAPCS shows up, you need to be able, immediately, to tell it to shut up (if you’re in the middle of a stream, for instance), so it’s still TBD whether it’s possible to interpret these as Class 1 frames.  One comment in the email was that this assertion strictly is not necessary.  It would only slow up in the discovery process if it were deleted altogether.

### Sections 10.3.3.2 and 10.3.10.2

AS:  Once a QAPCS enters a BSS, it cannot change its QAPCS enable capability.

MM:  Think we could remove the JOIN for something that is QAPCS enabled.

AS:  That may not be possible.  For an ad-hoc network a new QAPCS will do a scan followed either by a START or JOIN.

MM:  And if you want to defer, you can find that out (whether you need to defer) from the beacon, so can find it in your scan.

### Section 10.3.11.9

There were no comments in the review.

### Section 11.4

AS:  The first new change is that the QAPCS behaviour can be Enabled or Disabled.

JK:  May be an editorial remark:  This is defining a functionality that, with the exception of the new frame formats, already exists.  A QAP should understand and respond to those frame formats.  Any STA that does respond to these is a QAPCS [whether it would like to defer or not].  Don’t think this is a new option.  Perhaps just make the statement:  “supports the QAPCS behaviour”.

AS:  Of course adding HC capability and scheduling is significant.

JK:  But so is QoS / QSTA capability.  It adds quite a bit to legacy STA capabilities.

AS:  Will strike the word “optimal” and leave it up to the PICS writers to determine.

CW:  Is there a statement in this section about manually shutting down a QAPCS?  For instance, if it misbehaves, or for protection?

AS:  There’s no way to prevent a device from attacking the scanning BSSID and setting itself to the highest QAPCS ranking.  To avoid this we can only specify what all QSTAs do.  STAs that are QAPCSes could build a blacklist of violators.  Personally, I’d not want to have to write that into the standard.  But we should not lose sight of that as an Issue:  consider a Denial of Service attack by a rogue QAPCS pretending to hold the highest priority.  I suspect it won’t be easy to write that [defence].

CW:  Agree; it is a real problem.

### Section 11.4.1

DH:  A QAPCS that is going to go inactive should disassociate all of its STAs before it stops acting as a QAP.

AS:  Agree that this might have a problem.  Take a poll:  is this a problem or redundant?

MM:  Keep it [the “should disassociate”] in.

DH: Think it should be kept in

JK:  This makes for a clean teardown procedure.

CW:  Think it should stay.  Can improve the re-setup time rather than waiting for the next beacon.

RG:  Arguments against this are going to be:  “You still need to have a mechanism for that anyway, so technically becomes redundant.”

CW:  Agree that the new QAPCS can take over anyway.

RG:  There’s no real incentive for anybody to implement this.  But it isn’t a big deal.

CW:  Could make it optional.

HJ:  Having this will accelerate setup time, so I’d like to keep it in.  It would be better if it were mandatory for QAPCS capability.

AS:  Believe that it clearly should stay as a “should”.  Though there are times when a QAPCS can’t do this, it should remain a recommendation.

RG:  It looks like no one is disagreeing.  There will just be arguments about what happens [in specific circumstances].  I agree with “should” rather than “shall”.

AS:  ACTION:  will add this text.

MM:  Is there a reason code why [a disassociation happens]?  An advantage would be that the STAs would know earlier to start looking again.

AS:  Not yet, but that’s a good idea.

RG:  Section 11.4.1.3 is “should”.  Then if the QAPCS did disassociate with a reason code, then it shall not send out beacons and shall not respond to further probe requests.  Also, if it sends out “going down” messages, it shall not send out further beacons.

JK:  Need to add a clause about when the InhibitAPMobility bit shall not be set.

AS:  Will take the ACTION to add that clause.

RG:  Take the case of overlapping with the same BSSID.  Then a QAPCS will shut down if it sees another that is higher ranked.

AS:  Yes; the QAPCS will act in order to assure that there is only one AP.

RG:  In an Infrastructure is there a way that a user can set a “do not change” state?

AS:  The legacy AP will always take precedence.  For backward compatibility we need to defer to the legacy AP.

MM:  Believe we should drop the term “legacy”.

AS:  Will take the ACTION to rewrite as “non-QAPCS AP”

ST:  So it [the “non-QAPCS AP”] will win even if it is of a lower rank?

AS:  Yes.  You’ll still see non-QAPCS APs being installed in offices.  Here we’re really trying to support the home network, in which typically you don’t have a legacy AP.

DH:  Also:  make the “can” in the last sentence of the fourth paragraph [of Section 11.4.1] a “shall”.

AS:  ACTION:  Will do.

JK:  Why not make that mandatory?  “Shall” instead of “should”?

CW:   Will this conflict with the InhibitAPMobility bit?

AS:  The value of that bit already is figured into the rank.  If it is set, then that QAPCS will have the highest rank.

CW:  But what if the InhibitAPMobility bit is set in a new QAPCS, one that has just arrived?

AS:  Think probably that it should be illegal to come in with the bit set.

DH:  How about requiring that a QAPCS shall not set this bit unless it has at least one associated STA?

RG:  How about one TSPEC?

AS:  If you have an active application without a TSPEC, would you ever not want to take that down?

RG:  Is the reverse true?

AS:  Yes;  you won’t have two devices setting this bit unless both have active streams.  ACTION:  “A QAPCS that has no stations associated with it shall not set the InhibitAPMobility bit”.  But this rule has one problem:  this information goes into the layer above the MLME.  So we need to put in a STA management section.  Otherwise, if don’t do that, then may have to leave this requirement here [in Section 11.4.1].

AS:  Will take the ACTION to send out a change-bar version as Revision 4 of this document.

##### Reference Cleanup

CW:  Section 11.4.2.2 is mis-numbered as 11.4.3.2.

AS:  ACTION:  will change that.

#### Next Meeting

HJ:  Making it to a meeting at 3am is a little hard for people in Asia.   Can a somewhat later time be considered?

DH:  How about 3 hours later – so 1:00 PM, Pacific U.S. time?

AS:  If I hear no objections, we’ll change the meeting to that time.

#### 13 February End

Meeting adjourned:  11:04 USPST.

### Update, 14 February 2002

### Adrian Stephens announced on the stds-801-11.ieee.org reflector a new time for the remaining three teleconferences before Dallas (13:00 U.S. Pacific Time; 20, 27 February and 6 March 2002.)

{27 February 2002:  corrected attendance list and made minor format changes for 20 February 2002 meeting – D. Hunter}

# 20th February 2002

Adrian Stephens, Chair

Opened the meeting at 21:10 GMT.

Attendees:

Adrian Stephens		(AS)	adrian.stephens@mobilian.com

Toshihiro Fujita		(TF)	sukechan@sm.sony.co.jp

John Kowalski		(JK)	kowalskj@sharplabs.com

Mike Moreton		(MM)	mike.moreton@synad.com

Susan Tsao		(ST)	susan@woodsidenet.com

Chao-Chun Wang	(CW)	ccwang@tvia.com

** If I missed anyone, please email me at mmoreton@synad.com and I’ll correct this list, Mike Moreton.

Mike Moreton took these notes.

(Adrian:  Many thanks to Mike!)

Reviewed proposed agenda

(Agenda was re-announced by Adrian Stephens on the stds-802-11@ieee.org reflector 20th February 2002.)

1. Roll call

2. Review and approval of the proposed agenda

3. Presentation of 02/066r4 - continued from where we left off last time in revised version with change bars.

4. Check that the list of issues in 02/066r4 is complete.

5. Call for presentations regarding issues.

6. Discuss means to resolve those issues.

7. Agree, if possible, recommended changes

8. Assign responsibility for updating document

## Agenda Review

Approved without comment.

## AS continued presentation of the highlights of 02/66r4.

### Issues about 11.4.2, Behaviour supported by the inactive QAPCS

CW:  What would happen if the inactive QAPCS didn’t want to take over?

AS:  Could stop this happening by setting a different user priority.

CW:  Is there a default value for dot11MissedBeaconThreshold?

AS:  Yes, it’s 11.

CW: Should we use a time rather than number of beacons?

AS:  Problem is that a short time might be less than a beacon.

CW:  But what if beacon interval is long – this could take a while.

AS:  Not really a problem, as changeover should be infrequent.

AS:  Need to discuss what proportion of BSS configuration is carried over when a changeover happens.

CW, MM:  Probably all of it.

AS:  BSS configurations tend to be similar in the real world.

MM:  But the new parameters being added by other QoS groups may change this.

AS:  We should mark this decision as TBD, and put it in the issue list.

AS: There is another issue – what should an inactive QAPCS do if it is disassociated by its active AP?  This could be because the active QAPCS is closing down, or for some other reason such as a security problem or even load.  The latter cases tend to imply that the inactive QAPCS shouldn’t do anything special like trying to become active.  The purpose of this document is to ensure that there is an active AP for the SSID, not necessarily that it will guarantee service.

CW: 	So if an inactive QAPCS fails to authenticate can he still take over?

AS: 	Yes.

CW: 	What can it do in the meantime?

AS: 	Listen to the beacons is about all.

### 11.4.2.1 Active Takeover

TF  What happens if more than one QAPCS sends a takeover request at the same time?

AS:  The active QAPCS should respond with success to both.  Both will then start-up.  The two will then use the normal methodology to determine between the two of them.

ST:  What happens if the second message doesn’t get there until the active QAPCS has gone inactive.

AS:  It’s not defined – I’d suggest success.

ST:  But doesn’t that mean you can have two active QAPCS as a result?

AS:  Yes, but they’ll sort themselves out.

ST:  What if the two new ones both set their inhibit bits?

AS:  I don’t think it should happen – you can’t set the bit until you have a station associated.

CW: 	When a QAPCS becomes inactive he should refuse all assertion actions.  If the sender was better than the QAPCS that has just taken over, it will have to resend the assertion action to the new QAPCS.

AS:  It may be simpler this way round.  Proposed to modify the document this way round.

CW:  Why two beacon intervals for a timeout on the assertion action?

AS:  Had to be some number.

CW:  Shouldn’t the time be the same as for failure of the beaconing QAPCS?

AS:  No, because this is a directed frame with retry, and so should be more reliable.

CW:  Do you have any idea how long it will take an inactive QAPCS to become active?  Is there any requirement?  Maybe it should be within a beacon?

AS:  I don’t think it will normally be that fast as the AP starting up may want to scan alternative channels before starting up (especially if 11h compatible).

### 11.4.2.2 Passive Takeover

AS:  The first problem is that the delay should be related to a time base everyone understands – e.g. the TBTT of the failing QAPCS.  Document updated to reflect this.

AS:  I’m worried about cases like the one where a QAPCS is about to send a beacon, and just before it is due to send it, gets a higher priority beacon.  Is there enough time to change?  We shouldn’t propose anything that requires a hardware change.

#### Next Meeting

AS:  At next meeting plan to complete this document, and then resolve outstanding issues.  Please encourage any interested colleagues to submit any issues.

Date of next meeting :  21:00 GMT (13:00 US Pacific), 27th February 2002.

#### 20 February End

Meeting adjourned:  20:00 GMT.

# 27 February 2002

Adrian Stephens, Chair

Opened the meeting at 1:00 PM PST.

Attendees:

Adrian Stephens		(AS)	adrian.stephens@mobilian.com

David Hunter		(DH)	hunter@timefactor.com

John Kowalski		(JK)	kowalskj@sharplabs.com

Mike Moreton		(MM)	mike.moreton@synad.com

Vijay Petel		(VP)	qvp003@email.sbs.mot.com

Susan Tsao		(ST)	susan@woodsidenet.com

Chao-Chun Wang	(CW)	ccwang@tvia.com

** If I missed anyone, please email me at hunter@timefactor.com and I’ll correct this list, David Hunter.

David Hunter took these notes.

Reviewed proposed agenda

(Agenda was re-announced by Adrian Stephens on the stds-802-11@ieee.org reflector 25 February 2002.)

- Roll call

- Review and approval of the proposed agenda

- Presentation of 02/066r4 – continued from where we left off last time in revised version with change bars

- Check that the list of issues in 02/066r4 is complete.

- Call for presentations regarding issues.

- Discuss means to resolve those issues.

- Agree, if possible, recommended changes.

- Assign responsibility for updating document.

## Agenda Review

Approved without comment.

## AS continued the presentation of the highlights of 02/66r4.

### Section 11.4.3

Editorial asides:

- The first line of 11.4.3 contains a typo:  “A STA” should be “a STA”

- At least U.S. English would put a comma before the clause “depending on the reason for the takeover.”

- There is an extra space between “for” and “the” in that same clause.

AS:   The material in 11.4.3 itself describes old behaviour;  11.4.3.1, on the other hand, is new behaviour.

### Section 11.4.3.1

JK:  Need to add “with the same SSID” to the first sentence of the second paragraph, to make sure the BSSID is not assumed.

AS:  ACTION:  Will add that, plus an explanation why:  “because QAPCS devices will become inactive, and only non-QAPCS APs will continue to operate.”  Will also add the SSID clause to the next sentence.

### Section 11.4.4

DH:  What about the case of an AP (legacy AP) showing up while the active QAPCS is in the middle of a stream (with the InhibitAPMobility bit set)?

AS:  In general we can’t always prevent every user problem.  When the AP arrives we have the potential of splitting the network – and the feeling is that it is better to have a single net than two nets [and the user not knowing who belongs to what].

AS:  About the “The higher score indicates the higher rank.” sentence:  for now we’re trying to avoid the ranking issues.  These will be all brought up together at the end of this discussion.

AS:  About the “treating the MAC address as a 48-bit integer with the I/G bit in the least significant position”:  this ordering is the reverse from the normal MAC address order [to randomize this input to the prioritization].

MM:  Do you have to swap bits within bytes as well?

AS:  Yes you do.  But this becomes the same order as the bits have when they go out over the air in 802.11.

### Annex D

AS:  Remember that all three of the default values given in this Annex were arbitrarily chosen (11 beacons, 10 percent scan rate, and scan interval of 10).  We are still looking for good reasons [pro or con] for any of these values.

About the Editorial comment that currently is in the text:  TGh is specifying scanning, so we expect to receive ballot comments about these scanning numbers from someone who is involved in TGh.

AS:  This finally completes Item 3 of the Agenda for these meetings.

### Agenda Item 4, Review Log of Issues

See Page 4, Section 1.7 of this document (above).

DH:  Suggest that we add two more parameters to the list included in rankings:  (1) whether the QAPCS is attached to another LAN and there is at least one other node on that LAN (whether a wired LAN or another WLAN); and (2) whether the QAPCS is attached to the Internet.

In general, before we bring up ranking algorithms, we first need to list all the parameters that will be involved in the rankings and make sure we agree on them.  After that, we’ll be able to limit the ranking discussion to the relative priorities of the parameters.

JK:   I don’t have a strong feeling about the value of an internet connection.

AS:  We can list the infrastructure and the Internet parameters separately.

MM:  One issue is which parameters of the BSS are maintained when the QAP changes (when an inactive QAPCS becomes active).

AS:  ACTION:  Will add that to the Issue List.

[DH notetaker license:  (1)  The “other LAN connection” and “Internet connection” parameters are good examples of values must NOT be maintained.  (2) State variables to be maintained should be quite independent of the list of parameters that go into the ranking process.  (3)  If non-communal information (i.e., information that is not known by every STA in the BSS) is included in the state variables that must be maintained, then we also have to determine a way to pass this information from the QAPCS that is going inactive to the one that is activating.  And (4), finally, since non-QAPCS APs will not have any of this information, our choices about what state needs to be maintained might be limited to two:  practically none and none. ]

AS:   Called for presentations on any AP Mobility issues.

[None volunteered.]

AS:  So the best procedure seems to be to go through the current list in order.

Issue 1.4

MM:  Believe this should be withdrawn as an issue.  I suggested it originally, but now believe that you shouldn’t expect to be on the same ESS.  Can see that the AP Mobility proposal is aimed at LANs that currently are IBSSes.

AS:  In some respects we still need to look like an IBSS (maintain mobility, etc.)

Issue 5.9

MM:  This question was aimed at problems related to moving in an out of range and causing rapid changeovers.

AS:  In this proposal we’re trying to avoid hidden node issues, as we don’t have any better solution for those than 802.11 in general has.  George (??) suggested that the QAPCS could count all the other stations that it could see and include that fact;  the problem with this is that you could cause a QAPCS takeover just by moving STAs in and out of range.

MM:  Agree that that rule would make matters worse.  How about not allowing changes for a set period after the previous change – say a minute?

AS:  But if the current AP dies, you do want an AP installed as soon as possible.

[DH, more notetaker license:  in general I agree with the conclusion; however, I believe the “current AP dies” case could be accommodated by a second rule that the one-minute (or whatever time) rule is to apply only if AP beacons continue to be received in the current BSS.]

MM:  Should just note that this is a problem and move on for now.

AS:  Will do.  The AP choice will only thrash if we have rapid changeovers.

MM:  The issue came from the old Infrastructure case in which you have two APs that are far apart.  I can see that it is not such a problem in the IBSS case that is being targeted by this proposal.

AS:  True.  This isn’t a new problem with this proposal.

Issue 5.9.1

MM:  If a QAPCS is inactive, then it is not part of a DS

AS:  The real question is what is the state of those parameters

MM:  The key is that we’re  not expecting frequent changeovers, so currently I don’t think that this is an issue.

AS:  ACTION:  Will write a comment in the text to reference the fact that we don’t expect frequent takeovers.

Issue 7.3.2.xxx

AS:  Would like to discuss this later, as it involves rankings

Issue 10.3.3.2

AS:  We have a statistical problem here.  I currently have a request in to Michael Fischer about this issue.  We have discusses mandatory behaviour as if it below MLME.  We’re looking for proposals here.  Pragmatically we can leave it as is and see if the causes anyone problems.

MM:  But if we don’t put extra parameters into JOIN, then nobody will be able to use it.  The parameters here are the primitives that have been added to START.

AS:  Originally we put those into the JOIN because we were trying to make the same changes to START and JOIN.

MM:  If we took out the JOIN bits, then the only problems would be with START.

AS:  But do we need both JOIN and START?  Periodic scanning could be changed, but don’t see a way to change this easily.  Most implementers don’t implement service primitives anyway, so perhaps we shouldn’t worry about this too much.

MM:  This is really just what higher level software should be doing.

AS:  If we get pushback, the architecturally we will have to design a new structure above MLME and will have to create new service primitives (such as “loss of beacons”) to communicate between the two levels.

MM:  I thought that START is not designed to be the mechanism that activates one QAPCS over the others, but as something which just tells them to begin operation.  I propose to treat it as if all QAPCSs are told to start at the same time and later it is decided who wins.

AS:  ACTION:  Then I’ll remove [the new] JOIN parameters and add extra text to reference QAPCS sections for  behaviour.

Issue 11.4.1, Assertion Action

AS:  There is one problem with assertion:  it needs to be a Class 1 frame, because you have to send it to an AP that you are not associated with.  I need to check whether it is possible for such frame to be Class 1, and whether there are any other consequences of this designation.  In general the changeover process could work without assertion, but we’d have much slower handovers.  Right now I’m proposing to leave it as specified.

[No comments.]

Issue 11.4.1, Piggybacking

AS:  We haven’t had any responses from TGh members yet, so we need to leave this issue open for now.

Annex D

AS:  Again, we haven’t received any comments, so will leave it as is.

Issue 11.4.1.2, Scanning by an active QAPCS

AS: This was rejected because that is exactly what we are trying to achieve.

MM:  I wrote this issue, but agree with the rejection, because I see now that this is not in an Infrastructure oriented case.

Issue 11.4.1.3, Seen a Legacy AP

AS:  The legacy AP takes priority.

MM:  This issue also is one I wrote.  The idea is that, if the QAPCS stops being AP immediately, then it stops sending anything out, so it has no way of sending out the information.

AS:  We could just remove this constraint: “if it has seen a legacy AP…”

DH:  What about creating a dissociation reason that a legacy AP has been seen?

AS:  ACTION:  The issue here is not about the case that the QAPCS currently sees an AP, but that it has seen one previously, and, even though that AP currently has gone away, there’s a great probability that it will return.  It’s a matter of wording here.  I’ll change the wording to clearly indicate that this is about the case when the AP was seen earlier, but currently isn’t seen.  But will also add a dissociation reason for the QAPCS becoming inactive due to takeover.

[DH, yet more notetaker license:  this dissociation reason has the side benefit of telling QSTAs to expect to have another AP soon – which can influence their algorithms whether or not to start scrambling around for an IBSS to join.]

Issue 11.4.1.3, Setting InhibitAPMobility

AS:  I believe this issue was RG’s point that we need to have specific rules on setting the InhibitAPMobility bit.  I can add a rule that a QAPCS with active TSPECs should set the InhibitAPMobility bit.

DH:  Believe that this shouldn’t be “shall”; probably not even “should”.

AS:  ACTION:  I’ll will change the wording to indicate that it may be set [at the implementer’s discretion].

Issue 11.4.2

AS:  I’ve accepted this.

Issue 11.4.3.2

AS:  The intent here is to have a deterministic delay, so we did add a clarification here.

MM:  Does a QAPCS that takes over need to synchronize its beacons with the previous AP?  There’s a possible problem:  will this increase the probability of a collision?

AS:  What you’re describing isn’t the intent of this section. The idea is to be talking about the TBIT of the new BSS.   I’ll add a note to that effect to the description.

[Agenda Item 4 is now complete – as far as possible for now.]

Agenda Item 8, Assign responsibility for updating the document

AS:  If anyone wants to perform editorial duties, please volunteer.  I’ll gladly give up some or all of them…

[No response.]

AS:  So I’ll continue in that role myself.

[AS, CW and JK will be out of touch next week.]

MM “volunteered” to lead the next meeting (and final meeting before the 802.11 Interim in St. Louis.)

MM, CW:  We still have the problem that we may not receive the reflector list information, as we are not yet “Nearly Voters”.

DH:  ACTION:  will copy any AP Mobility related information to MM and CW.

Adjourned

13:04 PST.