IEEE P802.11
Wireless LANs

Annex A Motions for 
TGi Letter Ballot 52 Comment Resolutions

Date:	April 23, 2003

Authors:	Dave Halasz
	Cisco Systems

Frank Ciotti
 	Apacheta Corp.

Abstract

Motions drafted to address Letter Ballot 52 Comments on Annex A of 802.11i draft 3.0.

Comment 96, 1201, 1202 – Annex A

In Annex A replace(the current modifications):

Add the following text to this annex, where “X” in Robust Security Network Association Capable is the next number for the protocol capabilities:

| Item | Protocol Capability | References | Status | Support |
| --- | --- | --- | --- | --- |
|  | Are the following MAC protocol capabilities supported? |  |  |  |
| PCX | Robust Security Network Association |  | O | Yes o No o |
| PCX.1 | RSN IE | 7.3.2.17 | PCX:M, FT1:M, FR1:M, FT3:M, FR3:M, FT6:M, FR6:M, FT7:M, FR7:M | Yes o No o |
| PCX.1.1 | Group Key Cipher Suite | 7.3.2.17 | PCX.1:M | Yes o No o |
| PCX.1.2 | Pairwise Key Cipher Suite List | 7.3.2.17 | PCX.1:M | Yes o No o |
| PCX.1.2.1 | CCMP data privacy protocol | 8.3.4 | PCX:M | Yes o No o |
| PCX.1.2.1.1 | CCMP encapsulation procedure | 8.3.4.1.1 | PCX.1.2.1:M | Yes o No o |
| PCX.1.2.1.2 | CCMP decapsulation procedure | 8.3.4.1.2 | PCX.1.2.1:M | Yes o No o |
| PCX.1.2.1.3 | CCMP Security Serv. Mng. |  | M | Yes o No o |
| PCX.1.2.2 | TKIP data privacy protocol | 8.3.2 | O | Yes o No o |
| PCX.1.2.2.1 | TKIP encapsulation procedure | 8.3.2.1.1 | PCX.1.2.2:M | Yes o No o |
| PCX.1.2.2.2 | TKIP decapsulation procedure | 8.3.2.1.2 | PCX.1.2.2:M | Yes o No o |
| PCX.1.2.2.3 | TKIP counter measures | 8.3.2.4.2 | PCX.1.2.2:M | Yes o No o |
| PCX.1.2.2.4 | TKIP Security Serv. Mng. |  | M | Yes o No o |
| PCX.1.3 | Auth. Key Mng. Suite List | 7.3.2.17 | PCX.1:M | Yes o No o |
| PCX.1.3.1 | Unspec. EAP/802.11i Key Mng. | 7.3.2.17 | PCX.1:M | Yes o No o |
| PCX.1.3.2 | Preshard key/802.11i Key Mng. | 7.3.2.17 | PCX.1:M | Yes o No o |
| PCX.1.3.3 | 802.11i Key Mng. | 8.5 | PCX.1:M | Yes o No o |
| PCX.1.3.3.1 | Key Hierarchy | 8.5 | PCX.1:M | Yes o No o |
| PCX.1.3.3.1.1 | Pairwise Key Hierarchy | 8.5.1.2 | PCX.1:M | Yes o No o |
| PCX.1.3.3.1.2 | Group Key Hierarchy | 8.5.1.3 | PCX.1:M | Yes o No o |
| PCX.1.3.3.2 | 4 way handshake | 8.5.3 | PCX.1:M | Yes o No o |
| PCX.1.3.3.3 | Group key handshake | 8.5.4 | PCX.1:M | Yes o No o |
| PCX.1.4 | RSN Capabilities | 7.3.2.17 | PCX.1:M | Yes o No o |

With:

Add the following text to this annex, where “X” in Robust Security Network Association Capable is the next number for the protocol capabilities:

| Item | Protocol Capability | References | Status | Support |
| --- | --- | --- | --- | --- |
|  | Are the following MAC protocol capabilities supported? |  |  |  |
| PCX | Robust Security Network Association |  | O | Yes o No o |
| PCX.1 | RSN IE | 7.3.2.17 | PCX:M | Yes o No o |
| PCX.1.1 | Group Key Cipher Suite | 7.3.2.17 | PCX.1:M | Yes o No o |
| PCX.1.2 | Pairwise Key Cipher Suite List | 7.3.2.17 | PCX.1:M | Yes o No o |
| PCX.1.2.1 | CCMP data privacy protocol | 8.3.3 | PCX:M | Yes o No o |
| PCX.1.2.1.1 | CCMP encapsulation procedure | 8.3.3.3 | PCX.1.2.1:M | Yes o No o |
| PCX.1.2.1.2 | CCMP decapsulation procedure | 8.3.3.4 | PCX.1.2.1:M | Yes o No o |
| PCX.1.2.1.3 | CCMP Security Serv. Mng. | 8.3.3.5 | PCX:M | Yes o No o |
| PCX.1.2.2 | TKIP data privacy protocol | 8.3.2 | PCX:O | Yes o No o |
| PCX.1.2.2.1 | TKIP encapsulation procedure | 8.3.2.1.1 | PCX.1.2.2:M | Yes o No o |
| PCX.1.2.2.2 | TKIP decapsulation procedure | 8.3.2.1.2 | PCX.1.2.2:M | Yes o No o |
| PCX.1.2.2.3 | TKIP counter measures | 8.3.2.4.2 | PCX.1.2.2:M | Yes o No o |
| PCX.1.2.2.4 | TKIP Security Serv. Mng. | 8.3.2.3 | PCX.1.2.2:M | Yes o No o |
| PCX.1.3 | Auth. Key Mng. Suite List | 7.3.2.17 | PCX.1:M | Yes o No o |
| PCX.1.3.1 | Unspec. EAP/802.11i Key Mng. | 7.3.2.17 | PCX.1:M | Yes o No o |
| PCX.1.3.2 | Preshard key/802.11i Key Mng. | 7.3.2.17 | PCX.1:M | Yes o No o |
| PCX.1.3.3 | 802.11i Key Mng. | 8.5 | PCX.1:M | Yes o No o |
| PCX.1.3.3.1 | Key Hierarchy | 8.5 | PCX.1:M | Yes o No o |
| PCX.1.3.3.1.1 | Pairwise Key Hierarchy | 8.5.1.2 | PCX.1:M | Yes o No o |
| PCX.1.3.3.1.2 | Group Key Hierarchy | 8.5.1.3 | PCX.1:M | Yes o No o |
| PCX.1.3.3.2 | 4 way handshake | 8.5.3 | PCX.1:M | Yes o No o |
| PCX.1.3.3.3 | Group key handshake | 8.5.4 | PCX.1:M | Yes o No o |
| PCX.1.4 | RSN Capabilities | 7.3.2.17 | PCX.1:M | Yes o No o |