aIEEE P802.11
Wireless LANs

MIB  Variables

Date:	Sept 16, 2003

Author:	Tim Moore
	Microsoft
	1 Microsoft Way, Redmond, WA, 98052
	Phone: 1-425-703-9861
	Fax: 
	e-Mail: timmoore@microsoft.com

Abstract

Summary

Change

Dot11RSNAConfigEntry ::=

SEQUENCE {

dot11RSNAConfigIndex                   InterfaceIndexOrZero,

dot11RSNAConfigVersion			Integer32,

dot11RSNAConfigPairwiseKeysSupported	Unsigned32,

dot11RSNAConfigMulticastCipher		OCTET STRING,

dot11RSNAConfigGroupRekeyMethod		INTEGER,

dot11RSNAConfigGroupRekeyTime		Unsigned32,

dot11RSNAConfigGroupRekeyPackets        Unsigned32,

dot11RSNAConfigGroupRekeyStrict		TruthValue,

dot11RSNAConfigPSKValue			OCTET STRING,

dot11RSNAConfigPSKPassPhrase		DisplayString,

dot11RSNAConfigTSNEnabled		TruthValue,

dot11RSNAConfigGroupMasterRekeyTime	Unsigned32,

dot11RSNAConfigGroupUpdateTimeOut	Unsigned32,

dot11RSNAConfigGroupUpdateCount		Unsigned32,

dot11RSNAConfigPairwiseUpdateTimeOut	Unsigned32,

dot11RSNAConfigPairwiseUpdateCount	Unsigned32,

dot11RSNAConfigMulticastCipherSize	Unsigned32,

dot11RSNAConfigPMKLifetime              Unsigned32,

dot11RSNAConfigPMKReAuthThreshold       Unsigned32,

dot11RSNAConfigNumberOfReplayCounters	INTEGER,

dot11RSNAConfigSALifetime		Unsigned32,

dot11RSNAAuthenticationSuiteSelected	OCTET STRING,

dot11RSNAUnicastCipherSelected		OCTET STRING,

dot11RSNAMulticastCipherSelected	OCTET STRING,

dot11RSNAPMKIDUsed			OCTET STRING,

dot11RSNAAuthenticationSuiteRequested	OCTET STRING,

dot11RSNAUnicastCipherRequested		OCTET STRING,

dot11RSNAMulticastCipherRequested	OCTET STRING

}

Add following variables

dot11RSNAAuthenticationSuiteSelected OBJECT-TYPE

SYNTAX		OCTET STRING (SIZE(4))

MAX-ACCESS	read-only

STATUS		current

DESCRIPTION

"The selector of the authentication and key management suite negotiated."

::= { dot11RSNAConfigEntry 22 }

dot11RSNAUnicastCipherSelected OBJECT-TYPE

SYNTAX		OCTET STRING (SIZE(4))

MAX-ACCESS	read-only

STATUS		current

DESCRIPTION

"The selector of the Unicast Cipher negotiated."

::= { dot11RSNAConfigEntry 23 }

dot11RSNAMulticastCipherSelected OBJECT-TYPE

SYNTAX		OCTET STRING (SIZE(4))

MAX-ACCESS	read-only

STATUS		current

DESCRIPTION

"The selector of the Multicast cipher negotiated."

::= { dot11RSNAConfigEntry 24 }

dot11RSNAPMKIDUsed OBJECT-TYPE

SYNTAX		OCTET STRING (SIZE(16))

MAX-ACCESS	read-only

STATUS		current

DESCRIPTION

"The selector of the PMKID used in the last 4-way Handshake."

::= { dot11RSNAConfigEntry 25 }

dot11RSNAAuthenticationSuiteRequested OBJECT-TYPE

SYNTAX		OCTET STRING (SIZE(4))

MAX-ACCESS	read-only

STATUS		current

DESCRIPTION

"The selector of the last authentication and key management suite requested."

::= { dot11RSNAConfigEntry 26 }

dot11RSNAUnicastCipherRequested OBJECT-TYPE

SYNTAX		OCTET STRING (SIZE(4))

MAX-ACCESS	read-only

STATUS		current

DESCRIPTION

"The selector of the last unicast cipher requested."

::= { dot11RSNAConfigEntry 27 }

dot11RSNAMulticastCipherRequested OBJECT-TYPE

SYNTAX		OCTET STRING (SIZE(4))

MAX-ACCESS	read-only

STATUS		current

DESCRIPTION

"The selector of the last multicast cipher requested."

::= { dot11RSNAConfigEntry 28 }