IEEE P802.11
Wireless LANs

MIB Tables for Beacon Request and Report

Date:	October 2003

Authors:

Tim Olson
	Cisco Systems
	Phone: 408-853-4527
	e-Mail: tolson@cisco.com

Joe Kwak
	InterDigital Communications
	482 Degas
 	Bolingbrook, IL 60440
	Phone: 630-739-4327
	e-mail: joekwak@mindspring.com

Byoung-Jo “J” Kim
	AT&T Labs-Research
	200 Laurel Ave., A5 1C32, Middletown, NJ 07748
	Phone: 732-420-9028
	Fax: 732-368-9426
	e-Mail: macsbug@research.att.com

Abstract

This document presents MIB tables for entering report requests and retrieving beacon reports via SNMP. Most variables are one-to-one mapping from the fields in the request and report frame formats, except those that require simple translation for human-readibility for time units and binary status bits as commonly practiced with SNMP.

Insert the following in the ASN.1 encoding of the SMT MIB, dot11SMTnotification in Annex D with a proper sequence number where indicated with <<#>>.

dot11RRMReportReady NOTIFICATION-TYPE

OBJECTS { ifIndex, dot11RRMRqstIndex, dot11RRMRqstStatus }

STATUS current

DESCRIPTION

"The dot11RRMReportReady notification shall be sent when the RRM reports corresponding to a RRM request with dot11RRMRqstNotify set to true have been received and ready in a corresponding report table, or its status is determined otherwise. Dot11RRMRqstIndex in this notification corresponds to the index of the request. Dot11RRMRqstStatus of the corresponding request row is included to indicate any error conditions."

::= { dot11SMTnotification 0 <<#>> }

Insert the following in the ASN.1 encoding of the SMT MIB, dot11smt in Annex D with a proper sequence number where indicated with <<#>>.

-- **********************************************************************

-- * Textual conventions from 802 definitions

-- **********************************************************************

TSFtype ::= OCTET STRING (SIZE (8))

-- ********************************************************************

-- * dot11RRMRequest

-- ********************************************************************

dot11RRMRequest OBJECT IDENTIFIER ::= { dot11smt <<#>> }

dot11RRMRequestMaxTableSize OBJECT-TYPE

SYNTAX		Unsigned32(0..65535)

MAX-ACCESS	read-only

STATUS		current

DESCRIPTION

"Identifies the number of measurement requests that can be entered into RRMRequestTable.  Could use a value of zero to indicate that there are no external requests"

::= { dot11RRMRequest 1 }

dot11RRMRequestTable OBJECT-TYPE

SYNTAX SEQUENCE OF dot11RRMRequestEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"Group contains the current list of requests for RRM

report to be issued and have been issued. A network manager

adds a RRM request by updating a row and setting its status to active.

The request becomes ready to be issued when the row status

is set to Active. The rows can not be deleted. Once the SME issues the requested measurement the row status is changed to not active.

::= { dot11RRMRequest 2 }

dot11RRMRequestEntry OBJECT-TYPE

SYNTAX dot11RRMRequestEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"An entry in the dot11RRMRequestTable

Indexed by dot11RRMRqstIndex."

INDEX { dot11RRMRqstIndex }

::= { dot11RRMRequestTable 1 }

Dot11RRMRequestEntry ::=

SEQUENCE {

dot11RRMRqstIndex			Unsigned32,

dot11RRMRqstRowStatus		RowStatus,

dot11RRMRqstToken			OctetString,

dot11RRMRqstIfIndex		InterfaceIndex,

dot11RRMRqstType			INTEGER,

dot11RRMRqstTargetAdd		MacAddress,

dot11RRMRqstTimeStamp		TimeTicks,

dot11RRMRqstChanNumber		INTEGER,

dot11RRMRqstChanBand		INTEGER,

dot11RRMRqstRndInterval		Unsigned32,

dot11RRMRqstDuration		Unsigned32,

dot11RRMRqstParallel		TruthValue,

dot11RRMRqstEnable		TruthValue,

dot11RRMRqstRequest		TruthValue,

dot11RRMRqstReport		TruthValue,

dot11BeaconRqstMode		INTEGER,

dot11RRMRqstBssid			MacAddress,

dot11RRMRqstMeasPeriodUnit	INTEGER,

dot11RRMRqstMeasurementPeriod	INTEGER,

dot11RRMRqstMeasIntervalUnit 	INTEGER,

dot11RRMRqstMeasurementInterval INTEGER,

dot11RRMRqstReportingCondition  INTEGER,

dot11RRMRqstThresholdOffset	INTEGER,

dot11RRMRqstHysteresis 		INTEGER,

dot11MedSenseType			INTEGER,

dot11MedSenseRPIThreshold	INTEGER,

dot11MedSenseBinOffset		INTEGER,

dot11MedSenseBinInterval	INTEGER,

dot11MedSenseNumBin		INTEGER,

dot11STAStatRqstGroupID		INTEGER

}

dot11RRMRqstIndex OBJECT-TYPE

SYNTAX Unsigned32

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"Index for RRM Request elements in dot11RRMRequestTable, greater than 0."

::= { dot11RRMRequestEntry 1 }

dot11RRMRqstRowStatus OBJECT-TYPE

SYNTAX RowStatus

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"The Row Status column of the current row, used for

tracking status of an individual request. When this attribute is set to Active, AND a measurement request can be unambiguously created based on the parameters in the row according to Section << TGk references here>>, then SME may proceed to issue the request to its intended targets. If not, this attribute may be set to Not-ready immediately to indicate parametric errors. However, it is the network managers responsibility to correct the error"

::= { dot11RRMRequestEntry 2 }

dot11RRMRqstToken OBJECT-TYPE

SYNTAX OctetString

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"A unique string to identy a group of rows to be issued as parallel or back to back measurements. To guarantee the uniqueness of this token across multiple network managers, it is recommended that this token be prefixed with the IP address of the network manager creating this row. This token is not necessarily equivalent to the measurement tokens in RRM request frames. If this attribute is null string, then this row of request is independent from other requests."

DEFVAL { “”}

::= { dot11RRMRequestEntry 3 }

dot11RRMRqstIfIndex OBJECT-TYPE

SYNTAX InterfaceIndex

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"The InterfaceIndex for this row of RRM Request to be issued on.

::= { dot11RRMRequestEntry 4 }

dot11RRMRqstType OBJECT-TYPE

SYNTAX INTEGER {3..9}

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"The measurement type of this RRM request row.

3: Channel Load Request

4: Noise Histogram Request

5: Beacon Request

6: Frame Request

7: Hidden Node Request

8: Medium Sensing Time Histogram Request

9: STA statistics Request

The rest of the numbers are reserved.”

::= { dot11RRMRequestEntry 5 }

dot11RRMRqstTargetAdd OBJECT-TYPE

SYNTAX MacAddress

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"The MAC address of STA for this row of RRM Request is to be issued to. If not specified, the default value is broadcast address. If this attribute matches the MAC address of the dot11RRMRqstIfIndex, then measurement request is for this SME itself to be carried out."

DEFVAL {FFFFFFFFFFFF}

::= { dot11RRMRequestEntry 6 }

dot11RRMRqstTimeStamp OBJECT-TYPE

SYNTAX TimeTicks

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"The SysUpTime Value when the dot11RRMRqstRowStatus is set to active."

::= { dot11RRMRequestEntry 7 }

dot11RRMRqstChanNumber OBJECT-TYPE

SYNTAX INTEGER

MAX-ACCESS read-create

STATUS current

DESCRIPTION

" The channel number on which this request instructs the target STA to report detected measurements and probe responses. This attribute is ignored if dot11RRMRqstType = 9: STA statistics Request. However, even in that case, the manager should set this attribute to the current channel for this interface, to be compliant with MIB row creation procedures."

::= { dot11RRMRequestEntry 8 }

dot11RRMRqstChanBand OBJECT-TYPE

SYNTAX INTEGER(0..1)

MAX-ACCESS read-create

STATUS current

DESCRIPTION

" Channel Band indicates the frequency band, taken from Table 0-2, TGk Spec, in which the receiving STA shall conduct its measurement.

0 : 2.4 GHz

1 : 5 GHz

Other values are reserved.

This attribute is ignored if dot11RRMRqstType = 9: STA statistics Request. However, even in that case, this value should set to the current channel band for this interface, to be compliant with MIB row creation procedures."

::= { dot11RRMRequestEntry 9 }

dot11RRMRqstRndInterval OBJECT-TYPE

SYNTAX Unsigned32

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"This value helps set the Randomization Interval in the measurement Request Frame for this RRM Request. dot11RRMRqstRndInterval is expressed in TUs. The default value is 0. This attribute is ignored if dot11RRMRqstType = 9: STA statistics Request."

DEFVAL { 0 }

::= { dot11RRMRequestEntry 10 }

dot11RRMRqstDuration OBJECT-TYPE

SYNTAX Unsigned32

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"This value helps set the Measurement Duration in the measurement Request Frame for this RRM Request, expressed in TUs."

DEFVAL { 0 }

::= { dot11RRMRequestEntry 11 }

dot11RRMRqstParallel OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"This attribute corresponds to the parallel bit of the request frame that contains this row of request. Default is false."

DEFVAL { false }

::= { dot11RRMRequestEntry 12 }

dot11RRMRqstEnable OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"This attribute corresponds to the enable bit of the request frame that contains this row of request. Default is false."

DEFVAL { false }

::= { dot11RRMRequestEntry 13 }

dot11RRMRqstRequest OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"This attribute corresponds to the request bit of the request frame that contains this row of request. Default is false."

DEFVAL { false }

::= { dot11RRMRequestEntry 14 }

dot11RRMRqstReport OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"This attribute corresponds to the report bit of the request frame that contains this row of request. Default is false."

DEFVAL { false }

::= { dot11RRMRequestEntry 15 }

dot11BeaconRqstMode OBJECT-TYPE

SYNTAX INTEGER(0..2)

MAX-ACCESS read-create

STATUS current

DESCRIPTION

" dot11BeaconRqstMode corresponds to the Scan Mode for Beacon Request element. This attribute is only valid if the dot11RRMRqstType  is 5, indicating a beacon report. Otherwise this attribute is ignored.

0 : Passive Mode

1 : Active Mode

2 : Beacon Table Mode:

Other values are reserved as of now

In Passive Scan mode, the measuring STA shall passively receive on the specified channel and return a Beacon Report containing one information element for each STA from which it detects a beacon or probe response. If the measuring channel is also the serving channel, the STA shall concurrently carry out its normal data traffic operation.

In Active Scan mode, the measuring STA shall transmit a probe request with the broadcast SSID. The measuring STA’s Beacon Report shall contain one information element for each STA from which it detects a beacon or probe response, regardless of whether the probe response was triggered by the measuring STA’s own probe request

In Beacon Table mode, the measuring STA shall return a Beacon Report containing the current contents of its beacon table without performing additional measurements

"

DEFVAL { 0 }

::= { dot11RRMRequestEntry 16 }

dot11RRMRqstBssid OBJECT-TYPE

SYNTAX MacAddress

MAX-ACCESS read-create

STATUS current

DESCRIPTION

" BSSID indicates the BSSID of the particular AP for which this measurement is requested.  The BSSID shall be set to the broadcast BSSID when the measurement is to be performed on any AP(s) on this channel."

::= { dot11RRMRequestEntry 17 }

dot11RRMRqstMeasPeriodUnit OBJECT-TYPE

SYNTAX INTEGER (0..3)

MAX-ACCESS read-create

STATUS current

DESCRIPTION

" .  The Measurement Period Unit subfield defines the time unit for the Measurement Period subfield using the following values:

0: TU
1:  msec
2: sec
3: reserved "

::= { dot11RRMRequestEntry 18 }

dot11RRMRqstMeasurementPeriod OBJECT-TYPE

SYNTAX INTEGER (0.. 16383)

MAX-ACCESS read-create

STATUS current

DESCRIPTION

" The Measurement Period indicates whether this measurment is a single measurement event or is a periodic measurment which is scheduled and repeated each Measurment Period.  The Measurement Periods is an unsigned 14 bit integer number representing the repeating time interval for this periodic measurment.  The time unit used for Measurment Period is defined in Measurement Period Unit.  A Measurement Period value of 0 shall indicate that the measurment is not periodic but is a single measurement.  A Measurement Period value of 16383 (3FFF Hex) shall indicate that the measurement is periodic with no requested measurement period; in this case the measurment is performed on a best effort basis and as frequently as conditions will permit.  If scheduling conflicts prevent the STA from executing a periodic measurement at the requested measurement time, the STA may delay the periodic measurement, but shall execute the measurement as soon thereafter as possible.  A delayed periodic measurment shall not change the scheduled measurement time for any subsequent periodic measurements."

::= { dot11RRMRequestEntry 19 }

dot11RRMRqstMeasIntervalUnit OBJECT-TYPE

SYNTAX INTEGER (0..3)

MAX-ACCESS read-create

STATUS current

DESCRIPTION

" .  The Measurement Period Unit subfield defines the time unit for the Measurement Period subfield using the following values:

0: TU
1:  msec
2: sec
3: reserved "

::= { dot11RRMRequestEntry 20 }

dot11RRMRqstMeasurementInterval OBJECT-TYPE

SYNTAX INTEGER (0..16383)

MAX-ACCESS read-create

STATUS current

DESCRIPTION

" The Measurement Interval indicates the time interval during which this periodic measurement shall be implemented. Periodic measurements shall begin at the indicated start time.  Periodic measurements shall continue for the Measurement interval time, then periodic measurments shall end. Measurement Interval uses a 14 bit unsigned integer number representing the repeating time interval for this periodic measurment.  The time unit used for Measurment Interval is defined in Measurement Interval Unit.  A Measurement Interval value of 0 shall terminate any currently active periodic Beacon Request measurement for the indicated BSSID."

::= { dot11RRMRequestEntry 21 }

dot11RRMRqstReportingCondition OBJECT-TYPE

SYNTAX INTEGER (0..255)

MAX-ACCESS read-create

STATUS current

DESCRIPTION

" The Reporting Condition defines when the measured results are to be reported to the requesting STA.  The Reporting Condition values are as follows:

0: Report to be issued  after each measurment

1: Report to be issued when the RCPI level of the measured AP crosses above an absolute threshold with hysteresis

2: Report to be issued when the RCPI level of the measured AP crosses below an absolute threshold with  hysteresis.

3: Report to be issued when the RSSI level of the measured AP crosses above an absolute threshold with hysteresis.

4: Report to be issued when the RSSI level of the measured AP crosses below an absolute threshold with hysteresis.

5: Report to be issued when the RCPI level of the measured AP crosses above a threshold defined by an offset (with hysteresis) from the serving AP’s RCPI.

6: Report to be issued when the RCPI level of the measured AP crosses below a threshold defined by an offset (with hysteresis) from the serving AP’s RCPI.

7: Report to be issued when the RSSI level of the measured AP crosses above a threshold defined by an offset (with hysteresis) from the serving AP’s RSSI.

8: Report to be issued when the RSSI level of the measured AP crosses below a threshold defined by an offset (with hysteresis) from the serving AP’s RSSI.

9: Periodic reports (one per measurement) to begin when the RCPI level of the measured AP enters and remains in a range bound by the serving AP’s RCPI and an offset (with hysteresis) from the serving AP’s RCPI.

10: Periodic reports (one per measurement) to begin when the RSSI level of the measured AP enters and remians in a range bound by the serving AP’s RSSI and an offset (with hysteresis) from the serving AP’s RSSI.

11-255:  reserved"

::= { dot11RRMRequestEntry 22 }

dot11RRMRqstThresholdOffset OBJECT-TYPE

SYNTAX INTEGER (-128..127)

MAX-ACCESS read-create

STATUS current

DESCRIPTION

" Threshold/Offset provides either the threshold value or the offset value to be used for conditional reporting. A threshold value is an unsigned 8 bit integer having units equivalent to RSSI or RCPI. An offset value is a signed 8 bit integer in the range [-128, +127]."

::= { dot11RRMRequestEntry 23 }

dot11RRMRqstHysteresis OBJECT-TYPE

SYNTAX INTEGER (0..255)

MAX-ACCESS read-create

STATUS current

DESCRIPTION

" Hysteresis provides an unsigned 8 bit integer hysteresis value having units equivalent to the units used in the Threshold/Offset field."

::= { dot11RRMRequestEntry 24 }

dot11MedSenseType	OBJECT-TYPE

SYNTAX INTEGER

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"The attribute specifies the medium sense histogram request subtype if dot11RRMRqstType = 8: Medium Sensing Time Histogram Request. This attribute shall be ignored otherwise.

.

0: RCPI Time Histogram

1: CCA Idle Time Histogram

2: CCA Busy Time Histogram

3: CCA NAV Time Histogram

Other valued are reserved

"

DEFVAL { 0 }

::= { dot11RRMRequestEntry 25 }

dot11MedSenseRPIThreshold OBJECT-TYPE

SYNTAX INTEGER

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"This attribute corresponds to the Medium Sense RPI Threshold if dot11RRMRqstType = 8: Medium Sensing Time Histogram Request. This attribute shall be ignored otherwise."

DEFVAL { 0 }

::= { dot11RRMRequestEntry 26 }

dot11MedSenseBinOffset OBJECT-TYPE

SYNTAX INTEGER

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"The attribute corresponds to the Medium Sense Bin Offset if dot11RRMRqstType = 8: Medium Sensing Time Histogram Request. This attribute shall be ignored otherwise."

DEFVAL { 0 }

::= { dot11RRMRequestEntry 27 }

dot11MedSenseBinInterval OBJECT-TYPE

SYNTAX INTEGER

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"The attribute corresponds to the Medium Sense Bin Interval if dot11RRMRqstType = 8: Medium Sensing Time Histogram Request. This attribute shall be ignored otherwise."

DEFVAL { 0 }

::= { dot11RRMRequestEntry 28 }

dot11MedSenseNumBin OBJECT-TYPE

SYNTAX INTEGER

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"The attribute corresponds to the Medium Sense Number of Bins if dot11RRMRqstType = 8: Medium Sensing Time Histogram Request. This attribute shall be ignored otherwise."

DEFVAL { 0 }

::= { dot11RRMRequestEntry 29 }

dot11STAStatRqstGroupID OBJECT-TYPE

SYNTAX INTEGER

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"The attribute corresponds to the group identity if dot11RRMRqstType = 9: STA statistics Request. This attribute shall be ignored otherwise.

0 = STA Counters from dot11CountersTable

The rest are reserved."

DEFVAL { 0 }

::= { dot11RRMRequestEntry 30 }

-- **********************************************************************

-- *    End of dot11RRMRequest

-- **********************************************************************

-- ********************************************************************

-- * dot11BeaconReportTable

-- ********************************************************************

dot11RRMBeaconReportMaxTableSize OBJECT-TYPE

SYNTAX		Unsigned32(0..65535)

MAX-ACCESS	read-only

STATUS		current

DESCRIPTION

"Identifies the number of measurement reports that can be entered into BeaconReportTable."

::= { dot11RRMReport 1 }

dot11BeaconReportTable OBJECT-TYPE

SYNTAX SEQUENCE OF dot11BeaconReportEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"Group contains the current list of Beacon report that have been received by the SME. The report tables shall be maintained as FIFO to preserve freshness, thus this attribute can be overridden by memory constraints or other implementation constraints determined by the vendor of this SME."

::= { dot11smt <<#>> }

dot11BeaconReportEntry OBJECT-TYPE

SYNTAX dot11BeaconReportEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"An entry in the dot11BeaconReportTable

Indexed by dot11BeaconRprtIndex."

INDEX { dot11BeaconRprtIndex }

::= { dot11BeaconReportTable 1 }

Dot11BeaconReportEntry ::=

SEQUENCE {

dot11BeaconRprtIndex			Unsigned32,

dot11BeaconRprtRqstToken 		OCTET STRING,

dot11BeaconRprtIfIndex			InterfaceIndex,

dot11BeaconMeasuringSTAAddr		MacAddress,

dot11BeaconRprtChanNumber		INTEGER,

dot11BeaconRprtChanBand			INTEGER,

dot11BeaconRprtActualStartTime	TSFType,

dot11BeaconRprtMeasurementDuration	Unsigned32,

dot11BeaconRprtPhyType			INTEGER,

dot11BeaconRprtRCPI			INTEGER,

dot11BeaconRprtBSSID			MacAddress,

dot11BeaconRprtParentTSF		TSFType,

dot11BeaconRprtTargetTSF		TSFType,

dot11BeaconRprtBeaconInterval		Unsigned32,

dot11BeaconRprtCFStatus			INTEGER,

dot11BeaconRprtPrivacy			TruthValue,

dot11BeaconRprtBSSMode			INTEGER,

dot11BeaconRprtReceivedElements	OCTET STRING

}

dot11BeaconRprtIndex OBJECT-TYPE

SYNTAX Unsigned32

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"Index for Beacon Request elements in dot11BeaconReportTable, greater than 0."

::= { dot11BeaconRequestEntry 1 }

dot11BeaconRprtRqstToken OBJECT-TYPE

SYNTAX OctetString

MAX-ACCESS read-create

STATUS current

DESCRIPTION

" This attribute holds the request token that was specified in the measurement request that generated this measurement report.  This should be an exact match to the original dot11RRMRqstToken attribute.  Note that there may be multiple entries in the table that match this value since a single request may generate multiple measurement reports."

DEFVAL { “”}

::= { dot11BeaconRequestEntry 2 }

dot11BeaconRprtIfIndex OBJECT-TYPE

SYNTAX InterfaceIndex

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"The InterfaceIndex for this row of Beacon Report has been received on.

::= { dot11BeaconReportEntry 3 }

dot11BeaconMeasuringSTAAddr OBJECT-TYPE

SYNTAX MacAddress

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"The MAC address of the measuring STA for this row of Beacon report."

::= { dot11BeaconReportEntry 4 }

dot11BeaconRprtChanNumber OBJECT-TYPE

SYNTAX INTEGER

MAX-ACCESS read-only

STATUS current

DESCRIPTION

" The channel number on which the this row of report detected beacons and probe responses."

::= { dot11BeaconReportEntry 5 }

dot11BeaconRprtChanBand OBJECT-TYPE

SYNTAX INTEGER(0..1)

MAX-ACCESS read-only

STATUS current

DESCRIPTION

" Channel Band indicates the frequency band, taken from Table 0-2, TGk Spec, in which this row of beacon report has been conducted.

0 : 2.4 GHz

1 : 5 GHz

Other values are reserved."

::= { dot11BeaconReportEntry 6 }

dot11BeaconRprtActualStartTime OBJECT-TYPE

SYNTAX TSFType

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This attribute corresponds to the TSF value at the time when the measurement started."

::= { dot11BeaconReportEntry 7 }

dot11BeaconRprtMeasurementDuration OBJECT-TYPE

SYNTAX Unsigned32

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This attribute corresponds to the duration over which the Beacon Report was measured, expressed in TUs."

::= { dot11BeaconReportEntry 8 }

dot11BeaconRprtPhyType OBJECT-TYPE

SYNTAX INTEGER(1..6)

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This attribute corresponds to the Phy Type for this row of Beacon Report. Phy Type is defined in Table 0-7 in TGk as..

1: FH

2: DSS

3: unused

4: OFDM

5: High Rate DSS

6: ERP

other values are reserved."

::= { dot11BeaconReportEntry 9 }

dot11BeaconRprtRCPI OBJECT-TYPE

SYNTAX INTEGER(0..255)

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This value corresponds to the Received Signal Power in the measurement Report Frame for this row of Beacon Report, expressed in RCPI.”

::= { dot11BeaconReportEntry 10 }

dot11BeaconRprtBSSID OBJECT-TYPE

SYNTAX MacAddress

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This attribute corresponds to the BSSID of the beacon for this row of Beacon report."

::= { dot11BeaconReportEntry 11 }

dot11BeaconRprtParentTSF OBJECT-TYPE

SYNTAX TSFType

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This attribute corresponds to the TSF value of the serving measuring STA’s TSF value at the time the measuring STA received the beacon or probe response frame."

::= { dot11BeaconReportEntry 12 }

dot11BeaconRprtTargetTSF OBJECT-TYPE

SYNTAX TSFType

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This attribute corresponds to the TSF value contained in the beacon or probe response received by the measuring STA."

::= { dot11BeaconReportEntry 13 }

dot11BeaconRprtBeaconInterval OBJECT-TYPE

SYNTAX Unsigned32

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This attribute corresponds to the beacon interval value contained in the beacon or probe response received by the measuring STA."

::= { dot11BeaconRequestEntry 14 }

dot11BeaconRprtCFStatus OBJECT-TYPE

SYNTAX INTEGER(0..2)

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This attribute corresponds to the combination of CF pollable, and CF-Poll Request bits in the capability information contained in this row of Beacon report, as in Table 17, thus indicating the contention-free capabilities of the STA that this row of beacon report corresponds to.

0: No Point Coordinator in the AP

1: Point Coordinator for delivery only

2: Point Coordinator for delivery and polling

Other values are reserved.”

::= { dot11BeaconReportEntry 15 }

dot11BeaconRprtPrivacy OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This attribute corresponds to the Privacy subfield of the capability information contained in the beacon report element corresponding to this row."

::= { dot11BeaconReportEntry 16 }

dot11BeaconRprtBSSMode OBJECT-TYPE

SYNTAX INTEGER(0..2)

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This attribute indicates whether the BSS in the beacon report element corresponding to this row is in the Ad-Hoc mode or not, based on the information available from the beacon report corresponding to this row.

0: Unknown

1: Infrastructure Mode

2: Ad-hoc Mode

Other values are reserved."

::= { dot11BeaconReportEntry 17 }

dot11BeaconRprtReceivedElements OBJECT-TYPE

SYNTAX OCTET STRING (SIZE(0..100))

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This attribute contains a variable number of information elements. All information elements, except Timestamp, Beacon interval and Capability information, that are present in the measured beacon or probe response must be included if the measured BSSID is different from the STA’s current BSS. The Beacon Report will hereby enclose information about the 802.11 enhancements supported by the STA that transmitted the beacon or probe response. All reported TIM elements shall be truncated to 4 octets."

DEFVAL { “”}

::= { dot11BeaconReportEntry 18 }