IEEE P802.11
Wireless LANs

Template for TGn FRCC Comment Submission from STMicroelectronicss

Date:	March 12, 2004

Author:	Massimiliano Siti, Stefano Valle, and George Vlantis

STMicroelectronics

Sites:  Various

e-Mail: {Massimiliano.Siti, Stefano.Valle, George.Vlantis}@st.com

Adrian P Stephens, Chair TGn FRCC
	Intel Corporation
	15 JJ Thompson Ave, Cambridge, UK
	Phone: +44 771 276 3448 (mobile)
	Fax: 
	e-Mail: adrian.p.stephens@intel.com

clanzl@ieee.org

Abstract

This document contains a template for submission of comments to the March 2004 TGn FRCC meeting.

# Instructions

1.  Get an 802.11 document number from www.802wirelessworld.com

2. Update this file's properties and the header block above to reflect your details, not mine!

3. Fill in the table below with your comments.

4. Delete everything from "Abstract" (above) to the start of the "Comments" heading (below).

5. Upload the document to the 802.11 document server and email a copy to:

adrian.p.stephens@intel.com and

clanzl@aware.com

## Meaning of the columns

| Column | Purpose | Your responsibility |
| --- | --- | --- |
| Number | Used by the FRCC to label comments | Leave blank |
| Commenter's Name | Used by the FRCC to identify the author | Provide your name: Surname, Forename |
| Doc Reference | To identify which document you are commenting on | Provide this in the following format: 11-03/0814r16 |
| Section / Item | Itentify document section, or CC# | Fill this in. e.g. CC67.1 |
| Comment | Describe the issue | Describe your issue |
| Proposed Resolution | To contain a proposed resolution | Describe a change that would resolve the issue to your satisfaction |
| E, TN, TY | To understand importance of comment | E - means editorial, TN - means technical, but it would not cause you to vote no on the document if the comment was not resolved, TY - Means that this issue must be resolved before you will vote yes on the document containing the item. |
| Pri, Status, Consensus | Used by FRCC to organise and track progress of the comment | Leave blank |

# Comments

| Number | Commenter's Name | Doc_Reference | Section/Item | Comment | Proposed resolution | E, TN, TY | Pri | Status | Consensuso |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Siti, M.; Valle,S.; Vlantis, G. | 11-02-0814r17 11-02-0815r9 | CC59 | The CC document does not include text modification for CC59 proposed by STM (ref. document: 802.11-04/0210r0) and voted in 24 Feb conference. Straw poll (10/8) is reported in the cumulative minutes doc (802.11-02/815r9). Subject was the adoption of no impairments IM2, IM3, IM4 for simulations in this case. Motivation: as MIMO channel is ideal (AWGN), there is no reason to enable all the impaiments here. It would be no more an ideal scenario. | Add following text to CC59 definition: “Frequency offset compensation unit shall be switched off. Perfect timing acquisition, i.e. timing locked to the first sample of the OFDM symbol, and perfect channel estimation shall be considered. No phase noise modelling is required.” | TY |  |  |  |
|  | Siti, M.; Valle,S.; Vlantis, G. | 11-02-0814r17 | CCxx (new) | Proposal to introduce a new CC, specifically related to the evaluation ofA new CC which evaluates the “maximum achievableabsolute” performance of the proposed transmission/detection algorithms in non-AWGN channel, i.e. with ideal CSI at Rx and IM2-IM3-IM4 switched “off”. Reason: selection procedure between different proposals would be easier; in principle the same scheme designed to achieve high throughput may show a different robustness to the implementation impairments | Have a CC without PHY impairments (except IM1). Proposal for theThe text definition is specified in doc 802.11-04/0210r0. In addition, “no phase modelling is required” should be specified. | TN |  |  |  |
|  | Siti, M.; Valle,S.; Vlantis, G. | 11-02-0814r17 | CC67.2 | Frequency offset is specified in a range from -40ppm to +40ppm. This text is ambiguous and too many simulations can be required in principle, besides it could make it difficult to compare different proposals | Replaced by following: “The two worst case values of exactly -40 ppm and +40ppm for the carrier offset and symbol clock differences at the receiver relative to the transmitter shall be considered for simulations" (or use the -13.7ppm value.) “ | TN |  |  |  |
|  | Siti, M.; Valle,S.; Vlantis, G. | 11-02-0814r17 | All CCs | The CC document does not mention explicitly the antenna separation required for simulations. PHY layer results of different proposals can be not consistent, if the same antenna separation is not used. For the purpose of comparison, one set of antenna characteristics (e.g. uniform linear array, isotropic elements, l/2 spacing, no antenna coupling, vertical polarization) should be specified in the CCs. Different configurations should be allowable under the standard. | Adopt newColin Lanzl proposed a new IM7 to avoid modifying the Channel Model document. See D(doc. 11-04-240r0). for the text of the impairment. | TN |  |  |  |
|  | Siti, M.; Valle,S.; Vlantis, G. | 11-02-0814r17 | CC59 – CC67 – CC67.1 | Text currently specified for PER vs. SNR simulations: “packet length of 1000B” is generic and give rise to confusion. | Replace with: “reference PSDU length of 1000 bytes” similarly to what already specified in 802.11a standard | TN |  |  |  |
|  | Siti, M.; Valle,S.; Vlantis, G. | 11-02-0814r17 | CC67.2 | Reference PSDU size not specified. | Add: “PER vs. SNR simulations shall be carried out at reference PSDU length of 1000 bytes” | TY |  |  |  |
|  | Siti, M.; Valle,S.; Vlantis, G. | 11-02-0814r17 | CC67.2 | NLOS/LOS channel condition is not specified | Specify NLOS conditions, as in CC67 and CC67.1 | TN |  |  |  |
|  | Siti, M.; Valle,S.; Vlantis, G. | 11-02-0814r17 | IM5 | The impact of IM5 Noise Figure on the simulation scenarios required for CC59 – CC67 – CC67.1 – CC67.2 is not clear. PER vs. SNR can be simulated setting the desired SNR at the receiver side, providing the required noise variance. NF is not used in this case. It should be used in case a Rx sensitivity table is to be provided, but this is not mentioned in CC document. | Delete IM5 from CC document or better specify why it is needed | TY |  |  |  |

.