WPP Roadmap, Terminology and Issues

Date:                                                     June 30, 2004

Author:	Tom Alexander, VeriWave

Abstract

This document is intended to serve as a living list of discussion items, terminology and issues for the Wireless Performance Prediction (WPP) SG, as well as an outline of work areas and work to be done. It is expected to capture issues and discussion topics as the work progresses, and will be revised constantly. The document comprises three sections: a roadmap; a list of terms and definitions; and a list of issues.

# Outline and Roadmap

The discussion topics for WPP can be generally grouped into three categories: component, application and environment. This is depicted in the following figure. For editing convenience, the same information is provided in tabular form after the figure.

| Wireless Performance |
| --- |
| Performance Category | Description and Examples |
| Component | Performance measurements made on individual components of a WLAN Examples: Antennae, MACs, PHYs, Radios, Hardware Platform, etc |
| Application | Performance measurements pertinent to specific applications Examples: Multimedia performance: streaming media, VoIP Data performance: network performance, QoS |
| Environment | Miscellaneous performance aspects that are environment-dependent Examples: Online vs. offline performance measurements? Performance measured with encryption processing? Measurements in controlled or uncontrolled environments? Effects of channels: multipath, capacity Effects of interference: adjacent channel Variations with receive signal strength |

Wireless performance can also be defined, from the viewpoint of the various user communities, in terms of the following matrix:

| User Community | Throughput | Latency | Link Reliability | Signal Strength | Channel Volume | AP Position | Packet Loss | Trans. Time |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Back End (designers / optimizers) |
| Antennae | Yes | Yes | Yes | Yes | Yes | Yes | Yes |  |
| Radio | Yes | Yes | Yes | Yes | Yes |  |  |  |
| Hardware Integrators | Yes | Yes | Yes |  |  |  |  |  |
| Front End (users) |
| Hot Spot Providers | Yes |  | Yes |  |  | Yes |  |  |
| IT Managers | Yes |  |  |  |  | Yes |  |  |
| Product Reviewers | Yes |  |  |  |  |  |  |  |
| Performance Enthusiasts | Yes |  |  |  |  |  |  |  |

This outline should be discussed and updated as the group continues to do work.

## Scope

The “Scope” portion of the PAR is reproduced here for convenience during group discussions.

“The scope of the project is to provide a set of performance metrics, measurement methodologies, and test conditions to enable measuring and predicting the performance of 802.11 WLAN devices and networks at the component and application level.”

Additional explanatory text:

“The project will assume as a baseline the existence of 802.11-1999 Reaff 2003, with Amendments e, g, h, i, j and k.  The project may  also take as input the work of 802.11 Task Groups n, r and s.

The project will coordinate with 802.19 on any potential areas of synergy, such as some of the performance metrics.

For the purposes of this project the definition of prediction is as follows: the use of multiple input parameters to estimate performance characteristics useful for 802.11 network planning.  Input parameters are defined to be 802.11 device characteristics, network layout and usage parameters.”

## Purpose

The “Purpose” portion of the PAR is reproduced here for convenience during group discussions.

“The purpose of the project is to enable testing, comparison, and deployment planning of 802.11 WLAN devices based on a common and accepted set of performance metrics, measurement methodologies and test conditions.”

Additional explanatory text:

“The target audience for the Recommended Practice includes developers of chipsets, components, equipment and software that uses or must interact with 802.11 wireless equipment, as well as users of 802.11 equipment, including system installers, IT managers and test laboratories.”

# Terminology

The following table gives the definitions of terms of interest to WPP. These definitions or interpretations take precedence over the standard dictionary definitions of the terms.

| Term | Interpretation or Definition |
| --- | --- |
| Component | Anything that forms a physical part of an 802.11 network. A whole is considered to be an entire 802.11 network, and a component is a part thereof. |
| Application | The definition of applications for the purposes of WPP should be limited to the Layer 2 802.11 performance metrics required to support higher-layer applications. It does not include measuring performance of actual applications themselves. |
| Subcomponent | A subcomponent has no application to the network by itself, and has no standing by itself. |

# Issues List

The following issues need to be discussed and resolved by the group:

- Should “subcomponents” be limited to pieces that a user can replace?

# Text boxes

- Online/offline?

- Encryption processing?

- Controlled/uncontrolled?

- Channel

- Multi path

- Capacity

- Interference

- Adjacent Channel

- Receive signal strength (path loss)

Environment

- Antennae

- MAC

- Phi

- Radio

- Hardware platform

- Power?

Application

Component

Wireless Performance

(component, system, environment)

- Multimedia performance

- Streaming media

- Voice over IP

- Data Performance

- Network performance

- Quality of service?