IEEE P802.11
Wireless LANs

802.11 TGr Minimum Requirements

Date:	August 2, 2004

Author:	Jim Wendt
	Hewlett-Packard Company
	8000 Foothills Blvd.  M/S 5555
	Roseville, CA  95747-5555
	Phone: +1-916-785-5198
	e-Mail: jim.wendt@hp.com

Abstract

This document specifies the minimum requirements for the Fast-BSS-Transition mechanism to be defined by 802.11 TGr.

Table of Contents

1.1	Contributors	1

1.2	Revision History	1

1.3	Working Notes and Issues	2

1.4	Overview	2

1.5	Definitions and Assumptions	2

1.5.1	BSS-Transition	2

1.5.2	Fast-BSS-Transition Environment	2

1.5.3	Fast-BSS-Transition Definition	3

1.5.4	Fast-BSS-Transition-Time	3

1.6	General Requirements	4

1.7	Environment Requirements	4

1.7.1	Topology Scenarios	4

1.7.2	PHY/MAC Scenarios	4

1.7.3	RF Scenarios	5

1.7.4	Security Scenarios	5

1.8	Performance Requirements	5

1.8.1	Fast-BSS-Transition-Time Goals	5

1.9	Processing Requirements	5

1.9.1	Power Save	5

1.10	System Requirements	5

1.10.1	Compatibility	5

1.11	Documents List	5

## Contributors

| Name | Company | Address | Phone | Fax | Email |
| --- | --- | --- | --- | --- | --- |

## Revision History

| Revision | Comments | Date |
| --- | --- | --- |
| R0 | Initial requirements framework for group discussion purposes | 15 July 2004 |
| R1 | Incorporated changes made during Portland TGr meetings on 7/15/04. Doc is being posted with redline markups. A subsequent cleaned-up version will be posted shortly. | 15 July 2004 |
| R2 | Rolled in redline changes from R1. Updated diagrams. Filled in reference docs list and supporting clauses list. | 2 August 2004 |

## Working Notes and Issues

Working Notes and Issues:

- Need to add in security requirements from 802.11r Security Requirements ad-hoc group, when finalized.

## Overview

This document specifies the minimum requirements for the Fast-BSS-Transition mechanism which must be met by any proposed solution.

Note that proposed solutions are not precluded from going beyond these minimum requirements.

## Definitions and Assumptions

### BSS-Transition

A BSS-transition is currently defined as follows:

- (clause 5.4.2.1b) “BSS-transition: This type is defined as a station movement from one BSS in one ESS to another BSS within the same ESS.”

- (section 3.7) “basic service set (BSS): A set of stations controlled by a single coordination function.”

- (section 3.25) “extended service set (ESS): A set of one or more interconnected basic service sets (BSSs) and intergrated local are networks (LANs) that appear as a single BSS to the logical link control (LLC) layer at any station associated with one of those BSSs.”

This BSS-transition definition implies the following:

- The AP for each BSS must be in the same ESS

  - From clause 5.4.2.1b (shown above)

- The AP for each BSS in the ESS must have the same SSID

  - From Section 7.3.2.1 SSID element -- “The SSID element indicates the identity of an ESS or IBSS.”

- The AP for each BSS in the ESS must be connected to the same DS

  - From section 5.2.2 Distribution System (DS) Concepts -- “Instead of existing independently, a BSS may also form a component of an extended form of network that is built with multiple BSSs. The architectural component used to interconnect BSSs is the DS.”

- BSS-transitions are transparent to LLC

  - From section 5.2.2.1 Extended Service Set (ESS): The large coverage network -- “Stations within an ESS may communicate and mobile stations may move around from one BSS to another BSS (within the same ESS) transparently to LLC”

- The DS is notified when the STA completes the BSS-transition

  - From section 3.20: distribution system (DS): a system used to interconnect a set of basic service sets (BSSs) and integrated local area networks (LANs) to create an extended service set (ESS)

  - From section 5.4.2.3 Reassociation – “The reassociation service is invoked to “move” a current association from one AP to another. This keeps the DS informed of the current mapping between AP and STA as the station moves from BSS to BSS within an ESS.”

### Fast-BSS-Transition Environment

The Fast-BSS-Transition environment is shown in the figure below:

### Fast-BSS-Transition Definition

FBT.1 - A Fast-BSS-Transition is defined as a BSS-Transition that meets the Fast-BSS-Transition-Time goals as stated in this document.

### Fast-BSS-Transition-Time

The Fast-BSS-Transition-Time period is shown in the figure below:

FBT.2 - The Fast-BSS-Transition-Time is defined as follows:

- Security not enabled:

  - the period between the last possible point in time (tA) where STA-TE communication can pass through the Old-AP, to the first possible point in time (tB) where STA-TE communication can pass through the New-AP

- Security enabled:

  - the period between the last possible point in time (tA) where STA-TE communication can pass through the Old-AP, to the point in time (tB) where the first MSDU can pass through the controlled port

## General Requirements

GEN.1 – The Fast-BSS-Transition mechanism must meet the conditions stated in the TGr PAR.

## Environment Requirements

### Topology Scenarios

TOPO.1 - Fast-BSS-Transitions are only supported for a STA that supports the Fast-BSS-Transition capability.

TOPO.2 - Fast-BSS-Transitions at a minimum must be supported between two APs which both support the Fast-BSS-Transition capability.

### PHY/MAC Scenarios

PHYMAC.1 - A Fast-BSS-Transition shall be possible between two APs that support any of the following standards: 802.11a, 802.11b, 802.11g. Consideration would also be given to future MAC/PHY implementations

PHYMAC.2 - A Fast-BSS-Transition shall be possible between two APs that are using different channels

PHYMAC.3 - A Fast-BSS-Transition shall be possible between two APs that are using the same channel

PHYMAC.4 – A Fast-BSS-Transition should be possible between different 802.11 bands (a/b/g) as those bands are supported by the STA.

### RF Scenarios

RF.1 – Fast-BSS-Transition shall be supported across overlapping BSSes

RF.2 – Fast-BSS-Transition may be supported across tangential BSSes

### Security Scenarios

SEC.1 – xxx <security requirements to be provided by 802.11r Security Requirements ad-hoc group>

## Performance Requirements

### Fast-BSS-Transition-Time Goals

Proposals must submit transition time information as part of the proposal which follows a Fast-BSS-Transition-Time measurement methodology and reporting methodology that is to-be-determined.

## Processing Requirements

### Power Save

POW.1 – The Fast-BSS-Transition-Time goal is not required to be met when a STA has gone into power-save mode.

## System Requirements

### Compatibility

COMP.1 - Fast-BSS-Transition capable APs shall be able to concurrently support associations with both legacy STAs and Fast-BSS-Transition capable STAs.

COMP.2 - Fast-BSS-Transition capable STAs shall be able to support associations with both legacy APs and Fast-BSS-Transition capable APs.

## Documents List

11-03-813-12-000n / Functional Requirements

11-04-0086-03-frfh / Measurement of the 802.11 Roaming Intervals

11-04-0503-00-frfh / 802.11 Roaming

11-04-0516-00-frfh / Requirements Discussion

11-04-0614-01-frfh / What is an ESS

11-04-0619-01-frfh / RequirementsDocument

11-04-0629-01-frfh / The Nature of an ESS

11-04-0661-04-000r / TGr Document List

11-04-0666-01-000r / TGr Requirements Strawman

11-04-0677-01-000r  / Fast BSS Transition Use cases

11-04-0678-01-000r / TGr Scope

11-04-0785-01-000s / Interpretations DSS Based on the 802.11 Spec

21-04-0100-02-0000 / Cross Domain Trigger and Handover Talking Points

###