IEEE P802.11
Wireless LANs

Partial Proposal for 802.11n: ITRI Preamble Specification

Date:	August 13, 2004

Authors:	Yung-Yih Jian, Pangan Ting, Wei-Ping Chuang,
	Chun-Chun Kuo, Chang-Lung Hsiao
	Industrial Technology Research Institute (ITRI)
	Computer and Communication Research Laboratories (CCL)
	Bldg.14, 195 Sec. 4, Chung Hsing Rd. Chutung, Hsinchu, Taiwan 310, R.O.C.
	Phone: +886-3-5914752
	Fax: +886-3-5820371
	e-Mail: {yyjian, pating, joeChuang, godeman, clhsiao}@itri.org.tw

Wei-De Wu
	National Tsing Hua University
	Institute of Communications Engineering
	welder@micro.ee.nthu.edu.tw

Chih-Kai Chen
	Stanford University
	Department of Electrical Engineering
	chihkai@stanford.edu

Abstract

In this report, we propose a novel preamble structure for IEEE 802.11n standard. The proposed preamble structure is compliant with the FRCC documents and has good properties for frame detection and channel estimation.

### Short Training Symbols

The new STSs for IEEE 802.11n should following three properties:

- Periodicity with period 32.

- Zero cross-correlation among different STSs.

- Low detection probability for IEEE 802.11a receivers.

### Long Training Symbols

The proposed training block is shown in Figure 9, where , cyclic prefix (CP) is of 16 samples, and L is the basis of the proposed LTS for IEEE 802.11n, which is the same with the LTS of IEEE 802.11a [2]. With the structure of the proposed LTS for IEEE 802.11n, the receiver can estimate channel responses with low complexity. Specifically, an efficient 4 x 4 FFT matrix can be used.