IEEE P802.11
Wireless LANs

| Resource Request/Response Description |
| --- |
| Date: 2005-09-19 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Michael Montemurro | Chantry Networks | 1900 Minnesota Cr, Suite 125. Mississauga, ON. L5N 3C9 | 905-363-6413 | michael.montemurro@siemens.com |

Insert the following clauses after 8A.4.2

### 8A.4.3 Reservation over the DS

Reservation over the DS allows the TSTA to communicate with a target TAP through its existing association (with the current TAP). The TSTA transmits an Action frame containing the resource reservation and the BSSID of the target TAP to the current TAP. The current TAP relays the Resource Request to the target TAP over the DS. The target TAP processes the resource reservation and responds to the TSTA by sending the resource reservation response through the current TAP.

The resource reservation mechanism introduces a component called the Resource Request Broker (RRB). The function of the RRB is to generate Resource Reservation frames and relay messages between the CAP and the TAP. The RRB could be configured to block a Resouce Request or limit the number of pending Resource Requests from a TSTA.

The transport mechanism for the resource reservation request and response over the DS are out of scope of this standard.

### 8A.4.3.1 Resource Request Broker (RRB)

The Resource Request Broker resides in the SME on the Access Point and the STA and acts a termination point for Resource Requests over the DS.

The ResourceRequest Broker configuration is given in Table 1 along with default configuration.

Table 1 ResourceRequest Broker configuration

| Configuration Item | Value |
| --- | --- |
| dot11ResourceRequestTimeout | ? |
| dot11PendingResourceRequestLimit | ? |

The Resource Request Broker resides on the AP has two functions depending on its mode of operation:

- Respond to Resource Requests targeted to itself;

- Forward Resource Requests to the TAP across the DS;

If the Resource Request Broker at the AP receives a resource request, it will interact with the MAC SME to process resource requests and respond to the requesting STA.

If the Resource Request Broker at the AP receives a resource request directed to another AP and the AP supports “over the DS” communications, the AP will forward the Resource Request to the target AP. The AP will track the Resource Request until it receives a Resource Response. The AP will maintain a timer while it waits for the Resource Response. If no response is received in the dot11ResourceRequestTimeout period, the AP will respond with a Resource Response to the STA indicating that the resource request has timed out.

The communications between the target TAP and the current TAP should be protected. The target TAP and the current TAP must reside in the same mobility domain to successfully exchange Resource Reservation frames. The RRB on the CAP must be able to transmit Resource Reservation frames to the target TAP based on the BSSID supplied in the FT Action frames.

The message flow for a resource request over the DS is given in Figure 2. The STA indicates the destination target TAP BSSID as part of the FT Action frame. The RRB on the current TAP encapsulates the action frame and supplies the TSTA MAC address in the Resource Reservation frame.

Figure 2 Simple message flow for over the DS resource request

### 8A.4.3.2 Resource Request/Response Frame Definition

The Resource Request frame is transmitted over the DS from the current TAP to the target TAP. The ResourceRequest could be transmitted between Resource Request Broker’s on different AP in the same broadcast domain. For more complicated network infrastructures, the Resource Request/Response frames could use an IP mechanism to transmit ResourceRequest and ResourceResponse frames.

The frame format for the Resource Request/Response is given in Figure 4. Resource Request/Response frames will use an Ethertype of ??-??. The Resource Request/Response frame contains version, type, and length fields. The destination MAC shall be set to the BSSID of the target TAP for a Resource Request, and to the TSTA MAC for a Resource Response frame.

| Size | Field | Description |
| --- | --- | --- |
| 1 | Protocol Version | Must be 0x01 |
| 1 | Packet Type | 0x00 – for Resource Request 0x01 – for Resource Response |
| 2 | FT Action Length | Unsigned number representing the length in octets of the FT Action Frame field. |
| 6 | Destination MAC | The destination MAC for the request or the response frame. |
| Length | FT Action Frame | The contents of the FT Action frame |

Figure 4 Resource Reservation Request/Response Frame

Move Section 8A.6 to a subsection of 8A.4.3

8A.4.3.3 Broker Function

A broker function in the TAP is defined to facilitate policy enforcement and reservation request response co-ordination. This is shown in Figure 121L. The Broker Function is only invoked at the Current TAP when an over-the-DS reservation request is to be performed. Following are the tasks performed by a Broker function:

- At the minimum, the BF shall re-format the reservation request from the SME for consumption by the RRB. Similarly, it shall be able to re-format the response from the RRB to send it to the SME.

- A BF may choose to apply any policy dependent processing on the reservation request before forwarding it to the RRB. A BF may, similarly choose to apply any policy dependent processing on the resource response before forwarding it to the SME.

Remove Figure 121L

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.