IEEE P802.11
Wireless LANs

| TG 11k Conference Call Minutes Mar-May |
| --- |
| Date: 2005-07-28 |
| Author(s): Paul Gray |
| Name | Company | Address | Phone | email |
| Paul Gray | AirWave | 1700 S. El Camino Real | 650-678-5633 | paul@airwave.com |

# 07/28 Minutes 08:30

Attendance – Paine, Gray, Wang, Kwak

Blank Comment Resolution

Comment #8 – Clause 11.7.5 – Emeott

Problem - The sentence in the clause about refusing measurements is incomplete

Remedy - Change the sentence to read "However, the execution of each request in the Radio Measurement category is optional and may be refused by the receiving STA by sending a measurement report with the refused bit set in the Measurement Report Mode field if its execution would significantly degrade the station's performance."

Comment – this has been updated by Simon, but our spreadsheet is out of date.

Resolution – accept – Simon has not address

Comment #9 – Clause 11.7.6 – Emeott

Problem - It is not clear what the entry in Table k14 reading "none" means

Remedy - Replace the word none with "Not Allowed" or "Invalid"

Comment – TGe allows a direct connection and so we have specif measurement.

Comment – TGe is not ratified

Resolution – accept

Comment #10 – Clause 11.7.6 – Emeott

Problem - The first sentence of the fifth paragraph would read better if the words "by default" were added after the text "The Measurement Request elements are processed in sequence".

Remedy - Change the text

Resolution – accept – P51L22 change “sequence,” to “sequence by default,”

This is an Editoral Comment

Comment #11 - Clause 11.7.6 – Emeott

Problem - The information about autonomous measurements would be much easier to find if it were put in a separate clause

Remedy - Move the two paragraphs near the end of clause 11.7.6 on autonomous reporting of measurements into their own section, following clause 11.7.6, and call it "Autonomous Measurement Report frames"

Resolution – deferred – 05/0512r2 deletes these paragraphs

Comment #21 – Clause 11.7.8.1 – Emeott

Problem - The Beacon Report contains a one octet RCPI field.  The PICS do not contain an entry indicating whether RCPI Measurement during Passive Scanning is mandatory or optional.  If the RCPI Measurement during Passive Scanning is optional, the normative text should indicate what a STA should put in the RCPI field of the Beacon Report if it does not support RCPI measurement during Passive Scanning, or should indicate that the STA may refuse the measurement.

Remedy - Insert a row into the PICS with the heading RCPI Measurement during Passive Scanning and a row indicating that Measurement of RCPI on Beacon frames is mandatory, or put text into clause 11.7.8.1 explaining what a STA should put into the RCPI field when it is unable to measure the RCPI of received beacon frames.

Comment – this should have been in the PICs document – no

Resolution – declined – RCPI definition uses 255 to indicate measurement not available.  No PICs modification is required.

Comment #32 – Clause 11.8.2 - Lin

Problem - It says only associated STA can request a neighbor report. If security is not a concern, it should allow any STA to request neightorhood report in order to speed up roaming.

Remedy - If security is not a concern, any STA should be able to request a neighborhood report. If security IS a concern, then it should say only authenticated STA ( if RSN is enabled, it needs to be 802.11i authenticated) can request a neighborhood report.

Resolution – decline – P3:L37 TGk decided all measurement frames are class 3 frames.

Comment #36 – 7.3.2.21.6 - Lin

Problem - There should be a command to ask for measurement of "ALL REGULATORYCLASS" so multiband STA can scan all channels in one request

Remedy - Change table K1 to use 255 to indicate ALL supported regulatory class. When regulatory class field is 1, channel number should be either 0 or 255

Comment – this is not necessary, because you request twice and you are usually on one PHY

Resolution – decline – can only scan what is currently regulatory class.  Actively scanning channels is not legal in any regulatory domain.

Conference call ends 9:30.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document contains minutes for TGk conference calls between July and September 2005.

.