IEEE P802.11
Wireless LANs

| Dynamic Multi level Power Control |
| --- |
| Date: 2006-Feb-17 |
| Author(s): |
| Name | Company | Phone | email |
| Roger Durand | Research In Motion |  |  |
| Floyd Backes | AutoCell Labs | 1.978.264.4884 x225 | fbackes@autocell.com |
| Joe Epstein | Meru Networks | 1.408.215.5343 | jepstein@meru.com |
| Mike Montemurro | Chantry Networks | 1.905.363.6413 | michael.montemurro@siemens.com |
| Larry Stefani | AutoCell Labs | 1.978.264.4884 | lstefani@autocell.com |

Abstract

This document contains a normative text proposal in support of a mechanism for dynamic multi level transmitter power control in accordance with REQ2040 and REQ2041. This document is based largely on P802.11v-D0.1, P802.11k-D3.2, and P802.11-REVma-D5.1.

7. Frame formats

7.1 MAC frame formats

- Power Constraint element

Change the text of subclause 7.3.2.15 as follows:

The Power Constraint element contains the information necessary to allow a STA to determine the local maximum transmit power in the current channel. The format of the Power Constraint element is shown in Figure 70.

The Length field shall beis set to 1the number of octets in the following fields.

|  | Element ID | Length | Local Power Constraint | Station Aware Power Constraint (optional) |
| --- | --- | --- | --- | --- |
| Octets: | 1 | 1 | 1 | 1 |

Figure 70—Power Constraint element format

The Local Power Constraint field shall beis set to a value that allows the mitigation requirements to be satisfied in the current channel. The field is coded as an unsigned integer in units of decibels. The local maximum transmit power for a channel is thus defined as the maximum transmit power level specified for the channel in the Country element minus the local power constraint specified for the channel (from the MIB) in the Power Constraint element. If the Station Aware Power Constraint field is present, the Local Power Constraint is used for management frames. If the Station Aware Power Constraint field is not present, the Local Power Constraint is used for all frames.

The Station Aware Power Constraint field, if present, is set to a value that enhances frequency re-use in adjacent or near adjacent same channel cells. The field is coded as an unsigned integer in units of decibels. The local maximum transmit power for control and data frames for a channel is thus defined as the maximum transmit power level specified for the channel in the Country element minus the station aware power constraint specified for the channel (from the MIB) in the Power Constraint element.

The Power Constraint element is included in Beacon frames, as described in 7.2.3.1, and Probe Response frames, as described in 7.2.3.9. The use of Power Constraint elements is described in 11.9.2.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.