IEEE P802.11
Wireless LANs

| Dynamic Multi level Power Control |
| --- |
| Date: 2006-Mar-8 |
| Author(s): |
| Name | Company | Phone | email |
| Floyd Backes | AutoCell Labs | 1.978.264.4884 x225 | fbackes@autocell.com |

Abstract

This document contains work in progress on a normative text proposal in support of a mechanism for dynamic multi level transmitter power control in accordance with REQ2040 and REQ2041, and is intended to solicit comment. This document is based largely on P802.11v-D0.1, P802.11k-D3.5, and P802.11-REVma-D5.2.

7. Frame formats

7.1 MAC frame formats

7.3.2  Information Elements

Insert Element ID 57 into Table 26 and change the Reserved row accordingly:

Table 26—Element IDs

| Information Element | Element ID |
| --- | --- |
| Transmit Power Management | 57 |
| Reserved | 5758-220 |

Insert the following new clause after clause 7.3.2.40:

7.3.2.41 Transmit Power Management element

The Transmit Power Management Element contains information necessary to allow a non-AP STA to determine the maximum transmit power to be used when a part of this cell (i.e. associated to this AP).  The format of the Transmit Power Management element is shown in Figure vx.

|  | Element ID | Length | Transmit Power Management |
| --- | --- | --- | --- |
| Octets: | 1 | 1 | 1 |

Figure vx—Transmit Power Management element format

The Length field is set to 1.

The Transmit Power Management field is set to a value that allows the transmit power of data frames to be constrained by the AP to which the STA is associated.  The field is coded as an unsigned integer in units of decibels.  The use of the Transmit Power Management element is described in 11.15.4.

#### 7.2.3.1 Beacon frame format

Insert new row into Table 8 as shown below:

Table 8—Beacon frame body

| Order | Information | Notes |
| --- | --- | --- |
| 29 | Transmit Power Management | The Transmit Power Management element may be present if dot11WirelessManagementImplemented is true. |

#### 7.2.3.5 Association Response frame format

Insert new row into table 11 as shown below:

Table 11—Association Response frame body

| Order | Information | Notes |
| --- | --- | --- |
| 10 | Transmit Power Management | The Transmit Power Management Element may be present if dot11WirelessManagementImplemented is true. |

#### 7.2.3.7 Reassociation Response frame format

Insert new row into table 13 as follows:

Table 13—Reassociation Response frame body

| Order | Information | Notes |
| --- | --- | --- |
| 10 | Transmit Power Management | The Transmit Power Management Element may be present if dot11WirelessManagementImplemented is true. |

#### 7.2.3.9 Probe Response frame format

Insert new row into Table 15 as follows:

Table 15—Probe Response frame body

| Order | Information | Notes |
| --- | --- | --- |
| 27 | Transmit Power Management | The Transmit Power Management Element may be present if if dot11WirelessManagementImplemented is true. |

Insert the following new clause after clause 7.4.5.6

7.4.6 Radio Management Action details

Insert the following row into table v7 and update the reserved field appropriately:

Table v7 — Wireless Network Management Action field value

| Action field value | Description |
| --- | --- |
| 4 | Radio Management Request |
| 5-255 | Reserved |

#### 7.4.6.5 Radio Management Request frame format

The Radio Management Request frame uses the Action frame body format. It is transmitted by a STA requesting a non-AP STA to control its transmit power. The format of the frame is shown in Figure v11.

|  | Category | Action | Transmit Power Management |
| --- | --- | --- | --- |
| Octets: | 1 | 1 | 3 |

Figure v11—Radio Management Request frame body format

The Category field shall be set to the value indicating the Radio Management category, as specified in Table 19a in 7.3.1.11.

The Action field shall be set to indicate a Radio Management Request according to table v7 in clause 7.4.6.

The Transmit Power Management field shall contain the Transmit Power Management element as described 7.3.2.41.

Insert the following clause after clause 11.15.5:

11.15.4 Transmit Power Management Request

The Transmit Power Request is used by a STA to communicate to a non-AP STA the maximum transmit power to be used by the receiving STA for data frames.  The maximum transmit power to be used is defined as the lesser of:

1) the maximum transmit power level specified for the channel in the Country element minus the transmit power management specified for the current channel (from the MIB) in the Transmit Power Management element

2) the maximum transmit power level specified for the channel in the Country element minus the local power constraint specified for the channel (from the MIB) in the Power Constraint element.

When the Transmit Power Management element is received in a Radio Management Action frame the value of Transmit Power Management shall override the value received in a Beacon frame.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.