IEEE P802.11
Wireless LANs

| TGn Joint Proposal MAC Results |
| --- |
| Date: 2005-12-30 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Adrian Stephens | Intel Corporation | 15 JJ Thompson Ave Cambridge CB3 0FD United Kingdom |  | adrian.p.stephens@intel.com |
| Yuichi Morioka | Sony Corporation | Oval Court Ohsaki MARK WEST, 2-17-1 Higashigotanda, Shinagawa-ku, Tokyo, 141-0022 Japan | +81-3-6409-3201 | morioka@wcs.sony.co.jp |
| Tomoko Adachi | Toshiba Corporation | 1, Komukai Toshiba-cho, Saiwai-ku, Kawasaki, 212-8582 Japan | +81-44-549-2433 | tomo.adachi@toshiba.co.jp |
| Dmitry Akhmetov, Sergey Shtin | Intel Corporation | Leninsy ave 160, 196247 Saint Petersburg, Russia |  | dmitry.akhmetov@intel.com sergey.shtin@intel.com |

Introduction

Purpose of this Document

This document contains MAC simulation results for the TGn Joint Proposal to IEEE 802.11 TGn in compliance to the TGn call for proposals.

The TGn comparison criteria call for full disclosure of results and conditions.  We present the results at varying levels of detail in the following documents.  The most summarised form is found in the presentation material [6].  This document contains all of the mandatory results – except per-flow results. Documents [3], [4] and [5] contain the detailed per-flow results and parameter settings as well as results for other simulation conditions.

Revision History

| Document Revision | Date | Author | Change |
| --- | --- | --- | --- |
| pre R0 | 2005-12-23 | Adrian Stephens, Yuichi Morioka, Tomoko Adachi, Dmity Akhmetov, Sergey Shtin | First release for TGn Joint Proposal |
| R0 | 2005-12-28 | Dmity Akhmetov | Minor changes to reflect new MAC1 simulation numbers |

Simulation Methodology

### TBD UPDATE

Document [1] describes in full the methodology used to obtain this result.  This section contains a very brief summary of the methodologies.

Results were obtained using three independent MAC simulations which are called MAC1, MAC2 and MAC3 in this document.

The MAC1 simulation is based on the commercial Opnet ** simulation tool, with a substantially re-written MAC process and PHY pipeline.  The PHY model built into the pipeline is based on PER as a function of post-detection capacity.  The simulation uses three possible protection methods: Standard NAV, the LongNAV method of protection (a MAC-layer technique described in [2, section 8.1.7.1]) and Extended PHY Protection (described in [1]).

Results reported here from that model use the LongNAV protection method. The simulation supports MAC Header compression, reverse direction data and periodic reverse direction data MAC options Implicit BAR and Compressed BA as described in [1, section 2.1.8.5 and 2.1.8.6], A-MSDU aggregation as described in [1, section 2.1.8.7]

For the MAC1 simulation, variants of the standard SS with increased TCP offered load set to the equivalent of 100Mbps per TCP application in ss#1 and of 30Mbps per TCP application in ss#4 and ss#6 were also simulated.  These are shown as "SS1 +", "SS4 +" and "SS6 +" below.

The MAC2 simulation is a discrete event-based simulator written in "C".  The PHY model is based on PER as a function of SNR.  The simulation supports two protection methods:  Standard NAV and Extended PHY Protection (described in [1]).  Results reported here from that model use the Extended PHY protection method.

The MAC3 simulation is based on the commercial Opnet simulation tool with the model based on MAC1 (details are described in [1]). The differences between MAC1 model are that the BAR frame is completely deleted from the data aggregate to simulate the Implicit BAR behavior and the effect of link adaptation for short range channel variation is turned off which appears to be MCS fixed for each traffic per node. To turn off the effect of link adaptation based on PER given from post-detection capacity, the PHY model is changed to be based on PER as a function of SNR. The simulation uses Long NAV as the protection method.

The simulation supports the mandatory Extended BA features (described in [2]). The purpose of this simulation is to investigate the performance benefits of the Extended BA features. One of the benefits of Extended BA is that it reduces implementation load using Partial State BA. So the investigation is done under implementation realistic conditions (i.e., 8 MPDUs aggregated in A-MPDU). Therefore MAC3 simulation does not aim to improve the total throughput. Other features such as A-MSDU, Reverse Direction, PSMP, Multiple TID Block Ack, and N-Immediate BA are not used.

The offered load of SS1 +, 4 +, and 6 + in MAC3 is twice larger than the standard SS defined in the TGn UMs. The offered load of SS16, 17, 18, and 19 are the same with the standard SS definition. SS17 + shows the results for offered load three times larger than the one defined as the TGn UM.

Model Credits

The following people created the models and provided the PHY simulation results embodied in the MAC simulations.

| Model | MAC Model | PHY Curves |
| --- | --- | --- |
| MAC1 | Dmitry Akhmetov, Intel Adrian Stephens, Intel | John Sadowsky, Intel Sergey Shtin, Intel |
| MAC2 | Yuichi Morioka, Sony Kenzoh Nishikawa, Sony Kazuyuki Sakoda, Sony | Darren McNamarra, Toshiba John Sadowsky, Intel |
| MAC3 | Tomoko Adachi, Toshiba | Darren McNamara, Toshiba |

Results for Mandatory Comparison Criteria and FR

Summary of Configurations

### MAC1 2x2x20

| Parameter | Value |
| --- | --- |
| Number of Tx Antennae | 2 |
| Number of Rx Antennae | 2 |
| Nominal Channel Width | 20 MHz |
| PHY Options enabled | SGI where allowed |
| TCP Model | Reno |
| Protection Method | LongNAV |
| Channel Access Method | Optimised HCCA for QoS flows and EDCA for non-QoS flows mimicking the use of TSPECs |
| QoS parameter Optimization | An HCCA schedule was created manually that satisfied the QoS constraints. |
| BlockAck policy | Implicit BA, Compressed BA |
| A-MSDU usage | ON |
| A-MPDU usage | ON |
| PSMP | OFF |
| Reverse data flow | ON |

### MAC1 2x2x40

| Parameter | Value |
| --- | --- |
| Number of Tx Antennae | 2 |
| Number of Rx Antennae | 2 |
| Nominal Channel Width | 40 MHz |
| PHY Options enabled | SGI where allowed |
| TCP Model | Reno |
| Protection Method | LongNAV |
| Channel Access Method | Optimised HCCA for QoS flows and EDCA for non-QoS flows mimicking the use of TSPECs |
| QoS parameter Optimization | An HCCA schedule was created manually that satisfied the QoS constraints. |
| BlockAck policy | Implicit BAR, Compressed BA |
| A-MSDU usage | ON |
| A-MPDU usage | ON |
| PSMP | OFF |
| Reverse data flow | ON |

### MAC2 2x2x20

| Parameter | Value |
| --- | --- |
| Number of Tx Antennae | 2 |
| Number of Rx Antennae | 2 |
| Nominal Channel Width | 20 MHz |
| PHY Options enabled | None |
| TCP Model | New Reno |
| Protection Method | Extended PHY Protection |
| Channel access method | EDCA |
| QoS Parameter Optimization | Optimized EDCA Contention Window Settings were used to satisfy QoS Requirements. |
| BlockAck policy | Compressed BA |
| A-MSDU usage | OFF |
| PSMP | OFF |
| Reverse data flow | OFF |

### MAC2 2x2x40

| Parameter | Value |
| --- | --- |
| Number of Tx Antennae | 2 |
| Number of Rx Antennae | 2 |
| Nominal Channel Width | 40 MHz |
| PHY Options enabled | None |
| TCP Model | New Reno |
| Protection Method | Extended PHY Protection Note, Extended PHY Protection vs LongNAV comparisons derived from the MAC2 results are shown in section 3.1 below. |
| Channel access method | EDCA |
| QoS Parameter Optimization | Optimized EDCA Contention Window Settings were used to satisfy QoS Requirements. |
| BlockAck policy | Compressed BA |
| A-MSDU usage | OFF |
| PSMP | OFF |
| Reverse data flow | OFF |

### MAC3 2x2x20 Parameters

| Parameter | Value |
| --- | --- |
| Number of Tx Antennae | 2 |
| Number of Rx Antennae | 2 |
| Nominal Channel Width | 20 MHz |
| PHY Options enabled | None |
| TCP Model | Reno |
| Protection Method | Long NAV |
| Channel Access Method | Optimised HCCA for QoS flows and EDCA for non-QoS flows mimicking the use of TSPECs |
| QoS Parameter Optimization | An HCCA schedule was created manually that satisfied the QoS constraints. |
| BlockAck policy | Mandatory features of Extended BA |
| Max. No. of MPDUs in A-MPDU | 8 |
| A-MSDU usage | OFF |
| PSMP | OFF |
| Multiple TID Block Ack | OFF |
| Reverse Direction | OFF |
| N-Delayed BA | OFF |

### MAC3 2x2x40 Parameters

| Parameter | Value |
| --- | --- |
| Number of Tx Antennae | 2 |
| Number of Rx Antennae | 2 |
| Nominal Channel Width | 40 MHz |
| PHY Options enabled | None |
| TCP Model | Reno |
| Protection Method | Long NAV |
| Channel Access Method | Optimised HCCA for QoS flows and EDCA for non-QoS flows mimicking the use of TSPECs |
| QoS parameter Optimization | An HCCA schedule was created manually that satisfied the QoS constraints. |
| BlockAck policy | Mandatory features of Extended BA |
| Max. No. of MPDUs in A-MPDU | 8 |
| A-MSDU usage | OFF |
| PSMP | OFF |
| Multiple TID Block Ack | OFF |
| Reverse Direction | OFF |
| N-Delayed BA | OFF |

Results relating to MAC simulations

Note, the channel access mechanism used to obtain the results is indicated with these colours:

| Optimised HCCA for QoS flows and EDCA for non-QoS flows mimicking the use of TSPECs | Optimized EDCA Contention Window Settings |
| --- | --- |

| CC# | Name | Result | MAC1 | MAC2 | MAC3 |
| --- | --- | --- | --- | --- | --- |
|  |  |  | 2x2x20 | 2x2x40 | 2x2x20 | 2x2x40 | 2x2x20 | 2x2x40 |
| CC3 | List of goodput results for usage models 1, 4 and 6. | SS1 (Mbps) | n/a | n/a | 61.82 | 80.65 | n/a | n/a |
|  |  | SS1 + | 107.28 | 183.56 | n/a | n/a | 80.1 | 117.8 |
|  |  | SS4 | n/a | n/a | 56.93 | 88.93 | n/a | n/a |
|  |  | SS4 + | 106.87 | 215.82 | n/a | n/a | 87.7 | 162.5 |
|  |  | SS6 | n/a | n/a | 47.16 | 64.06 |  |  |
|  |  | SS6 + | 98.29 | 194.12 | n/a | n/a | 61.2 | 119.0 |
| CC15 | Sharing of medium with legacy devices | T1 (Mbps) | 99.97 | n/a | n/a | n/a | See section 1.7 |
|  |  | T2 (Mbps) | 45.22 | n/a | n/a | n/a |  |
|  |  | T3 (Mbps) | 59.54 | n/a | n/a | n/a |  |
|  |  | T4 (Mbps) | 23.34 | n/a | n/a | n/a |  |
| CC18 | HT Usage Models Supported (non QoS) | SS1 (Mbps/ratio) | n/a | n/a | 9.77/0.32 | 28.60/0.92 | n/a | n/a |
|  |  | SS1 + | 54.84/0.27 | 131.10/0.66 | n/a | n/a | 27.8/0.14 | 65.5/0.33 |
|  |  | SS4 | n/a | n/a | 47.97/0.11 | 80.00/0.18 | n/a | n/a |
|  |  | SS4 + | 97.80/0.22 | 206.71/0.27 | n/a | n/a | 80.7/0.10 | 155.4/0.20 |
|  |  | SS6 | n/a | n/a | 4.00/0.20 | 21.41/1.07 | n/a | n/a |
|  |  | SS6 + | 53.53/0.18 | 149.28/.50 | n/a | n/a | 16.4/0.055 | 74.2/0.25 |
| CC19 | HT Usage Models Supported (QoS) | SS1 | n/a | n/a | 16/17 | 17/17 | n/a | n/a |
|  |  | SS1 + | 17/17 | 17/17 | n/a | n/a | 17/17 | 17/17 |
|  |  | SS4 | n/a | n/a | 18/18 | 18/18 | n/a | n/a |
|  |  | SS4 + | 18/18 | 18/18 | n/a | n/a | 18/18 | 18/18 |
|  |  | SS6 | n/a | n/a | 39/39 | 39/39 | n/a | n/a |
|  |  | SS6 + | 39/39 | 39/39 | n/a | n/a | 39/39 | 39/39 |
| CC20 | BSS Aggregate Goodput at the MAC data SAP | SS1 | M1 | n/a | n/a | 61.82 | 80.65 | n/a | n/a |
|  |  |  | M2 | n/a | n/a | 61.80 | 80.65 | n/a | n/a |
|  |  |  | M3 | n/a | n/a | 61.32 | 80.65 | n/a | n/a |
|  |  | SS1 + | M1 | 107.30 | 183.57 | n/a | n/a | 80.1 | 117.8 |
|  |  |  | M2 | 107.28 | 183.56 | n/a | n/a | 80.1 | 117.8 |
|  |  |  | M3 | 107.30 | 183.57 | n/a | n/a | 80.1 | 117.8 |
|  |  | SS4 | M1 | n/a | n/a | 56.93 | 88.93 | n/a | n/a |
|  |  |  | M2 | n/a | n/a | 56.93 | 88.93 | n/a | n/a |
|  |  |  | M3 | n/a | n/a | 56.93 | 88.93 | n/a | n/a |
|  |  | SS4 + | M1 | 106.91 | 215.82 | n/a | n/a | 87.7 | 162.5 |
|  |  |  | M2 | 106.87 | 215.79 | n/a | n/a | 87.7 | 162.6 |
|  |  |  | M3 | 106.91 | 215.82 | n/a | n/a | 87.7 | 162.5 |
|  |  | SS6 | M1 | n/a | n/a | 47.16 | 64.06 | n/a | n/a |
|  |  |  | M2 | n/a | n/a | 47.16 | 64.06 | n/a | n/a |
|  |  |  | M3 | n/a | n/a | 47.16 | 64.06 | n/a | n/a |
|  |  | SS6 + | M1 | 98.35 | 194.12 | n/a | n/a | 61.2 | 119.0 |
|  |  |  | M2 | 98.29 | 194.01 | n/a | n/a | 61.2 | 119.0 |
|  |  |  | M3 | 98.35 | 194.12 | n/a | n/a | 61.2 | 119.0 |
| CC24 | MAC Efficiency | SS1 | n/a | n/a | 0.67 | 0.56 | n/a | n/a |
|  |  | SS1 + | 0.77 | 0.70 | n/a | n/a | 0.65 | 0.47 |
|  |  | SS4 | n/a | n/a | 0.54 | 0.45 | n/a | n/a |
|  |  | SS4 + | 0.83 | 0.80 | n/a | n/a | 0.67 | 0.60 |
|  |  | SS6 | n/a | n/a | 0.49 | 0.40 | n/a | n/a |
|  |  | SS6 + | 0.76 | 0.74 | n/a | n/a | 0.47 | 0.44 |
| CC27 | Throughput / Range |  | n/a | See section 1.8 |  |  | n/a | See section 1.8 |
| CC28 | Throughput / Range in 20MHz |  | See section 1.9 | n/a |  |  | See section 1.9 | n/a |
| CC58 | HT Spectral Efficiency | bps/Hz | From the CC28 curve, goodput is ~113.9 Mbps at a PSDU PHY rate of 130 Mbps for channel Models B and D. (GI=0.8us) Spectral Efficiency = 113.9/20 = 5.695 bps/Hz (for channel models B and D) | From CC27, goodput is 225.6 Mbps at a PSDU PHY rate of 270.0Mbps for Channel Models B and D. (GI=0.8us) Spectral Efficiency = 225.6/40 = 5.64 bps/Hz (for channel models B and D) |  |  |  |  |
| Note1: Refer to [3] for CC18/19 per-flow MAC1 results |
| Note2: Refer to [4] for CC18/19 per-flow MAC2 results |

MAC Comparison Criteria not related to simulation results

| CC# | Name | Disclosure |
| --- | --- | --- |
| CC11 | Backward compatibility with 802.11-1999 (Rev 2003) and 802.11g | Backwards compatibility is provided at the PHY level [2, section 12.3.1.2] essentially by retaining the legacy short and long training fields and the legacy signal field. Backward compatibility is managed within the MAC through the definition of an operating mode and rules for operation in each operating mode. Protection mechanisms are defined using both PHY-level ("extended PHY protection") and MAC-level techniques using legacy and legacy duplicate frames to establish protection. |
| CC46 | MAC Compatibility and parameters. | See section 1.10 |
| CC47 | MAC extensions | See section 1.11 |

CC15 from MAC3 simulation

The following tables show results for CC15 from the MAC3 simulation.

| CC# | Name | Result | MAC3 | MAC3 |
| --- | --- | --- | --- | --- |
|  |  |  | 2x2x20 | 2x2x40 |
|  |  |  | w/o Extended BA | wi. Extended BA | w/o Extended BA | wi.Extended BA |
| CC15 | Sharing of medium with legacy devices | SS17 | n/a | 98.989 | n/a | n/a |
|  |  | SS17 + | n/a | 122.441 | n/a | n/a |
|  |  | SS18 | 44.112 |  | n/a | n/a |
|  |  | SS19 | See next table | See next table | n/a | n/a |

The table below shows the throughput results for CC15 from the MAC3 simulation, vs. MCS for HT device.

54Mbps (64QAM, 3/4, 1x) is used as the MCS for legacy device.

| For HT device | w/o Extended BA | wi. Extended BA |
| --- | --- | --- |
| MCS | Rate(Mbps) | HT | Legacy | Total | HT | Legacy | Total |
| 64QAM,3/4,1x | 58.5 | 22.680 | 21.344 | 44.024 | 23.294 | 21.227 | 44.521 |
| 64QAM,5/6,1x | 65 | 23.261 | 22.462 | 45.722 | 24.739 | 21.827 | 46.566 |
| 16QAM,1/2,2x | 52 | 18.696 | 22.873 | 41.569 | 22.190 | 20.168 | 42.359 |
| 16QAM,3/4,2x | 78 | 26.323 | 22.991 | 49.314 | 32.597 | 19.698 | 52.295 |
| 64QAM,2/3,2x | 104 | 33.120 | 23.141 | 56.261 | 43.469 | 18.845 | 62.314 |
| 64QAM,3/4,2x | 117 | 37.195 | 22.748 | 59.943 | 43.896 | 20.521 | 64.417 |
| 64QAM,5/6,2x | 130 | 37.728 | 23.813 | 61.541 | 51.101 | 19.227 | 70.327 |

CC27

Figure 1 shows results for CC27 from the MAC1 simulation, truncated at 100m range for Channel B and Channel D.

The MAC and PHY parameters used are defined in [3, CC27 2x2x40 tab].   Any parameters (e.g. SIFS spacing and slot timings) not specified there take on the 802.11a values.

Figure 1 - CC27 Results from the MAC1 simulation

Figure 2 shows results for CC27 from the MAC3 simulation with Extended BA, truncated at 90m range for Channel B.

Figure 2  - CC27 Results from the MAC3 simulation

CC28

Figure 3 shows results for CC28 from the MAC1 simulation, truncated at 100m range for Channel B and Channel D.

The MAC and PHY parameters used are defined in [3, CC28 2x2x20 tab]. Any parameters (e.g. SIFS spacing and slot timings) not specified there take on the 802.11a values.

Figure 3 - CC28 Results from the MAC1 simulation

Figure 4 shows results for CC28 from the MAC3 simulation with Extended BA, truncated at 90m range for Channel B.

Figure 4 - CC28 Results from the MAC3 simulation

CC46 – Baseline options

"Provide a list of optional features of 802.11a/b/d/e/g/h/i/j that are required for HT operation, and a summary description of the manner in which they are used.  Include references to the sections in the technical proposal document where the complete details are given."

IEEE 802.11e

| Item | Feature | Brief Description | Sections in [2] |
| --- | --- | --- | --- |
| CF12 | QoS Supported | The proposal requires the use of features introduced in the IEEE 802.11e amendment. | TBD |
| QB4 | Block Acknowledgement | The TGn Joint Proposal requires support for Block Acknowledgment in the context of frame aggregation See below for a summary of the extensions.. | TBD |
| QB5 | Automatic Power Save Delivery | Enhanced in the context of power-saving multi-poll (PSMP) sequences. | TBD |
| QD3 | Continuation of EDCA TXOP Support | Under LongNAV rules, a TXOP can be truncated by use of CF-END | TBD |

CC47

"Provide a summary description of MAC extensions beyond 802.11a/b/d/e/g/h/i/j that are required for HT operation. Include references to the sections in the technical proposal document where the complete details are given."

| Feature | Brief Description | Section in [2] |
| --- | --- | --- |
| A-MPDU Aggregation | Allows the transmission of multiple MPDU in a single PSDU | TBD |
| A-MSDU Aggregation | Allows the transmission of multiple MSDU within a single Data MPDU | TBD |
| Bi-directional data flow | Allows the aggregation of control MPDUs in one direction with Data MPDUs in the reverse direction under control of the TXOP owner | TBD |
| MAC Protection | Two additional procedures for MAC protection, Long NAV, and Extend PHY Protection | TBD |
| Coexistence Mechanisms | Definition of a rules for legacy protection and management of channel selection and width. | TBD |
| MAC Support for Closed Loop Link adaptation | Allows the adaptation of modulation coding scheme according to channel conditions | TBD |
| Extended BA | BA extended by the following features: Compression of the BA Implicit BAR Partial State Multiple-TID BA/BAR | TBD |
| Power-Save Multi-Poll | A Power-save multipoll combines with 802.11e Unscheduled and Scheduled APSD to allow STA to wake at known times for downlink and uplink data. | TBD |

FR1

"Demonstrate at least one set of conditions under which 100 Mbps at the top of the MAC SAP can be achieved.  Provide all relevant information to document this."

In 2x2x40 mode of operation, the MAC1 simulation demonstrates a goodput of >225.6Mbps for SS16 using the mandatory features only of the MAC and PHY, simulation methodology described in [1] and the MAC and PHY parameters reported in [3,  "ss#16 CC27 2x2x40"].

FR2

"Proposal supports at least one mode of operation that supports 100Mbps throughput at the top of the MAC SAP in a 20MHz channel. Provide all relevant information to document this."

The mandatory minimum PHY mode of operation is 2x2, 64 QAM, R=5/6

This corresponds to 130Mbps instantaneous rate at the PHY (using GI=0.8).

A maximum goodput of 113.9. Mbps is reported in [3, "ss#16 CC28 2x2x20" tab]. The curve crosses 100Mbps at about 13m range. (channel model B)

Required Additional Disclosures

| Number | Name | Disclosure |
| --- | --- | --- |
| AD2 | TCP Model Parameters | Refer to [3, "Common" tab]. Refer to [1, section 3.1] (MAC2 TCP parameters) |
| AD3 | MAC simulation methodology | This is described in [1], please refer to [1]. |
| AD4 | MAC simulation occupied channel width | For nxnx40 results, a nominal channel width of 40MHz was occupied. For nxnx20 results, a nominal channel width of 20MHz was occupied. |
| AD5 | Justification of low PLR rates achieved | This disclosure relates specifically to the MAC1 2x2x40 simulation. MAC1 simulation targets < 10% PER at the top of the PHY. The fast link adaptation method described in [1, section 2.2.4] achieves the performance shown in [1, section 5]. Typically PER is < 1% except at extreme range. Assuming a PER of 1%, the specified residual PLR of 10-7 can be reached by permitting 4 transmission attempts (3 retries). Assuming uncorrelated errors, these retry attempts will include (with high probability) only a single Data MPDU. At the PHY rates observed in simulation for the Video flows (average 230Mbps), a single Data MPDU / BAR / BA retry exchange takes ~300us. 3 retries takes ~1ms. The average transport delay observed with the Video traffic is <30ms. Attributing this entirely to channel access delay, 3 retries in a separate TXOP would take ~31ms, which is comfortably less than the 200ms delay bound. |

Characterisation of MAC Features

Protection Mechanisms

Selected CC results are presented from the MAC2 simulation to show the relative performances of the two protection modes described in [1] relating to the MAC2 simulation.

| CC# | Result | MAC2 2x2x40 Standard NAV | MAC2 2x2x40 Extended PHY Protection |
| --- | --- | --- | --- |
| CC3 | SS1 (Mbps) | 74.55 | 80.65 |
|  | SS4 | 79.31 | 88.93 |
|  | SS6 | 52.89 | 64.06 |
| CC18 | SS1 (Mbps/ratio) | 22.49/0.73 | 28.60/0.92 |
|  | SS4 | 70.37/0.16 | 80.00/0.18 |
|  | SS6 | 9.96/0.50 | 21.41/1.07 |
| CC19 | SS1 | 16/17 | 17/17 |
|  | SS4 | 18/18 | 18/18 |
|  | SS6 | 39/39 | 39/39 |
| CC20 | SS1 | M1 | 74.55 | 80.65 |
|  |  | M2 | 74.54 | 80.65 |
|  |  | M3 | 74.05 | 80.65 |
|  | SS4 | M1 | 79.31 | 88.93 |
|  |  | M2 | 79.31 | 88.93 |
|  |  | M3 | 79.31 | 88.93 |
|  | SS6 | M1 | 52.89 | 64.06 |
|  |  | M2 | 52.89 | 64.06 |
|  |  | M3 | 52.89 | 64.06 |
| CC24 | SS1 | 0.54 | 0.56 |
|  | SS4 | 0.44 | 0.45 |
|  | SS6 | 0.36 | 0.40 |

Extended BA

Compressed BA, Partial State BA, and Implicit BAR are the mandatory features of the TGn Joint Proposal.  This section shows the performance results from the MAC3 simulator with/without the use of these features.

### Summary of Extended BA benefit

From the SS6 results of 20 MHz, it can be seen that the aggregate throughput is increased by approximately 10% when the Extended BA feature is used.

### Extended BA Results

| CC# | Name | Result | MAC3 | MAC3 |
| --- | --- | --- | --- | --- |
|  |  |  | 2x2x20 | 2x2x40 |
|  |  |  | w/o Extended BA | wi. Extended BA | w/o Extended BA | wi.Extended BA |
| CC3 | List of goodput results for usage models 1, 4 and 6. | SS1 + (Mbps) | 75.3 | 80.1 | 111.9 | 117.8 |
|  |  | SS4 + | 80.8 | 87.7 | 152.9 | 162.5 |
|  |  | SS6 + | 55.7 | 61.2 | 110.5 | 119.0 |
| CC18 | HT Usage Models Supported (non QoS) | SS1 + (Mbps/ratio) | 23.9/ 0.12 | 27.8/ 0.14 | 59.6/0.30 | 65.5/0.33 |
|  |  | SS4 + | 73.7/ 0.09 | 80.7/ 0.10 | 145.9/0.19 | 155.4/0.20 |
|  |  | SS6 + | 10.9/ 0.036 | 16.4/ 0.055 | 65.8/0.22 | 74.2/0.25 |
| CC19 | HT Usage Models Supported (QoS) | SS1 + | 17/17 | 17/17 | 17/17 | 17/17 |
|  |  | SS4 + | 18/18 | 18/18 | 18/18 | 18/18 |
|  |  | SS6 + | 39/39 | 39/39 | 39/39 | 39/39 |
| CC20 | BSS Aggregate Goodput at the MAC data SAP | SS1 + | M1 | 75.3 | 80.1 | 111.9 | 117.8 |
|  |  |  | M2 | 75.3 | 80.1 | 111.9 | 117.8 |
|  |  |  | M3 | 75.3 | 80.1 | 111.9 | 117.8 |
|  |  | SS4 + | M1 | 80.8 | 87.7 | 152.9 | 162.5 |
|  |  |  | M2 | 80.8 | 87.7 | 152.9 | 162.5 |
|  |  |  | M3 | 80.8 | 87.7 | 152.9 | 162.5 |
|  |  | SS6 + | M1 | 55.7 | 61.2 | 110.5 | 119.0 |
|  |  |  | M2 | 55.7 | 61.2 | 110.5 | 119.0 |
|  |  |  | M3 | 55.7 | 61.2 | 110.5 | 119.0 |
| CC24 | MAC Efficiency | SS1 + | 0.61 | 0.65 | 0.45 | 0.47 |
|  |  | SS4 + | 0.62 | 0.67 | 0.57 | 0.60 |
|  |  | SS6 + | 0.43 | 0.47 | 0.41 | 0.44 |
| CC15 | Sharing of medium with legacy devices | SS17 |  | 98.989 |  |  |
|  |  | SS17 + |  | 122.441 |  |  |
|  |  | SS18 | 44.112 |  | n/a | n/a |
|  |  | SS19 | See section 4.2.7 | See section 4.2.7 |  |  |
| CC27 | Throughput / Range | SS16 | n/a | n/a |  | See section 4.2.8 |
| CC28 | Throughput / Range in 20MHz | SS16 |  | See section 4.2.9 | n/a | n/a |

References

[1] IEEE 802.11-05/1267, "TGn Joint Proposal MAC Simulation Methodology"

[2] IEEE 802.11-05/1095, "TGn Joint Proposal MAC Specification"

[3] IEEE 802.11-05/1268, "TGn Joint Proposal MAC1 Simulation Results"

[4] IEEE 802.11-05/1269, "TGn Joint Proposal MAC2 Simulation Results"

[5] IEEE 802.11-05/1270, "TGn Joint Proposal MAC3 Simulation Results"

[6] IEEE 802.11-05/1165, "TGn Joint Proposal MAC Detail"

# Footnotes

** Other names and brands may be claimed as the property of others.

Note that the PHY model used for this simulation (results T1-T4) was the same as that used for the other MAC simulations.  As such it included impairments IM1, IM5 and IM6.  This is not expected to significantly affect these results.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document discloses results required by the 802.11n comparison criteria and functional requirements related to the MAC performance of the TGn Joint Proposal [1] [2].