IEEE P802.11
Wireless LANs

| Draft TGu Functional Requirements and Scope |
| --- |
| Date: 2005-01-18 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Stephen McCann | Siemens Roke Manor | Roke Manor Research Ltd Old Salisbury Lane Romsey Hampshire SO51 0ZN United Kingdom | +44 1794 833341 | stephen.mccann@roke.co.uk |

Document Version History

| Revision | Comments | Date | Authors | Editor |
| --- | --- | --- | --- | --- |
| r0 | Initial Version | December 10, 2004 | See above author list…. | Stephen McCann |

Table of Contents

Introduction	3

Document Purpose	3

Scenario and Definitions	3

Categories for Organization of Functional Requirements and Scope (Informative)	4

Minimum Functional Requirements	5

Scope Clarification Organized by Functional Categories for TGu	5

User Access and User Experience (USER_ACCESS)	5

Support Required by Operators (OPERATOR)	6

References	6

# Introduction

## Document Purpose

This document specifies the minimum functional requirements (FRs) that must be addressed by the first draft specification of IEEE 802.11 Task Group u.  It also defines the scope of the efforts undertaken by TGu.  This document is intended to supplement the 802.11u PAR [1] and 5 Criteria [2] documents, which provide the overriding requirements for TG u.

The focus of the scope description is to clarify the areas of functionality that will or will not be considered by TGu.  This is intended to provide additional informative guidelines for proposals.  This document does not attempt to further prioritize the “in-scope” functions.  Labeling of individual features as mandatory or optional will be done as a later step.

This document is a working document that presents a “best estimate” summary for the minimum functional requirements and scope of TGu, but which will also evolve and be updated as the TGu effort progresses.

## Scenario and Definitions

Introductory text.

# Categories for Organization of Functional Requirements and Scope (Informative)

The following table includes a list of system functional categories that are relevant for IEEE 802.11u Interworking with External Networks, and will be covered by the functional requirements and scope descriptions in this document.   These categories are only informative and intended to help with the organizational structure of the functional requirements and scope items in Section 0 and Section 0.

| Functional Category Label | Functional Category Description |
| --- | --- |
| GEN | Generic |
| USER_ACCESS | User access and user experience |
| OPERATOR | Support required by operators |

Table 1: Functional Categories for TGu

# Minimum Functional Requirements

The following table defines the minimum functional requirements that must be addressed by the first draft specification of IEEE 802.11 TG u.  A proposal submitted for consideration to 802.11 TGu and declared to be complete is required to meet the functional requirements defined in this table.  A partial proposal may meet some of the requirements stated here.

A separate comparison criteria document [x] includes a template with an entry for each functional requirement in this table, allowing those submitting proposals to check off which FRs are covered by a proposal and provide references to relevant sections of the proposal where each FR is covered.

| Number | Functional Category (see Table 1) | Name | Requirement | From PAR | Notes (informative) |
| --- | --- | --- | --- | --- | --- |
| FR1 | GENERIC | Interworking | The proposal shall enable interworking between an IEEE 802.11 access network and external networks | X |  |
| FR2 | … | … | … |  |  |

Table 2: Minimum Functional Requirements for TGu

# Scope Clarification Organized by Functional Categories for TGu

This document defines the scope of the efforts undertaken by TGu.   It indicates which aspects of standards develop are or are not considered by the TGu effort as follows:

- In-scope – aspects that will be considered, addressed, or affected by TGu

- Out-of-scope – aspects that will not be considered or addressed by TGu

- Unaffected – aspects that may co-exist with TGu, but will be unaffected, or essentially preserved, by TGu

- To-be-determined – aspects which are, as yet, TBD (to-be-determined) with respect to TGu

The focus of this section is to clarify the areas of functionality that will or will not be considered by TGu.  This is intended to provide additional informative guidelines for proposals.  This section does not attempt to further prioritize the “in-scope” functions as mandatory or optional.

## User Access and User Experience (USER_ACCESS)

The following captures the scope of user access and user experience requirements to be considered by TGu (this could include requirements for network detection and selection, MAC address anonymity, support for user registration, secure anonymous access etc.):

| Functionality Applicability | Notes (Informative) |
| --- | --- |
| In-scope |  |  |
| USER_ACCESS_SCP1 | This provides additional information to STAs about the characteristics of the network to support network selection decisions |  |
| USER_ACCESS_SCP2 | Investigate aspects related to beacon scaleability. |  |
| Unaffected |  |  |
| To-be-determined |  |  |
| Out-of-scope |  |  |
|  | Specification of network detection and selection protocols implemented at Layer-3 | Solution provided by IEEE 802.21 |

## Support Required by Operators (OPERATOR)

The following captures required support in the IEEE 802.11 network to allow operators to provide the required service to their users (this could include policy, QoS mapping, charging requirements etc.):

| Functionality Applicability | Notes (Informative) |
| --- | --- |
| In-scope |  |  |
| OPERATOR_SCP1 | Issue concern how policy rules from the network are enforced within the IEEE 802.11 access point |  |
| OPERATOR_SCP2 | Specific requirements placed on IEEE 802.11 by external network operators, where traffic enforcement policies are applied to user traffic. This particularly applies to the scenario where multiple operators share the IEEE 802.11 hotspot infrastructure. |  |
| Unaffected |  |  |
| To-be-determined |  |  |
| Out-of-scope |  |  |

# References

[1] 11-04-0506-11-wien-draft-par-ieee-802-11-wien.doc

[2] 11-04-0507-04-wien-draft-5-criteria-ieee-802-11-wien.doc

[3] 11-04-0805-02-000r-tgr-requirements.doc

[4] 11-04-1174-09-000s-draft-tgs-functional-requirements-and-scope.doc

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document specifies the minimum functional requirements and scope for Interworking with External Networks mechanisms to be defined by 802.11 TGu.