IEEE P802.11
Wireless LANs

| Proposed Normative Text for QoS Metrics |
| --- |
| Date: 2005-03-9 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Emily H. Qi | Intel Corporation | 2111 N.E 25th Ave. Hillsboro, OR 97124 | 503-264-7799 | Emily.h.qi@intel.com |
| Simon Black | Nokia |  | +441353648857 | EXT-simon.3.black @nokia.com |
| Tim Olson | Cisco Systems, Inc. | 170 W. Tasman Dr. San Jose, CA 95134 | 408-853-4527 | tolson@cisco.com |
| Dave Stephenson | Cisco Systems, Inc. | 170 W. Tasman Dr. San Jose, CA 95134 | 408-527-7991 | daves@cisco.com |
| Joe Kwak | InterDigital Coummunication | 482 Degas Bolingbrook, IL 60440 | 630-739-4327 | joekwak@mindspring.com |
| Jari Jokela | Nokia |  | +358504860445 | jari.jokela@nokia.com |
| Jarkko Kneckt | Nokia |  | +358504821550 | jarkko.kneckt@nokia.com |

Modify Table 20b as indicated below:

Table 20b—Measurement Type Definitions for Measurement Requests

| Name | Measurement Type |
| --- | --- |
| Basic Request | 0 |
| Clear Channel Assessment (CCA) request | 1 |
| Receive power indication (RPI) histogram request | 2 |
| Channel Load request | 3 |
| Noise histogram request | 4 |
| Beacon request | 5 |
| Frame request | 6 |
| Hidden node request | 7 |
| Medium sensing time histogram request | 8 |
| STA statistics request | 9 |
| LCI request | 10 |
| Measurement Pause Request | 11 |
| Transmit QoS Metrics request | 12 |
| Reserved | 13-255 |

Add the following subsection after Clause 7.3.2.21.12 in 802.11k draft 2.0 as indicated below:

##### 7.3.2.21.13 Transmit QoS Metrics Request

The Measurement Request field corresponding to a Transmit QoS Metrics Request is shown in Figure +1. A response to a Transmit QoS Metrics Request is a Transmit QoS Metrics Report.

|  | Randomization Interval | Measurement Duration | Peer QSTA Address | Traffic Identifier | Bin 0 Range |
| --- | --- | --- | --- | --- | --- |
| Octets: | 2 | 2 | 6 | 1 | 1 |

Figure +1 – Measurement Request field format for a Transmit QoS Metrics Request

Randomization Interval shall be set to the desired maximum random delay in the measurement start time, expressed in TUs. The use of Randomization Interval is described in 11.7.3.

The Measurement Duration shall be set equal to the duration of the requested measurement, expressed in TUs.

The Peer QSTA Address shall contain the 6 byte MAC address in the Address 1 field of the measured Data frames.

Traffic Identifier shall indicate the TC or TS for which traffic is to be measured. Values 0 through 15 are defined. Values 16-255 are reserved.

Bin 0 Range shall indicate the delay range of the first bin (Bin 0) of the Transmit Delay Histogram, expressed in TUs. It is also used to calculate the delay ranges of the other 5 bins making up the histogram. The delay range for each bin shall increase in a binary exponential fashion as described in 7.3.2.22.13.

Modify the table 20c as indicated below:

Table 20c—Measurement Type definitions for measurement reports

| Name | Measurement Type |
| --- | --- |
| Basic report | 0 |
| Clear Channel Assessment (CCA) report | 1 |
| Receive power indication (RPI) histogram report | 2 |
| Channel Load report | 3 |
| Noise histogram report | 4 |
| Beacon report | 5 |
| Frame report | 6 |
| Hidden node report | 7 |
| Medium sensing time histogram report | 8 |
| STA statistics report | 9 |
| LCI request | 10 |
| Measurement Pause Request | 11 |
| Transmit QoS Metrics report | 12 |
| Reserved | 13 - 255 |

Add the following subsection after Clause 7.3.2.22.12 in 802.11k draft 2.0 as indicated below:

7.3.2.22.13 Transmit QoS Metrics Report

The format of the Measurement Report field corresponding to a Transmit QoS Metrics Report is shown in Figure k+2.

|  | Actual Measurement Start Time | Measurement Duration | Peer QSTA Address | Traffic Identifier |
| --- | --- | --- | --- | --- |
| Octets: | 8 | 2 | 6 | 1 |

|  | Transmitted MSDU Count | MSDU Discarded Count | MSDU Failed Count | MSDU Multiple Retry Count | QoS CFPolls Lost Count | Average Queue Delay | Average Transmit Delay |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Octets: | 4 | 4 | 4 | 4 | 4 | 4 | 4 |

|  | Bin 0 Range | Bin 0 Count | Bin 1 Count | Bin 2 Count | Bin 3 Count | Bin 4 Count | Bin 5 Count |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Octets: | 1 | 4 | 4 | 4 | 4 | 4 | 4 |

Figure k+2 – Measurement Report field format for Transmit Delay Metric Report

Actual Measurement Start Time shall be set equal to the TSF at the time at which the measurement started.

Measurement Duration shall be set equal to the duration over which the Transmit Frame Delay Report was measured, expressed in TUs.

The Peer QSTA Address shall contain the 6 byte MAC address in the Address 1 field of the measured Data frames.

Traffic Identifier shall indicate the TC or TS for which traffic is to be measured. Values 0 through 15 are defined. Values 16-255 are reserved.

The Transmitted MSDU Count, MSDU Failed Count, MSDU Discarded Count, MSDU Multiple Retry Count and QoS CFPolls Lost Count, Average Queue Delay, Average Transmit Delay, and delay histogram fields relate to transmissions to the QSTA given in the peer QSTA Address field.

The Transmitted MSDU Count field contains the number of MSDUs for the TC, or TS given by the Traffic Identifier successfully transmitted in the measurement duration.

The MSDU Discarded Count field contains the number of MSDUs for the TC, or TS given by the Traffic Identifier discarded due either to the number of transmit attempts exceeding dot11ShortRetryLimit or dot11LongRetryLimit as appropriate, or due to the MSDU lifetime having been reached.

The MSDU Failed Count field contains the number of MSDUs for the TC, or TS given by the Traffic Identifier discarded during the measurement duration due to the number of transmit attempts exceeding dot11ShortRetryLimit or dot11LongRetryLimit as appropriate.

The MSDU Multiple Retry Count field contains the number of MSDUs for the TC, or TS given by the Traffic Identifier that are successfully transmitted after more than one retransmission attempt.

The QoS CFPolls Lost Count field contains the number of QoS (+)CF-Poll frames transmitted where there was no response from the QSTA. QoS CFPolls Lost Count shall only be returned if the reporting QSTA is a QAP and the Traffic Identifier is for TS. If unused QoS CFPolls Lost count shall be set to 0.

Average Queue Delay shall be the average queuing delay of the frames (MSDUs) that are passed to the MAC during the measurement duration for the indicated destination and the indicated Traffic Identifier. Queue Delay shall be measured from the time the MSDU is passed to the MAC until the point at which the first, or only fragment is ready for transmission and shall be expressed in TUs.

Average Transmit Delay shall be the average delay of the frames (MSDUs) that are successfully transmitted during the measurement duration for the indicated destination and the indicated Traffic Identifier. Delay shall be measured from the time the MSDU is passed to the MAC until the point at which the entire MSDU has been successfully transmitted, including receipt of the final ACK from the peer QSTA if the QoSAck service class is being used. Average Transmit delay shall be expressed in TUs.

Bin 0 Range shall indicate the delay range of the first bin (Bin 0) of the Transmit Delay Histogram, expressed in TUs. It is also used to calculate the delay ranges of the other 5 bins making up the histogram. The delay range for each bin shall increase in a binary exponential fashion as follows:

B0 duration:   	 0 (  Delay <, 		for i =0;

Bi duration:  	*(  Delay < *     	for 1< i <5

Note: For instance, if Bin 0 Range is 10ms, the bin durations should be defined in table +1

Table k+1 – Delay Definitions for a Transmit QoS Report

| Bin | Measured Delay (TUs) |
| --- | --- |
| 0 | Delay <10 |
| 1 | 10 ( Delay < 20 |
| 2 | 20 ( Delay <40 |
| 3 | 40 ( Delay <80 |
| 4 | 80 ( Delay <160 |
| 5 | Delay ( 160 |

To compute the value reported in Bin i, Bi, 0 ≤ i < 5, of the Transmit Delay Histogram, the STA initializes all bin counts to zero.  For each MSDU successfully transmitted, the measured Transmit Delay determines which bin count is to be incremented.  If the measured delay has a duration time t within Bin i, then the frame count in Bin i is increased by one, up to a ceiling value of 232-1. Transmit Delay shall be measured from the time the MSDU is passed to the MAC until the point at which the entire MSDU has been successfully transmitted, including receipt of the final ACK from the peer QSTA if the QoSAck service class is being used. During the Transmit QoS Metrics Measurement, a histogram is generated that represents the distribution of Transmit Delay.

Add the following subsection after Clause 11.7.8.9  in 802.11k draft 2.0 as indicated below:

##### 11.7.8.10 Transmit QoS Metrics Report

A QSTA receiving a Transmit QoS Metrics Request shall respond with a Radio Measurement Report frame containing one Measurement (Transmit QoS Metrics) Report element. If the traffic stream (TS) that is corresponding to the Traffic Identifier is deleted, either by a DELTS Action Frame or by disassociation, the STA shall cease sending Radio Measurement Reports.

The Transmit QoS Metrics measurement shall be made on traffic that is transmitted from the measuring QSTA to the peer QSTA and TC or TS indicated in the request. The peer QSTA Address may be the MAC address of the QSTA from which the Measurement Request was sent, or the MAC address of another QSTA within the QBSS. This enables a QAP to query Transmit QoS metrics for DLS links. A QAP shall refuse measurement requests for traffic to other QSTAs in the BSS.

The requesting and reporting STAs must be QSTAs. A non-QSTA receiving a Transmit QoS Metrics Measurement Request shall reject the request with indication of “incapable”.

### ANNEX A

In A.4.13 add new entry RRM12 and renumber all following PICS items:

| RRM12 RRM12.1 RRM12.2 | Transmit Qos Metrics Type Transmit QoS Metrics Request Transmit QoS Metrics Report | 11.7, 11.7.8.10 7.3.2.21.13 7.3.2.22.13 | CFk AND CF12:O CFk AND CF12:O CFk AND CF12:O | Yes, No Yes, No Yes, No |
| --- | --- | --- | --- | --- |

### ANNEX D

In dot11CountersTable change Dot11CountersEntry as follows:

Dot11CountersEntry ::=

SEQUENCE {	dot11TransmittedFragmentCount	Counter32,

dot11MulticastTransmittedFrameCount	Counter32,

dot11FailedCount	Counter32,

dot11RetryCount	Counter32,

dot11MultipleRetryCount	Counter32,

dot11FrameDuplicateCount	Counter32,

dot11RTSSuccessCount	Counter32,

dot11RTSFailureCount	Counter32,

dot11ACKFailureCount	Counter32,

dot11ReceivedFragmentCount	Counter32,

dot11MulticastReceivedFrameCount	Counter32,

dot11FCSErrorCount	Counter32,

dot11TransmittedFrameCount	Counter32,

dot11WEPUndecryptableCount	Counter32,

dot11QoSDiscardedFragmentCount	Counter32,

dot11AssociatedStationCount	Counter32,

dot11QoSCFPollsReceivedCount	Counter32,

dot11QoSCFPollsUnusedCount	Counter32,

dot11QoSCFPollsUnusableCount	Counter32,

dot11QoSCFPollsLostCount	Counter32 }

Insert the following attribute definition to the end of the dot11CountersEntry attributes:

Dot11QoSCFPollsLostCount OBJECT-TYPE

SYNTAX Counter32

MAX-ACCESS read-only

STATUS current

DESCRIPTION

“This counter shall increment for each QoS (+)CF-Poll that has been issued by the HC where there was no response from the QSTA indicated in the RA field.”

::= { dot11CountersEntry 20 }

Add attributes to Dot11RRMRequestEntry as follows:

Dot11RRMRequestEntry ::=

SEQUENCE {

dot11RRMRqstIndex	Unsigned32,

dot11RRMRqstRowStatus 	RowStatus,

dot11RRMRqstToken 	OCTET STRING,

dot11RRMRqstIfIndex 	InterfaceIndex,

dot11RRMRqstType 	INTEGER,

dot11RRMRqstTargetAdd 	MacAddress,

dot11RRMRqstTimeStamp 	TimeTicks,

dot11RRMRqstChanNumber 	INTEGER,

dot11RRMRqstChannelBand 	INTEGER,

dot11RRMRqstRndInterval 	Unsigned32,

dot11RRMRqstDuration 	Unsigned32,

dot11RRMRqstParallel 	TruthValue,

dot11RRMRqstEnable 	TruthValue,

dot11RRMRqstRequest 	TruthValue,

dot11RRMRqstReport 	TruthValue,

dot11RRMRqstDurationMandatory 	TruthValue,

dot11RRMBeaconRqstMode 	INTEGER,

dot11RRMRqstBssid 	MacAddress,

dot11RRMRqstMeasPeriodUnit 	INTEGER,

dot11RRMRqstMeasurementPeriod 	INTEGER,

dot11RRMRqstMeasIntervalUnit 	INTEGER,

dot11RRMRqstMeasurementInterval 	INTEGER,

dot11RRMRqstReportingCondition 	INTEGER,

dot11RRMRqstThresholdOffset 	INTEGER,

dot11RRMRqstHysteresis 	INTEGER,

dot11MedSenseType 	INTEGER,

dot11MedSenseRCPIThreshold 	INTEGER,

dot11MedSenseBinOffset 	INTEGER,

dot11MedSenseBinDuration 	INTEGER,

dot11MedSenseNumBin 	INTEGER,

dot11STAStatRqstGroupID 	INTEGER,

dot11LCIRqstOctet 	INTEGER,

dot11TransmitQoSMetricsPeerQSTAAddress	MacAddress,

dot11TransmitQoSMetricsTrafficIdentifier	INTEGER,

dot11TransmitQoSMetricsBin0Range	INTEGER }

Change dot11RRMRqstType as follows:

dot11RRMRqstType OBJECT-TYPE

SYNTAX INTEGER {

channelLoad(3),

noiseHistogram(4),

beaconRequest(5),

frameRequest(6),

hiddenStation(7),

mediumSensingTimeHistogram(8),

staStatistics(9),

Pause(10),
LCI(11),

TransmitQoSMetrics(12) }

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"The measurement type of this RRM request row."

::= { dot11RRMRequestEntry 5 }

Add Attributes as follows after dot11LCIRqstOctet

dot11TransmitQoSMetricsPeerQSTAAddress OBJECT-TYPE

SYNTAX MacAddress

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"This attribute specifies the peer QSTA address to be measured for a TransmitQoSMetrics measurement"

::= { dot11RRMRequestEntry 33 }

dot11TransmitQoSMetricsTrafficIdentifier OBJECT-TYPE

SYNTAX INTEGER(0..16)

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"This attribute specifies the TC, or TS to be measured for a TransmitQoSMetrics measurement"

::= { dot11RRMRequestEntry 34 }

dot11TransmitQoSMetricsBin0Range OBJECT-TYPE

SYNTAX INTEGER(1..255)

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"This attribute specifies the delay range for bin 0 of the transmit delay histogram."

::= { dot11RRMRequestEntry 35 }

Add the following text after dot11STAStatisticsReport table:

-- ********************************************************************

-- * dot11TransmitQoSMetricsReport	TABLE

-- ********************************************************************

dot11TransmitQoSMetricsReportTable OBJECT-TYPE

SYNTAX SEQUENCE OF dot11TransmitQoSMetricsReportEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"Group contains the current list of Transmit Delay Metrics reports that have been received by the MLME. The report tables shall be maintained as FIFO to preserve freshness, thus the rows in this table can be deleted for memory constraints or other implementation constraints determined by the vendor. New rows shall have different RprtIndex values than those deleted within the range limitation of the index. One easy way is to monotonically increase RprtIndex for new reports being written in the table."

::= { dot11RRMReport 1 }

dot11TransmitQoSMetricsReportEntry OBJECT-TYPE

SYNTAX dot11TransmitQoSMetricsReportEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"An entry in the dot11TransmitQoSMetricsReportTable Indexed by dot11TransmitQoSMetricsRprtIndex."

INDEX { dot11TransmitQoSMetricsRprtIndex }

::= { dot11TransmitQoSMetricsReportTable 1 }

Dot11TransmitQoSMetricsReportEntry ::=

SEQUENCE {

dot11TransmitQoSMetricsRprtIndex	Unsigned32,

dot11TransmitQoSMetricsRprtRqstToken	OCTET STRING,

dot11TransmitQoSMetricsRprtIfIndex	InterfaceIndex,

dot11TransmitQoSMetricsMeasuringSTAAddr	MacAddress,

dot11TransmitQoSMetricsRprtActualStartTime	TSFType,

dot11TransmitQoSMetricsRprtMeasurementDuration	Unsigned32,

dot11TransmitQoSMetricsRprtPeerSTAAddress	MacAddress,

dot11TransmitQoSMetricsRprtTID	INTEGER,

dot11TransmitQoSMetricsRprtAverageQueueDelay	Integer32,

dot11TransmitQoSMetricsRprtAverageTransmitDelay	Integer32,

dot11TransmitQoSMetricsRprtTransmittedMSDUCount	Integer32,

dot11TransmitQoSMetricsRprtMSDUDiscardedCount	Integer32,

dot11TransmitQoSMetricsRptMSDUFailedCount	Integer32,

dot11TransmitQoSMetricsRptMultipleRetryCount	Integer32,

dot11TransmitQoSMetricsRptCFPollsLostCount 	Integer32,

dot11TransmitQoSMetricsRprtBin0Range	Integer,

dot11TransmitQoSMetricsRprtDelayHistogram	OCTET STRING }

dot11TransmitQoSMetricsRprtIndex OBJECT-TYPE

SYNTAX Unsigned32

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"Index for Transmit Delay Metrics Report elements in dot11TransmitQoSMetricsReportTable, greater than 0."

::= { dot11TransmitQoSMetricsReportEntry 1 }

dot11TransmitQoSMetricsRprtRqstToken OBJECT-TYPE

SYNTAX OctetString

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This attribute holds the request token that was specified in the measurement request that generated this measurement report.  This should be an exact match to the original dot11RRMRqstToken attribute. Note that there may be multiple entries in the table that match this value since a single request may generate multiple measurement reports."

::= { dot11TransmitQoSMetricsReportEntry 2 }

dot11TransmitQoSMetricsRprtIfIndex OBJECT-TYPE

SYNTAX InterfaceIndex

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"The InterfaceIndex for this row of TransmitQoSMetrics Report has been received on."

::= { dot11TransmitQoSMetricsReportEntry 3 }

dot11TransmitQoSMetricsMeasuringSTAAddr OBJECT-TYPE

SYNTAX MacAddress

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"The MAC address of the measuring STA for this row of Transmit Delay Metrics report."

::= { dot11TransmitQoSMetricsReportEntry 4 }

dot11TransmitQoSMetricsRprtActualStartTime OBJECT-TYPE

SYNTAX TSFType

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This attribute corresponds to the TSF value at the time when the measurement started."

::= { dot11TransmitQoSMetricsReportEntry 5 }

dot11TransmitQoSMetricsRprtMeasurementDuration OBJECT-TYPE

SYNTAX Unsigned32

MAX-ACCESS read-only

UNITS “TUs”

STATUS current

DESCRIPTION

"This attribute corresponds to the duration over which the Transmit Delay Metrics Report was measured, expressed in TUs."

::= { dot11TransmitQoSMetricsReportEntry 6 }

dot11TransmitQoSMetricsRprtPeerQSTAAddress OBJECT-TYPE

SYNTAX MacAddress

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"The MAC address present in the Address 1 filed of the measured data frames for this row of Transmit QoS Metrics report."

::= { dot11TransmitQoSMetricsReportEntry 7 }

dot11TransmitQoSMetricsRprtTID OBJECT-TYPE

SYNTAX INTEGER(0..16)

MAX-ACCESS read-only

STATUS current

DESCRIPTION

“Traffic Identifier shall indicate the TC or TS for which traffic is to be measured. Values 0 through 15 are defined. Values 16-255 are reserved. .”

::= { dot11TransmitQoSMetricsReportEntry 8 }

dot11TransmitQoSMetricsRprtAverageQueueDelay OBJECT-TYPE

SYNTAX Integer32

MAX-ACCESS read-only

UNITS “TUs”

STATUS current

DESCRIPTION

"This attribute holds the average delay of the frames (MSDUs) that are passed to the MAC during the measurement duration for the specified destination and the specified Traffic Identifier. Queue Delay shall be measured from the time the MSDU is passed to the MAC until the transmission starts and shall be expressed in TUs."

::= { dot11TransmitQoSMetricsReportEntry 9 }

dot11TransmitQoSMetricsRprtAverageTransmitDelay OBJECT-TYPE

SYNTAX Integer32

MAX-ACCESS read-only

UNITS “TUs”

STATUS current

DESCRIPTION

"This attribute holds the average delay of the frames (MSDUs) that are successfully transmitted during the measurement duration for the specified destination and the specified Traffic Identifier. Delay shall be measured from the time the MSDU is passed to the MAC until ACK is received from the intermediate destination."

::= { dot11TransmitQoSMetricsReportEntry 10}

dot11TransmitQoSMetricsRprtBin0Range OBJECT-TYPE

SYNTAX Integer

MAX-ACCESS read-only

STATUS current

DESCRIPTION

“Contains the delay range for Bin 0 of the delay histogram, expressed in TU.”

::= { dot11TransmitQoSMetricsReportEntry 11 }

dot11TransmitQoSMetricsRprtTransmittedMSDUCount

SYNTAX Integer32

MAX-ACCESS read-only

STATUS current

DESCRIPTION

“Contains the number of MSDUs to the peer QSTA for the TC, or TS given by the Traffic Identifier successfully transmitted in the measurement duration”

::= {dot11TransmitQoSMetricsReportEntry 12}

dot11TransmitQoSMetricsRprtMSDUDiscardedCount

SYNTAX Integer32

MAX-ACCESS read-only

STATUS current

DESCRIPTION

“Contains the number of MSDUs to the peer QSTA for the TC, or TS given by the Traffic Identifier discarded due either to the number of transmit attempts exceeding dot11ShortRetryLimit or dot11LongRetryLimit as appropriate, or due to the MSDU lifetime having been reached”

::= {dot11TransmitQoSMetricsReportEntry 13}

dot11TransmitQoSMetricsRptMSDUFailedCount

SYNTAX Integer32

MAX-ACCESS read-only

STATUS current

DESCRIPTION

“Contains the number of MSDUs to the peer QSTA for the TC, or TS given by the Traffic Identifier discarded during the measurement duration due to the number of transmit attempts exceeding dot11ShortRetryLimit or dot11LongRetryLimit as appropriate.”

::= {dot11TransmitQoSMetricsReportEntry 14}

dot11TransmitQoSMetricsRptMultipleRetryCount

SYNTAX Integer32

MAX-ACCESS read-only

STATUS current

DESCRIPTION

“Contains the number of MSDUs for the TC, or TS given by the Traffic Identifier that are successfully transmitted after more than one retransmission attempt.”

::= {dot11TransmitQoSMetricsReportEntry 15}

dot11TransmitQoSMetricsRptCFPollsLostCount

SYNTAX Integer32

MAX-ACCESS read-only

STATUS current

DESCRIPTION

“Contains the number of QoS (+)CF-Poll frames transmitted to the peer QSTA where there was no response from the QSTA. ”

::= {dot11TransmitQoSMetricsReportEntry 15}

dot11TransmitQoSMetricsRprtDelayHistogram OBJECT-TYPE

SYNTAX OCTET STRING (SIZE 6)

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"This attribute holds the histogram of delay of the frames (MSDUs) that are successfully transmitted during the measurement duration for the specified Traffic Identifier and the specified destination. Delay shall be measured from the time the MSDU is passed to the MAC until the ACK is received from the intermediate destination and shall be expressed in TUs. "

::= { dot11TransmitQoSMetricsReportEntry 16 }

-- ********************************************************************

-- * End of dot11TransmitQoSMetricsReport	TABLE

-- ********************************************************************

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This submission contains a proposal to add additional QoS metrics to the latest TGk draft. This proposal defines a new measurement type: Transmit QoS Metrics providing measurements for each traffic category or traffic stream per destination. Each traffic category/stream can be identified by a Traffic Identifier.  The Transmit QoS Metrics includes a number of counters, average queue delay, average transmit delay, and a delay histogram. This contribution provides resolution for LB73 comment#121, 138, 157, 258, 293, 466, 467, 493, 691, 692, 1121, 1140 and 1214.