IEEE P802.11
Wireless LANs

| Normative Text Changes for TSF Drift Rate |
| --- |
| Date: 2006-MAR-06 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Joe Kwak | InterDigital Communications | 482 Degas Bolingbrook, IL 60440 | 630-739-4159 | joekwak@sbcglobal.net |

Abstract

This document contains normative text changes to TGk draft to incorporate improved TSF Information to include a TSF drift rate measurement.   This extends the useful lifetime of the reported TSF information from several seconds to tens of minutes.

This contribution addresses  LB78 comment 1514

Changes are shown with respect to TGk draft D3.2.

.

Modify clauses of TGk draft D3.2 as indicated below in red and blue highlights:

#### 7.3.2.27 Neighbor Report element

The format of the Neighbor Report element is shown in Figure k61.

|  |  |  | Zero or more, one for each neighbor |  |
| --- | --- | --- | --- | --- |
|  | Element ID | Length | Neighbor List |  |
| Octets: | 1 | 1 | Variable |  |

Figure k61—Neighbor Report element format

The Element ID field is equal to the Neighbor Report value in Table 20.

The value of Length field is dependent on the number of Neighbor List Entries representing the neighboring APs being reported. Each entry describes an AP and consists of BSSID, BSSID Information, Channel Number, Regulatory Class, PHY Options, and optionally may include the TSF offset fields. The minimum value of the Length field is 0 (i.e., with no neighbor APs in the Neighbor Report element).

The Neighbor List comprises of zero or more Neighbor List Entries. See Figure k63.

|  | BSSID | BSSID information | Channel Number | Regulatory Class | PHY Options | TSF offset (optional) |
| --- | --- | --- | --- | --- | --- | --- |
| Octets: | 6 | 2 | 1 | 1 | 1 | 4 |

Figure k63—Neighbor list entry format

The BSSID is the BSSID of the BSS being reported. The subsequent fields in the Neighbor List Entry pertain to this BSS.

The BSSID Information field may be used to help determine neighbor BSS transition candidates. It shall be two octets in length and shall contain the subfields as shown in Figure k65.

|  | B0 | B1 | B2 | B3 | B4 | B9 | B10 | B15 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | AP Reachability | Security | Key Scope | Capabilities | Reserved |
| Bits: | 2 | 1 | 1 | 6 | 6 |

Figure k65—BSSID information field

The AP Reachability field indicates whether the AP identified by this BSSID is reachable by the STA that requested the Neighbor Report for the exchange of preauthentication frames as described in clause 8.4.6.1. The values are shown in Table k19.

Table k19—Reachability field

| Value | Reachability | Usage |
| --- | --- | --- |
| 0 | Reserved | n/a |
| 1 | Not Reachable | A station sending a preauthentication frame to the BSSID will not receive a response even if the AP represented by the BSSID is capable of preauthentication. |
| 2 | Unknown | The AP is unable to determine if the value Reachable or Not Reachable is to be returned. |
| 3 | Reachable | The station sending a preauthentication frame to the BSSID can receive a response from an AP that is capable of preauthentication. |

The Security bit, if set, indicates that the AP identified by this BSSID advertises all of the security capabilities of the AP with which the STA is currently associated. If the bit is not set, it indicates that either the capabilities do not match or the information is not available to the AP at this time.

The Key Scope bit, when set, indicates the AP represented by this BSSID has the same authenticator as the AP sending the report. If this bit is not set, it indicates a distinct authenticator or the information is not available.

The Capabilities Subfield contains selected capability information for the AP represented by this BSSID. The bit fields within this subfield shall have the same meaning and be set equal to the equivalent bits within the Capability Information field being sent in the beacons by the AP being reported. The format of the Capabilities subfield is as in Figure k67.

|  | B4 | B5 | B6 | B7 | B8 | B9 |
| --- | --- | --- | --- | --- | --- | --- |
|  | Spectrum Management | QoS | APSD | Radio Mesaurement | Delayed Block Ack | Immediate Block Ack |
| Bits: | 1 | 1 | 1 | 1 | 1 | 1 |

Figure k67—Capabilities Subfield

Bits 10 – 15 are reserved and shall be set to 0 on transmission and ignored on reception.

Channel Number indicates the current operating channel of the AP represented by the BSSID in this neighbor list entry.

Regulatory Class contains an enumerated value from Annex J specifying the frequency band in which the Current Channel is valid.

The PHY Options field contains the Condensed PHY type and TSF offset Flag as shown in the Figure k69.

|  | B0 B6 | B7 |
| --- | --- | --- |
|  | Condensed PHY Type | TSF offset Flag |
| Bits: | 7 | 1 |

Figure k69—PHY Options field

Condensed PHY Type indicates the PHY type of the AP being reported. It shall have an integer value between 0 and 127 as defined by dot11PHYType.

TSF offset Flag is a one bit field. When it is set to 1 it indicates that a TSF offset field is present for this Neighbor List Entry. When set to 0 it indicates that a TSF offset field is not present for this Neighbor List Entry. The Neighbor Report may have the TSF offset Flag set in some Neighbor List Entries and not set in others.

The TSF offset is 4 octets long and contains TSF Offset and Beacon Interval subfields.

|  | TSF Offset | Beacon Interval | TSF Drift Rate |
| --- | --- | --- | --- |
| Octets: | 2 | 2 | 1 |

Figure k71—TSF offset field format

The TSF Offset subfield is 2 octets long and contains the neighbor AP’s TSF timer offset. This is the time difference, in TU units, between the serving AP and a neighbor AP. This offset is given modulo the neighbor AP’s Beacon Interval and rounded to the nearest TU boundary.

The Beacon Interval field is the beacon interval of the Neighbor AP being reported. This field is defined in clause 7.3.1.3 and illustrated in Figure 26.

The TSF Drift Rate subfield contains the drift rate value of the measured drift rate between the serving AP's TSF timer clock and the neighbor AP's TSF timer clock as defined in Table kx.  Valid TSF drift rate values range from 0 to 16.  TSF drift rate value of 0 is used to indicate that  measured TSF drift rate is unavailable or unknown.

Table kx—TSF Drift Rate Value

| TSF Drift Rate Value | Measured TSF Drift Rate Range | Max TSF Offset drift (in 20.5 seconds) |
| --- | --- | --- |
| 0 | TSF drift rate not available | unknown |
| 1 | -50 ppm < TSF drift rate < -43 ppm | -1 TU |
| 2 | -43 ppm < TSF drift rate < -36 ppm | -0.86 TU |
| 3 | -36 ppm < TSF drift rate < -29 ppm | -0.72 TU |
| 4 | -29 ppm < TSF drift rate < -22 ppm | -0.58 TU |
| 5 | -22 ppm < TSF drift rate < -15 ppm | -0.44 TU |
| 6 | -15 ppm < TSF drift rate < -8 ppm | -0.30 TU |
| 7 | -8 ppm < TSF drift rate < -4 ppm | -0.16 TU |
| 8 | -4ppm < TSF drift rate < 0 ppm | -0.08 TU |
| 9 | 0 < TSF drift rate < +4 ppm | +0.08 TU |
| 10 | +4 ppm < TSF drift rate < +8 ppm | +0.16 TU |
| 11 | +8 ppm < TSF drift rate < +15 ppm | +0.30 TU |
| 12 | +15 ppm < TSF drift rate < +22 ppm | +0.44 TU |
| 13 | +22 ppm < TSF drift rate < +29 ppm | +0.58 TU |
| 14 | +29 ppm < TSF drift rate < +36 ppm | +0.72 TU |
| 15 | +36 ppm < TSF drift rate < +43 ppm | +0.86 TU |
| 16 | +43 ppm < TSF drift rate < +50 ppm | +1 TU |
| 17-255 | reserved |  |

### 11.12.3 Receiving a Neighbor Report

An AP receiving a Neighbor Report Request shall respond with a Neighbor Report Response frame containing zero or more Neighbor Report elements. If SSID elements are specified in the corresponding Neighbor Report Request frame, the Neighbor Report element shall only contain information from the MIB table dot11RRMNeighborReportTable concerning neighbor APs that are members of the current ESS or ESSs identified by the SSID elements contained within the Neighbor Report Request. If the SSID element is omitted the Neighbor Report element shall contain information from the MIB table dot11RRMNeighborReportTable concerning neighbor APs that belong to the same ESS as the requesting STA. If there are no list entries available the AP shall send a Neighbor Report Response with no Neighbor List Entries.

A serving AP shall include a TSF Offset field in the Neighbor List Entry only if it is able to guarantee an accumulated error of ±1.5 TU or better on the TSF Offset subfield. If available, the serving AP shall include the TSF drift rate for the target AP in the Neighbor Report Entry. The TSF drift rate for the target AP is the difference in the TSF timer clock frequencies between the serving and tartget AP divided by the serving AP's TSF timer clock frequency.  If a measured target AP TSF drift rate is not available, the serving AP shall report a TSF drift rate value of 0.

NOTE—The error budget (±1.5 TU) can be broken down as follows:

Error caused by rounding to the nearest TU boundary when converting Neighbor TSF Offset from microseconds to TUs (±0.5 TU).

TSF timer clock drift error due to clock frequency difference between the serving AP and target AP TSF timer clocks.  The ratio of the frequency difference over the frequency is the clock drift rate. The TSF timer clock drift error is a product of the TSF timer clock drift rate and the elapsed time since the reported TSF Offset was measured ((±1 TU).

# Annex D

-- ********************************************************************

-- * dot11RRMNeighborReport TABLE

-- ********************************************************************

dot11RRMNeighborReportNextIndex OBJECT-TYPE

SYNTAX INTEGER(0..255)

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"Identifies the next available index for managing the Neighbor Report table.

If this attribute is 0, it indicates that the Neighbor Report feature is not

configurable via SNMP, or the table is full and new rows cannot be

accepted."

::= { dot11RRMConfig 2 }

dot11RRMNeighborReportTable OBJECT-TYPE

SYNTAX SEQUENCE OF Dot11RRMNeighborReportEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"Group contains pertinent information on a collection of BSSID’s that are

candidates to which STA’s can roam. The rows are created using createAndWait

method and fill in the attributes. When the rowStatus is set to active, the

row can be included in Neighbor Report IEs. If there is an error, the

rowStatus shall be set to notReady by SME. Since this table contains all

Neighbor Report IE entries for all interfaces enabled with the Neighbor

Report feature, it is possible to have too many entries for one interface,

while still remaining under the MaxTableSize. In that situation, SME shall

only include Neighbor Report entries with lower

dot11RRMNeighborReportIFIndex up to the maximum possible number of entries

for a particular interface identified by ifIndex.

SME shall set the rowStatus to notInService for those rows that cannot be

included in the Neighbor Report element for that interface."

::= { dot11RRMConfig 3 }

dot11RRMNeighborReportEntry OBJECT-TYPE

SYNTAX Dot11RRMNeighborReportEntry

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"An entry in the dot11RRMNeighborReportTable"

INDEX { dot11RRMNeighborReportIndex }

::= { dot11RRMNeighborReportTable 1 }

Dot11RRMNeighborReportEntry ::=

SEQUENCE {

dot11RRMNeighborReportIndex Unsigned32,

dot11RRMNeighborReportIfIndex InterfaceIndex,

dot11RRMNeighborReportBSSID MacAddress,

dot11RRMNeighborReportReachability INTEGER,

dot11RRMNeighborReportSecurity TruthValue,

dot11RRMNeighborReportCapSpectrumMgmt TruthValue,

dot11RRMNeighborReportCapQoS TruthValue,

dot11RRMNeighborReportCapAPSD TruthValue,

dot11RRMNeighborReportCapRRM TruthValue,

dot11RRMNeighborReportCapBlockAck TruthValue,

dot11RRMNeighborReportKeyScope TruthValue,

dot11RRMNeighborReportChannelNumber INTEGER,

dot11RRMNeighborReportRegulatoryClass INTEGER,

dot11RRMNeighborReportPhyOptions	INTEGER,

dot11RRMNeighborReportNeighborTSFInfo Unsigned32,

dot11RRMNeighborReportTSFOffsetFlag TruthValue,

dot11RRMNeighborReportBeaconInterval Unsigned32,

dot11RRMNeighborReportRowStatus RowStatus,

dot11RRMNeighborReportMeasurementMode INTEGER,

dot11RRMNeighborReportTSFDriftRate INTEGER }

dot11RRMNeighborReportIndex OBJECT-TYPE

SYNTAX Unsigned32

MAX-ACCESS not-accessible

STATUS current

DESCRIPTION

"Index for Neighbor Report configuration table in

dot11RRMNeighborReportTable, greater than 0."

::= { dot11RRMNeighborReportEntry 1 }

dot11RRMNeighborReportIfIndex OBJECT-TYPE

SYNTAX InterfaceIndex

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"The ifIndex for this row of Neighbor Report entry belongs to."

::= { dot11RRMNeighborReportEntry 2 }

dot11RRMNeighborReportBSSID OBJECT-TYPE

SYNTAX MacAddress

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"The BSSID of the STA to which this row of Neighbor Report applies."

::= { dot11RRMNeighborReportEntry 3 }

dot11RRMNeighborReportReachability OBJECT-TYPE

SYNTAX INTEGER {

notReachable(1),

unknown(2),

reachable(3)

}

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"Indicates the reachability of the AP represented by

the dot11NeighborReportBSSID."

::= { dot11RRMNeighborReportEntry 4 }

dot11RRMNeighborReportSecurity OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"Indicates the RSN capability of the AP

represented by dot11NeighborReportBSSID"

::= { dot11RRMNeighborReportEntry 5 }

dot11RRMNeighborReportCapSpectrumMgmt OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"Indicates the spectrum management capability of the AP

represented by dot11NeighborReportBSSID"

::= { dot11RRMNeighborReportEntry 6 }

dot11RRMNeighborReportCapQoS OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"Indicates the QoS capability of the AP represented by

dot11NeighborReportBSSID"

::= { dot11RRMNeighborReportEntry 7 }

dot11RRMNeighborReportCapAPSD OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"Indicates the APSD capability of the AP represented by

dot11NeighborReportBSSID"

::= { dot11RRMNeighborReportEntry 8 }

dot11RRMNeighborReportCapRRM OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"Indicates the RRM capability of the AP represented by

dot11NeighborReportBSSID"

::= { dot11RRMNeighborReportEntry 9 }

dot11RRMNeighborReportCapBlockAck OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"Indicates the BlockAck capability of the AP represented

by dot11NeighborReportBSSID"

::= { dot11RRMNeighborReportEntry 10 }

dot11RRMNeighborReportKeyScope OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"Indicates a shared authenticator identity for the AP represented by dot11NeighborReportBSSID"

::= { dot11RRMNeighborReportEntry 11 }

dot11RRMNeighborReportChannelNumber OBJECT-TYPE

SYNTAX INTEGER (1..255)

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"This is the current operating channel of the STA returning the report"

::= { dot11RRMNeighborReportEntry 12 }

dot11RRMNeighborReportRegulatoryClass OBJECT-TYPE

SYNTAX PHYType

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"This corresponds to the frequency band for the channel list being

reported."

REFERENCE

"IEEE 802.11, Annex J"

::= { dot11RRMNeighborReportEntry 13 }

dot11RRMNeighborReportPhyOptions OBJECT-TYPE

SYNTAX INTEGER

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"The PHY Options of the Neighbor AP Entry."

::= { dot11RRMNeighborReportEntry 14 }

dot11RRMNeighborReportNeighborTSFInfo OBJECT-TYPE

SYNTAX Unsigned32

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"The Neighbor TBTT Offset field is as defined in clause 7.3.2.26."

::= { dot11RRMNeighborReportEntry 15 }

dot11RRMNeighborReportTSFOffsetFlag OBJECT-TYPE

SYNTAX TruthValue

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"Indicates the TSFOffset is included in the Neighbor Report entry.”

::= { dot11RRMNeighborReportEntry 16 }

dot11RRMNeighborReportBeaconInterval OBJECT-TYPE

SYNTAX Unsigned32

UNITS "TUs"

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"The Beacon Interval field is as defined in clause 7.3.2.27."

::= { dot11RRMNeighborReportEntry 17 }

dot11RRMNeighborReportRowStatus OBJECT-TYPE

SYNTAX RowStatus

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"Contains the row status of the Neighbor Report, essentially used for

indicating whether the row has all valid attributes filled in. Then set to

active to be used in Neighbor Report information elements. If any parameter

is invalid, the SME shall set this attribute back to notReady. It is the

responsibility of the manager to correct the parameters."

::= { dot11RRMNeighborReportEntry 18 }

dot11RRMNeighborReporMeasurementMode OBJECT-TYPE

SYNTAX INTEGER {

lateBit(0),

incapableBit(1),

refusedBit(2),

}

MAX-ACCESS read-only

STATUS current

DESCRIPTION

"MeasurementMode corresponds to the Measurement Report Mode field in

the Measurement Report Element and is used to indicate the reason for

a failed measurement request. 0 indicates the STA is unable to carry

out a measurement request because it received the request after the

requested measurement time. 1 indicates this STA is incapable of

generating the report. 3 indicates his STA is refusing to generate

the report."

DEFVAL { 0 }

::= { dot11RRMNeighborReportEntry 19 }

dot11RRMNeighborTSFDriftRate OBJECT-TYPE

SYNTAX INTEGER

UNITS "TUs"

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"The TSF Drift Rate subfield contains the drift rate value of the measured drift rate between the serving AP's TSF timer clock and the neighbor AP's TSF timer clock as defined in Table kx.  Valid TSF drift rate values range from 0 to 16.  TSF drift rate value of 0 is used to indicate that  measured TSF drift rate is unavailable or unknown."

::= { dot11RRMNeighborReportEntry 20 }

-- ********************************************************************

-- * End of dot11RRMNeighborReport TABLE

-- ********************************************************************