IEEE P802.11
Wireless LANs

| LB84 Comment Submission CID #8221: Analysis of the 802.11n channel Interleaver latency penalty when used with the 802.11n LDPC codes |
| --- |
| Date: 2006-07-05 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Devis Gatti | STMicroelectronics, N.V. | Centro Direzionale Colleoni; Palazzo "La Dialettica"; 20041 Agrate Brianza, Milano; Italy | +39.039.603.7236 | Devis.Gatti@st.com |
| George Vlantis | STMicroelectronics, Inc. | 1060 East Brokaw Road; San Jose, CA 95131 | +1.408.451.8109 | George.Vlantis@st.com |

# Latency assumptions:

Let’s consider the following simplified latency assumptions:

- time for decoding (i.e. deinterleaving & channel decoding):      6.0us.

- Interleaver processing: 						            1.0us

- 1 iteration of Layered Belief Propagation (LBP):          		  0.5us

Thus, in order to cope with the latency assumptions we target 12 LBP iterations without the channel interleaver versus 10 LBP iterations with the channel interleaver.

Because one iteration of LBP performs as two iterations of standard Belief Propagation (BP) we run simulations with 24 and 20 BP iterations without and with channel interleaver, respectively.

# Simulation Details

According to the LDPCC PPDU encoding procedures, codewords of 648 and 1944 bits length has be selected depending on the packet length. For each mode, two different packet sizes have been simulated (the shortest and the longest codeword cases). Packet sizes have been selected in order to minimize the amount of shortening, puncturing and repetition. Packet length selection is reported in Table 1.

# Simulation Conditions:

- perfect synchronization and CSI

- no impairments

- IEEE 802.11n channel model: Channel D, 2x2, element spacing 0.5 ;

- MMSE detection;

- 20  LDPCC iterations of BP with 802.11n Interleaver

- 24  LDPCC iterations of BP withouth 802.11n Interleaver

- 100 erroneous packets per SNR

Tble 1

| Simulation Table |
| --- |
| Simulation Number | MCS | FEC | Packet Length [Bytes] |
| 1 | 8 | LDPCC 648 | 37 |
| 2 | 8 | LDPCC 1944 | 970 |
| 3 | 9 | LDPCC 648 | 37 |
| 4 | 9 | LDPCC 1944 | 970 |
| 5 | 10 | LDPCC 648 | 56 |
| 6 | 10 | LDPCC 1944 | 909 |
| 7 | 11 | LDPCC 648 | 24 |
| 8 | 11 | LDPCC 1944 | 970 |
| 9 | 12 | LDPCC 648 | 37 |
| 10 | 12 | LDPCC 1944 | 909 |
| 11 | 13 | LDPCC 648 | 50 |
| 12 | 13 | LDPCC 1944 | 970 |
| 13 | 14 | LDPCC 648 | 56 |
| 14 | 14 | LDPCC 1944 | 909 |
| 15 | 15 | LDPCC 648 | 63 |
| 16 | 15 | LDPCC 1944 | 1010 |

## Simulation Results

# Conclusion

Simulation results show that only in the cases with MCS 13 and 14 and for short packet sizes does the use of the channel interleaver combined with 20 LDPCC iterations gives performance results slightly better than 24 LDPCC iterations without the channel interleaver. In all the other cases, it is shown that is more beneficial to use the time required for deinterleaving to perform additional LDPCC decoder iterations. Thus we propose to remove the channel interleaver from the IEEE 802.11n Draft.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document presents an analysis of the 802.11n interleaver, when used in conjunction with the LDPC codes, in terms of the trade-off between performance and latency requirements for the decoder.  The analysis is carried out comparing LDPCC simulation results with and without the channel interleaver.  IEEE Channel Model D, MCS’s 8 - 15 and Nss=2 spatial streams in 20MHz Bandwidth have been considered in a 2x2 configuration. The time budget for the decoding process is assumed to be fixed.  The latency penalty of the interleaver and its subsequent reduction in decoder iterations in the same time budget is contrasted with the interleaver’s performance benefits.  Based on these simulation results, we have shown that the presence of the channel interleaver, at best, doesn’t introduce a significant advantage.