IEEE P802.11
Wireless LANs

| Proposal for resolution of editor’s comments for P802.11.2-D0.8 |
| --- |
| Date: 2006-07-10 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Neeraj K. Sharma | Intel | 2111 NE 25th Avenue, Hillsboro, OR 97124 | 503-712-7458 | neeraj.k.sharma@intel.com |
| Uriel Lemberger | Intel | PO Box 1659, Matam Industrial Park, Haifa 31015 Israel | +972-4-865-5701 | uriel.lemberger@intel.com |
| Alexander Tolpin | Intel | PO Box 1659, Matam Industrial Park, Haifa 31015 Israel | +972-4-865-5430 | alexander.tolpin@intel.com |
| Guy Halperin | Intel | PO Box 1659, Matam Industrial Park, Haifa 31015 Israel | +972-4-465-4321 | guy.halperin@intel.com |

# Comment from P802.11.2 Draft Status – May 2006

“Subclauses 5.5 (OTA Indoor NLOS test environment) and 5.6 (OTA Indoor LOS test environment) have only minor differences. Consider consolidating to simplify draft.” [2]

# Resolution of Comment

Current Section 5.6.2.2 Test setup (page 36):

“The general setup comprises the DUT and the WLCP. The typical setup is very similar to an OTA outdoor LOS environment, as already depicted In Figure 3 of 5.4.

The WLCP is placed on a test stand…….”

Section 5.6.2.2 Test setup should be replaced by:

“The setup is the same as OTA outdoor LOS environment, as already depicted in Figure 3 of 5.4.”

Current Section 5.6.2.3 Test parameters (page 36):

“Table 5 describes the test parameters relevant to this environment, as well as the corresponding requirements for their values.”

“Figure reference within the table….”

Section 5.6.2.3 Test setup should be replaced by:

“The test parameters for this setup are the same as OTA indoor NLOS environment, as already depicted in Table 3 of 5.5 with the following change to item 6 as shown in Table 5.”

Replace entire contents of Table 5-Indoor LOS test parameters with the following contents with no changes to Figure 11.

Table 5-Indoor LOS test parameters

| Item | Test Parameter | Requirement | Applicable figure |
| --- | --- | --- | --- |
| 6 | Location of DUT and WLCP | The DUT should be placed at maximal distance of 70 meters from the WLCP, with the test area marked at x meter increments. This requirement is intended to enable throughput measurements to be easily made at repeatable locations. | Figure 11 |

# References

- P802.11.2-D0.8. Draft Recommended Practice for the Evaluation of 802.11 Wireless Performance.

- IEEE 802.11-06-0726r0. Draft Status – May 2006.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document contains the proposal for resolution of editor’s comments to draft P802.11.2-D0.8. The comments referenced to are listed in the document IEEE 802.11-06-0726r0.