IEEE P802.11
Wireless LANs

| Alternatives for Possible Restructuring of the HT Action Frames |
| --- |
| Date: 2006-07-13 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Adrian Stephens | Intel Corporation | 15 JJ Thompson Avenue, Cambridge, CB3 0FD, United Kingdom |  | adrian.p.stephens@intel.com |

# “As it currently is (In D1.01) Format”:

# Insert the following new subclause:

      - MIMO Compressed Steering

The MIMO Compressed Steering management action frame is of category HT. The format of its frame body is defined in Table n2

EDITORIAL NOTE—Insert the Category code for HT obtained from the 802.11 ANA in the table below.

- MIMO Compressed Steering

| Order | Information | Name | Size | Value |
| --- | --- | --- | --- | --- |
| 1 | Category | HT | 1 | <ANA> |
| 2 | Action | MIMO Compressed Steering | 1 | 8 |
| 3 | CSI Matrices Control | CSI Matrices Control | 2 | See text. |
| 4 | MCMR Segment Sequence | MCMR Segment Sequence | 1 | Reserved |
| 5 | Receiver SNR | RX SNR | 1 | Average Signal to Noise Ratio in the STA sending the report. |
| 6 | Explicit Feedback Sequence | Explicit Feedback Sequence | 1 | See text |
| 7 | Quantized Steering Matri ces Feedback Information | Quantized Steering Matrices Feedback Information | Vari able | See text |

The size of the Quantized Steering Matrices Feedback Information field depends on the values in the format field in the CSI Matrices control field.

The CSI Matrices Control field is defined in Figure nxx and used as defined in Table nxx.

- Use of CSI Matrices Control fields (MIMO Compressed Steering)

| Field | Description |
| --- | --- |
| Nc | Number of columns in the steering matrix V |
| Nr | Number of rows in the steering matrix V |
| Explicit Channel Feedback Format | See Table n (Explicit Feedback Format field (MIMO Compressed Steering)) |

In a MIMO Compressed Steering frame, the Explicit Feedback Format field is defined in Table n (Explicit Feedback Format field (MIMO Compressed Steering)).

- Explicit Feedback Format field (MIMO Compressed Steering)

| Field | Length | Values | Meaning |
| --- | --- | --- | --- |
| Grouping (Ng) | 2 bits | 00 | Ng=1 (No Grouping) |
|  |  | 01 | Ng=2 |
|  |  | 10 | Ng=4 |
|  |  | 11 | Reserved |
| Codebook information | 2 bits | 00 | 1 bit for , 3 bits for  |
|  |  | 01 | 2 bits for , 4 bits for  |
|  |  | 10 | 3 bits for , 5 bits for  |
|  |  | 11 | 4 bits for , 6 bits for  |

Each compressed steering matrix feedback has a unique sequence number encoded in the Explicit Feedback Sequence field. This is incremented between measurements.

The Quantized Steering Matrices Feedback Information field contains channel matrix elements indexed in order of data subcarrier index and angle. This simplifies the interpolation angles between subcarriers, if grouping other than 1 is employed. The explanation on how these angles are generated from the steering matrix V is given in  (Error! Reference source not found.).

The angles are sent in order given in Table n (Order of angles in the Quantized Steering Matrices Feedback Information field).

- Order of angles in the Quantized Steering Matrices Feedback Information field

| V(f) | Number of angles | The order of angles in the Quantized Steering Matrices Feedback Information field |
| --- | --- | --- |
| 2x1 | 2 | f11, y21 |
| 2x2 | 2 | f11, y21 |
| 3x1 | 4 | f11, f21, y21, y31, |
| 3x2 | 6 | f11, f21, y21, y31, f22, y32 |
| 3x3 | 6 | f11, f21, y21, y31, f22, y32 |
| 4x1 | 6 | f11, f21, f31, y21, y31, y41 |
| 4x2 | 10 | f11, f21, f31, y21, y31, y41, f22, f32, y32, y42 |
| 4x3 | 12 | f11, f21, f31, y21, y31, y41, f22, f32, y32, y42, f33, y43 |
| 4x4 | 12 | f11, f21, f31, y21, y31, y41, f22, f32, y32, y42, f33, y43 |

The angles are quantized according to the following formulae:

where

and

where

is the number of bits used to quantize and

is the number of bits used to quantize (See Explicit Feedback Format field (MIMO Compressed Steering)47).

All angles are transmitted LSB to MSB.

Subcarriers are sent in order according to the following sequence. For 20 MHz bandwidth operation:

For 40 MHz bandwidth operation:

For example, 40 MHz operation with Ng=2 would have subcarriers in the following order:

[-58,-56….-4,-2,2,4…….56,58].

Example: 2x2, 20 MHz, no grouping, bits for each  = 3, bits for each =5. Each ij over all tone indices has 168 bits. Each ij over all tone indices has 280 bits.

| Bits | b1 to b5 | b6 to b10 | … | b276 to b280 | b281 to b283 | b284 to b286 | … | b446 to b448 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| data | 11(f-28) | 11(f-27) | … | 11(f28) | 21(f-28) | 21(f-27) | … | 21(f28) |

Example: 4x2, 40 MHz, 4 tone grouping, ,  = 4. Each ij over all tone indices has 120 bits. Each ij over all tone indices has 60 bits.

| Bits | b1 to b4 | b5 to b8 | … | b117 to b120 | b121 to b124 | … | b361 to b362 | … | b661 to b664 | … | b899 to b900 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| data | 11(f-58) | 11(f-54) | … | 11(f58) | 21(f-58) | … | 21(f-58) | … | 32(f-58) | … | 42(f58) |

# “Table format, plus fields in the right places” (In D1.01):

(The issue here is that the fields named in the action table have to be defined in the appropriate place.  Each such named field or element requires its own subclause)

# Insert the following new subclause:

- MIMO Compressed Steering

The MIMO Compressed Steering management action frame is of category HT. The format of its frame body is defined in Table n (MIMO Compressed Steering).

# The Category code is set to 1 (representing HT)

# The Action code is set to 42 (represening fish).

# The CSI Matrices Control field is defined 7.1.2.3.4

(Etc... with the other fields)

- MIMO Compressed Steering

| Order | Information | Name | Size | Value |
| --- | --- | --- | --- | --- |
| 1 | Category | HT | 1 | <ANA> |
| 2 | Action | MIMO Compressed Steering | 1 | 8 |
| 3 | CSI Matrices Control | CSI Matrices Control | 2 | See text. |
| 4 | MCMR Segment Sequence | MCMR Segment Sequence | 1 | Reserved |
| 5 | Receiver SNR | RX SNR | 1 | Average Signal to Noise Ratio in the STA sending the report. |
| 6 | Explicit Feedback Sequence | Explicit Feedback Sequence | 1 | See text |
| 7 | Quantized Steering Matri ces Feedback Information | Quantized Steering Matrices Feedback Information | Vari able | See text |

      - The Quantized Steering Matrices Feedback field

The size of the Quantized Steering Matrices Feedback Information field depends on the values in the format field in the CSI Matrices control field.

      - The CSI Matrices Control field

The CSI Matrices Control field is defined in Figure n (Error! Reference source not found.) and used as defined in

- Use of CSI Matrices Control fields (MIMO Compressed Steering)

| Field | Description |
| --- | --- |
| Nc | Number of columns in the steering matrix V |
| Nr | Number of rows in the steering matrix V |
| Explicit Channel Feedback Format | See Table n (Explicit Feedback Format field (MIMO Compressed Steering)) |

      - Explicit Feedback Format field

In a MIMO Compressed Steering frame, the Explicit Feedback Format field is defined in Table n (Explicit Feedback Format field (MIMO Compressed Steering)).

- Explicit Feedback Format field (MIMO Compressed Steering)

| Field | Length | Values | Meaning |
| --- | --- | --- | --- |
| Grouping (Ng) | 2 bits | 00 | Ng=1 (No Grouping) |
|  |  | 01 | Ng=2 |
|  |  | 10 | Ng=4 |
|  |  | 11 | Reserved |
| Codebook information | 2 bits | 00 | 1 bit for , 3 bits for  |
|  |  | 01 | 2 bits for , 4 bits for  |
|  |  | 10 | 3 bits for , 5 bits for  |
|  |  | 11 | 4 bits for , 6 bits for  |

Each compressed steering matrix feedback has a unique sequence number encoded in the Explicit Feedback Sequence field. This is incremented between measurements.

      - The Quantized Steering Matrices Feedback Information field

The Quantized Steering Matrices Feedback Information field contains channel matrix elements indexed in order of data subcarrier index and angle. This simplifies the interpolation angles between subcarriers, if grouping other than 1 is employed. The explanation on how these angles are generated from the steering matrix V is given in  (Error! Reference source not found.).

The angles are sent in order given in Table n (Order of angles in the Quantized Steering Matrices Feedback Information field).

- Order of angles in the Quantized Steering Matrices Feedback Information field

| V(f) | Number of angles | The order of angles in the Quantized Steering Matrices Feedback Information field |
| --- | --- | --- |
| 2x1 | 2 | f11, y21 |
| 2x2 | 2 | f11, y21 |
| 3x1 | 4 | f11, f21, y21, y31, |
| 3x2 | 6 | f11, f21, y21, y31, f22, y32 |
| 3x3 | 6 | f11, f21, y21, y31, f22, y32 |
| 4x1 | 6 | f11, f21, f31, y21, y31, y41 |
| 4x2 | 10 | f11, f21, f31, y21, y31, y41, f22, f32, y32, y42 |
| 4x3 | 12 | f11, f21, f31, y21, y31, y41, f22, f32, y32, y42, f33, y43 |
| 4x4 | 12 | f11, f21, f31, y21, y31, y41, f22, f32, y32, y42, f33, y43 |

The angles are quantized according to the following formulae:

where

and

where

is the number of bits used to quantize and

is the number of bits used to quantize (See Explicit Feedback Format field (MIMO Compressed Steering)47).

All angles are transmitted LSB to MSB.

Subcarriers are sent in order according to the following sequence. For 20 MHz bandwidth operation:

For 40 MHz bandwidth operation:

For example, 40 MHz operation with Ng=2 would have subcarriers in the following order:

[-58,-56….-4,-2,2,4…….56,58].

Example: 2x2, 20 MHz, no grouping, bits for each  = 3, bits for each =5. Each ij over all tone indices has 168 bits. Each ij over all tone indices has 280 bits.

| Bits | b1 to b5 | b6 to b10 | … | b276 to b280 | b281 to b283 | b284 to b286 | … | b446 to b448 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| data | 11(f-28) | 11(f-27) | … | 11(f28) | 21(f-28) | 21(f-27) | … | 21(f28) |

# “Figure format, plus fields in the right places” (In D1.01):

(This is the same as the previous format,  plus conversion of the table to a figure as the commenter requested).

# Insert the following new subclause:

      - MIMO Compressed Steering

The MIMO Compressed Steering management action frame is of category HT. The format of its frame body is defined in Figure n1

# The Category code is set to 1 (representing HT)

# The action code is set to 42 (represening fish).

# The CSI Matrices Control field is defined 7.1.2.3.4 (ETC)

|  | Category | Action | CSI Ma trices Control | MCMR Seg ment Se quence | Receiver SNR | Explicit Feed back Se quence | Quan tized Steering Matrices Feedback Informa tion |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Octets: | 1 | 1 | 2 | 1 | 1 | 1 | variable |

- MIMO Compressed Steering frame body

      - The Quantized Steering Matrices Feedback field

The size of the Quantized Steering Matrices Feedback Information field depends on the values in the format field in the CSI Matrices control field.

      - The CSI Matrices Control field

The CSI Matrices Control field is defined in Figure n (Error! Reference source not found.) and used as defined in

- Use of CSI Matrices Control fields (MIMO Compressed Steering)

| Field | Description |
| --- | --- |
| Nc | Number of columns in the steering matrix V |
| Nr | Number of rows in the steering matrix V |
| Explicit Channel Feedback Format | See Table n (Explicit Feedback Format field (MIMO Compressed Steering)) |

      - Explicit Feedback Format field

In a MIMO Compressed Steering frame, the Explicit Feedback Format field is defined in Table n (Explicit Feedback Format field (MIMO Compressed Steering)).

- Explicit Feedback Format field (MIMO Compressed Steering)

| Field | Length | Values | Meaning |
| --- | --- | --- | --- |
| Grouping (Ng) | 2 bits | 00 | Ng=1 (No Grouping) |
|  |  | 01 | Ng=2 |
|  |  | 10 | Ng=4 |
|  |  | 11 | Reserved |
| Codebook information | 2 bits | 00 | 1 bit for , 3 bits for  |
|  |  | 01 | 2 bits for , 4 bits for  |
|  |  | 10 | 3 bits for , 5 bits for  |
|  |  | 11 | 4 bits for , 6 bits for  |

Each compressed steering matrix feedback has a unique sequence number encoded in the Explicit Feedback Sequence field. This is incremented between measurements.

      - The Quantized Steering Matrices Feedback Information field

The Quantized Steering Matrices Feedback Information field contains channel matrix elements indexed in order of data subcarrier index and angle. This simplifies the interpolation angles between subcarriers, if grouping other than 1 is employed. The explanation on how these angles are generated from the steering matrix V is given in  (Error! Reference source not found.).

The angles are sent in order given in Table n (Order of angles in the Quantized Steering Matrices Feedback Information field).

- Order of angles in the Quantized Steering Matrices Feedback Information field

| V(f) | Number of angles | The order of angles in the Quantized Steering Matrices Feedback Information field |
| --- | --- | --- |
| 2x1 | 2 | f11, y21 |
| 2x2 | 2 | f11, y21 |
| 3x1 | 4 | f11, f21, y21, y31, |
| 3x2 | 6 | f11, f21, y21, y31, f22, y32 |
| 3x3 | 6 | f11, f21, y21, y31, f22, y32 |
| 4x1 | 6 | f11, f21, f31, y21, y31, y41 |
| 4x2 | 10 | f11, f21, f31, y21, y31, y41, f22, f32, y32, y42 |
| 4x3 | 12 | f11, f21, f31, y21, y31, y41, f22, f32, y32, y42, f33, y43 |
| 4x4 | 12 | f11, f21, f31, y21, y31, y41, f22, f32, y32, y42, f33, y43 |

The angles are quantized according to the following formulae:

where

and

where

is the number of bits used to quantize and

is the number of bits used to quantize (See Explicit Feedback Format field (MIMO Compressed Steering)47).

All angles are transmitted LSB to MSB.

Subcarriers are sent in order according to the following sequence. For 20 MHz bandwidth operation:

For 40 MHz bandwidth operation:

For example, 40 MHz operation with Ng=2 would have subcarriers in the following order:

[-58,-56….-4,-2,2,4…….56,58].

Example: 2x2, 20 MHz, no grouping, bits for each  = 3, bits for each =5. Each ij over all tone indices has 168 bits. Each ij over all tone indices has 280 bits.

| Bits | b1 to b5 | b6 to b10 | … | b276 to b280 | b281 to b283 | b284 to b286 | … | b446 to b448 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| data | 11(f-28) | 11(f-27) | … | 11(f28) | 21(f-28) | 21(f-27) | … | 21(f28) |

# Example: 4x2, 40 MHz, 4 tone grouping, ,  = 4. Each ij over all tone indices has 120 bits. Each ij over

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This submission illustrates alternative presentations of the HT action frames.   It is not proposed as text to go in the TGn draft – it is just an example!

Related CIDs: 2231, 2237, 2245, 2253, 2273, 2297, 2345, 2353

The commenter said:

- The frame formats would be much better shown as a Figure than a table

- Change to a Figure showing sizes of each field, and a short paragraph below with the information currently in the "Value" column