IEEE P802.11
Wireless LANs

| LB84-Regular-sounding in Link Adaptation-text-proposal |
| --- |
| Date: 2006-07-13 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Tomoya Yamaura | Sony Corporation | 6-7-35 Kitashinagawa, Shinagawa-ku, Tokyo 1410001, Japan | +81 3 6409 3201 | yamauratomoya@yahoo.co.jp |

## Received Comments related to ‘regular’ sounding capability at LB#84

| CID | Clause (Ed) | Type (Ed) | Comment | Proposed change |
| --- | --- | --- | --- | --- |
| 3971 | 7.3.2.47.6 | T | There is no capability defined for Transmit/Receive sounding when sounding is not segmented or ZLF | Add capability bits for these cases |
| 10071 | 7.3.2.47.6 | ST | Add Capability of regular frame sounding, and add rule that staggered sounding capable devices shall support regular sounding also, to reduce capability fragmentation. | bit 25 - Receive regular sounding capable bit 26 - Transmit regular sounding capable And add restriction when B1 is '1', B25 shall be '1', and when B2 is '1', B26 shall be '1'. |
| 10072 | 7.3.2.47.6 | ST | Add Capability of regular frame sounding, and add rule that ZLF sounding capable devices shall support regular sounding also, to reduce capability fragmentation. | bit 25 - Receive regular sounding capable bit 26 - Transmit regular sounding capable And add restriction when B3 is '1', B25 shall be '1', and when B4 is '1', B26 shall be '1'. |
| 12000 | 7.3.2.47.6 | T | Add Capability of regular frame sounding replace reserved bits 25 and 26 | bit 25 - Receive regular sounding capable bit 26 - Transmit regular sounding capable |

## Background of proposal in this submission

Comment submitters have discussed how to resolve this issue, and concluded that it would be better to mandate transmission or reception (depending on supported features) of ‘regular’ sounding if the STA advertises its capabilities of TxBF using implicit feedback and/or TxBF using explicit feedback and/or fast link adaptation using HTC, rather than defining ‘regular sounding Tx/Rx capabilities which consumes reserved bits in capability field.

Please note that this new requirement shall not be applied to the devicves, which doesn’t support features described here.

For TxBF using explicit feedback (clause 9.20.3), 06/0886 would cover this issue.

For TxBF using implicit feedback (clause 9.20.2), 06/0593 would cover this issue.

This submission only covers this issue for Fast Link Adaptation (clause 9.19.2).

This submission would be classified as ‘counter’.

## Proposal

Instruct editor to add paragraphs shown below between line-38 and line-39 in clause 9.19.2 “Link Adaptation using the HT Control Field”, in page 105 of P802.11n D1.0.

The MCS feedback capable STA ("MCS feedback" field = '11' in Extended HT Capabilities Info field) shall support MFB estimate computation and feedback on the receipt of MCS request (MRQ=1 in HTC) in sounding PPDU which doesn't contain extension HT-LTFs.

The MCS feedback capable STA ("MCS feedback" field = '11' in Extended HT Capabilities Info field) shall support MFB estimate computation and feedback on the receipt of MCS request (MRQ=1 in HTC) in staggered sounding PPDU only if this STA is 'Receive staggered sounding capable'.

The MCS feedback capable STA ("MCS feedback" field = '11' in Extended HT Capabilities Info field) shall support MFB estimate computation and feedback on the receipt of ZLF (9.22) only if this STA is 'Receive ZLF capable'. The sender shall set the MRQ bit to 1 in the frame there the ZLF Announcement bit will be set to 1.

## References:

[1] IEEE P802.11n D1.0

[2] 11-06-0886-00-000n

[3] 11-06-0593-02-000n

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document includes proposed text for modification of the TGn 1.0 draft. The text is intended to provide a solution partly to the issue raised by LB84 Comment ID (CID) 3971, 10071, 10072, and 12000 regarding reuqest to add ‘regular (not staggered nor ZLF)’ sounding capability.