IEEE P802.11
Wireless LANs

| Capability Information Field settings for non-AP MPs to ensure backward compatibility with legacy STAs |
| --- |
| Date: 2006-07-18 |
| Author(s): |
| Name | Company | Address | Phone | email |
| W. Steven Conner | Intel Corporation | JF3-206, 2111 NE 25th Ave, Hillsboro OR 97124 | +1-503-712-4990 | w.steven.conner@intel.com |
| Anil K. Sanwalka | Neesus Datacom Inc. | 245 West Beaver Creek Rd, Unit 9B Richmond Hill, Ontario, L4B 1L1 | +1-905-762-1212 | anils@neesus.com |

This text specifies values for the ESS and IBSS fields in the capability information field of beacons and probe response frames sent by non-AP Mesh Points to avoid backward compatibility issues with legacy STAs.

Background:

P802.11s-D0.02 allows for beacon and probe responses to be sent both by Mesh APs as well as non-MAP Mesh Points.

If a legacy STA receives a  Beacon or Probe Response from a non-MAP MP, how does the legacy STA know that the MP will not accept an Association Request?  The current draft deals with this issue with the following text in Clause 7.2.3.1:

When dot11WLANMeshService is true but the interface on which the beacon is being sent is not configured as an Access Point, the SSID IE shall be set to the wildcard value. [Note: the SSID is a required IE in beacon frames. To avoid having non-mesh STAs send association requests to non-MAP Mesh Points, a valid SSID should not be included in beacons sent by non-MAP Mesh Points. To avoid backward compatibility issues, rather than removing the SSID IE from MP (non-MAP) beacons the wildcard value is used.]

This existing mechanism is not sufficient to prevent legacy STAs from attempting Association Requests since legacy APs are frequently configured to send the null SSID in their Beacons, allegedly as a security measure.  Legacy STAs will therefore still interpret these Beacon sources as APs.

To resolve this issue, the text below leverages the capability information field included in beacons and probe response frames which includes a bit for “ESS” and a bit for “IBSS”.  The base standard says that APs set the ESS subfield to 1 and the IBSS subfield to 0 while STAs within an IBSS set the ESS subfield to 0 and the IBSS subfield to 1.  To deal with this legacy issue, a new sentence should be added in clause 7.3.1.4 to say “Non-AP MPs set both the ESS subfield and IBSS subfield to 0 in transmitted Beacon or Probe Response management frames.”

The following is normative text proposed as an amendment to P802.11s/D0.02.

Make the following changes to the fourth paragraph of Clause 7.3.1.4 “Capability Information field”:

APs set the ESS subfield to 1 and the IBSS subfield to 0 within transmitted Beacon, or Probe Response, Association Request, or Association Response management frames. STAs within an IBSS set the ESS subfield to 0 and the IBSS subfield to 1 in transmitted Beacon or Probe Response management frames.  Non-AP MPs set both the ESS subfield and IBSS subfield to 0 in transmitted Beacon, Probe Response, Association Request, or Association Response management frames.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This submission contains normative text specifying the correct values for the ESS and IBSS fields in the capability information field of beacons and probe response frames sent by non-AP Mesh Points to avoid backward compatibility issues with legacy STAs.