IEEE P802.11
Wireless LANs

| Clause 11A.5 — Security |
| --- |
| Date: 2006-07-17 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Jesse Walker | Intel Corporation | JF3-206, 2111 NE 25th Ave, Hillsboro, OR USA 97124 | +1-503-264-8036 | jesse.walker@intel.com |
| Dan harkins | Tropos | 555 Del Rey Avenue, Sunnyvale, CA 94085 | +1-408-470-7372 | dharkins@itropos.com |

# Replace Clause 11A.5 with the following:

Editorial Note: This is a new outline for Clause 11A.5. Different security proposals may be supported by inserting them into the correct subclause or by adding new subclauses.

# 11A.5 Mesh Link Security

This clause specifies the enhancements needed to the Clause 8 mechanisms to secure links in a WLAN Mesh network. The defined security mechanisms provide link-by-link security. End-to-end security is beyond the scope of this specification.

    - Security Framework

Link security for a WLAN Mesh is provided in five stages:

- Discovery. Each MP advertises its security policy in the Beacons and Probe Responses it generates. Other MPs within range interpret received Beacons and Probe Responses to learn the security policy of the message source.

- IEEE 802.11 Authentication. When used this performs peer authentication and implicit authorization to perform mesh forwarding.

- Role determination. The security policy is consumed by an algorithm that determines which party plays the role of IEEE 802.1X Authenticator and which Supplicant for each link instance. This algorithm executes prior to beginning the link establishment procedure defined in Clause 11A.3.2.1.

- Policy selection. Policy selection is similar to that in Clause 8, with the Supplicant selecting among the pairwise ciphersuites and authenticated key management protocols advertised by the Authenticator in its Beacons and Probe Responses. The Supplicant asserts its selection through the WLAN Mesh link establishment procedure, defined in Clause 11A.3.2.1. The IEEE 802.1X entity closes its controlled port when the link establishment procedure begins.

- Authentication and key management. After link establishment completes, the Authenticator initiates IEEE 802.1X authentication and a variant of the authenticated key management process defined in Clause 8.5. IEEE 802.1X authentication may be null if a pre-shared key is employed. The use of this mechanism is optional

- Secure link operation. Once authenticated key management completes, the IEEE 802.1X entity opens its controlled port to allow data to flow, which is now protected.

When security is enabled, at least one of b) and e) is required.

      - Discovery

An MP discovers another MP by inspecting the mesh ID in its beacons. When it notices an MP with which it does not have an association is advertising a mesh ID for a mesh it supports it will deem the other MP discovered and proceed to 802.11 authentication.

      - 802.11 Authentication

After Discovery an MP shall utilize 802.11 authentication to authenticate the discovered MP.

      - Role determination

      - Policy selection

      - Authentication and key management

      - Secure link operation

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This submission contains a new outline for Clause 11A.5.