IEEE P802.11
Wireless LANs

| FT State Machines |
| --- |
| Date: 2006-07-26 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Jouni Malinen | Devicescape Software, Inc | 900 Cherry Ave, 6th Floor, San Bruno, CA 94066 | +1 650-829-2630 | jkm@devicescape.com |
| Dorothy Stanley | Aruba Networks | 1322 Crossman Ave Sunnyvale, CA 94089 | +1 630-363-1389 | dstanley@arubanetworks.com |

Background

FT Processing introduces new key management operations, and new means by which a security association is established. This document contains text for the new RSNA Key Management State Machines, including:

- A new FT Supplicant State Machine

- Modifications to the Authenticator (PTK) State Machine

- A new PMKR0-KH state machine

- Clarification changes related to existing GTK state machines

- Modifications to  RSNA Key Management Supplicant State Machine pseudocode

FT Architecture Components

The PMKRO-KH, PMKR1-KH and PTK-Holder perform RSNA Key Management State Machine Functions. Figure 10, Clause 5.8 in IEEE 802.11-REVma D7.0, duplicated below, shows the placement of RSNA Key management within the SME.

RSNA Key Management uses the MA_UNITDATA interface to send/receive EAPOL-Key data-frames.  FT processing uses EAPOL-Key data frames, the MLME_SETKEYS and MLME_SETPROTECTION primitives and defines three new mechanisms for Key Management data to be sent and received:

- The MLME ACTION  interfaces for key management data received over the DS,

- The MLME_AUTH interface for Key Management data sent and received over the air, and

- The MLME_REASSOC interface for Key Management data sent and received over the air.

This is shown in the figure below.

Insert the following text as a new section, 8.5.6.5

8.5.6.5 RSNA FT Supplicant Key Management State Machine

The Supplicant State Machine shall be instantiated when an FT mechanism is used. It is used for all FT mechanisms except for the Initial Association, which uses the RSNA Supplicant State Machine. [Need modifications to the current state machine pseudo code for PMKR1]

8.5.6.5.1 RSNA FT Supplicant Key Management state machine variables

To be provided

8.5.6.5.1 RSNA FT Supplicant Key Management state machine procedures

To be provided

Insert the following text as a new section after 8.5.7

8.5.8 RSNA Authenticator R0 Key Management State Machine

The RSNA Authenticator R0 Key Management State Machine shall be instantiated by the Authenticator when the STA has successfully authenticated to a Mobility Domain.

8.5.8.1 RSNA Authenticator R0 Key Management state machine variables

To be provided; RIKHID available, transition to CALCPMKR1?

8.5.6.5.1 RSNA Authenticator R0 Key Management state machine procedures

To be provided

Replace the current Part 1 of the Authenticator State Machine with the following:

Text changes to state machine variables and procedures - To be provided

GTK text changes– If GTK changed during the FT Handshake, trigger Group Key Handshake (Update) for this STA - To be provided

Update EAPOL() to D7.0 – To be provided

References:

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document contains initial drafts of FT RSNA Key Management State machines for both the Authenticator and Supplicant.