IEEE P802.11
Wireless LANs

| TGp Comment Resolution Annex I and J Changes |
| --- |
| Date: 2006-08-02 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Wayne Fisher | ARINC, Inc | 2551 Riva Road, Annapolis, MD 21401 | 410-266-4958 | wfisher@arinc.com |

|  | LB81 Comment Resolution |
| --- | --- |
| CID | Commenter: | Clause: | Addressed By: | Original Date Prepared |
| Multiple | Multiple | 20. | Wayne Fisher | August 2, 2006 |

- COMMENT:  [From Spreadsheet]

In response to comments received for Clause 20.

- Commenter’s Suggested Remedy (If appropriate):  [From Spreadsheet]

Not included here. (Not directly applicable.) Note, many comments were incorporated into the draft for changes to Annex I and Annex J.

- Background, Explanation, Discussion, etc.:

In response to the many comments received on Clause 20 of P802.11p D1.0 section 4 presents a draft of changes to Annex I and Annex J in place of the information that was contained in Clause 20.

In the ongoing development of IEEE Std 802.11 the regulatory requirements and country or regional information have been moved from Clause 17 to Annex I or Annex J.  Likewise, what country or regulatory information that was in Clause 20 is being added to the appropriate parts of Annex I or Annex J.

The additional spectrum mask requirements for WAVE are being relocated to Annex I.  In comparing the transmit spectrum masks requirements for WAVE to the present requirements in 802.11ma, please note that the higher power transmit capabilities of WAVE devices operating in a highly mobile environment require deeper skirts on the transmit spectrum masks.  This supports the interoperability requirements of nearby devices operating on other WAVE channels.

- Recommended Resolution of the Comment:

A draft of changes/additions to Annex I and Annex J  are provided:

# Annex I

(informative)

# Regulatory classes

## I.1 External regulatory references

In Table I.1- Regulatory requirement list, Insert to the list of documents for the United States as shown:

Table I.1—Regulatory requirement list

| Geographic area | Approval standards | Documents | Approval authority |
| --- | --- | --- | --- |
| Japan | Ministry of Internal Affairs and Communications (MIC) | MIC Equipment Ordinance (EO) for Regulating Radio Equipment Articles 7, 49.20, 49.21a | MIC |
| United States | Federal Communications Commission (FCC) | FCC CFR47 [B8], Part 15, Sections 15.205, 15.209, and 15.247; and Subpart E, Sections 15.401–15.407, Section 90.210, Section 90.1201-90.1217 Section 90.371-383, Section 95.639, Section 95.1501-1511 | FCC |
| Europe | Europe European Conference of Postal and Telecommunications (CEPT) Administrations and its Electronic Communications Committee (ECC). Also, European Radiocommunications Office, European Telecommunications Standards Institute | ECC DEC (04) 08, ETSI EN301 893 | CEPT |

Change Table I.2- Emissions limits sets, to add the Emissions limits sets for WAVE as shown:

Table I.2—Emissions limits sets

| Emissions limits set | USA | Europe | Japan |
| --- | --- | --- | --- |
| 0 | Not specified | Not specified | Not specified |
| 1 nomadic use | FCC CFR47 [B8], Section 15.407 | ETSI EN 301 389-1 | MIC EO Articles 49.20, 49.21 |
| 2 interference-limited areas | Reserved | Reserved | MIC EO Article 49.21 |
| 3 other interference areas | Reserved | Reserved | MIC EO Article 49.21 |
| 4 | FCC CFR47 [B8], Section 15.247 | Reserved | Reserved |
| 5 public safety | FCC CFR47 [B8], Section 90.210 | Reserved | Reserved |
| 6 WAVE Mode Class A | FCC CFR 47, Sections 90.375, 90.377 ; FCC CFR 47, Sections 90.1511, 90.639 | Reserved | Reserved |
| 7 WAVE Mode Class B | FCC CFR 47, Sections 90.375, 90.377 and 95.1511 | Reserved | Reserved |
| 8 WAVE Mode Class C | FCC CFR 47, Sections 90.375, 90.377 and 95.1511 | Reserved | Reserved |
| 9 WAVE Mode Class D | FCC CFR 47, Sections 90.375, 90.377 and 95.1511 | Reserved | Reserved |
| 10-255 | Reserved | Reserved | Reserved |

In Table I.3- Behavior limits sets, Add entries to the Behavior limits sets for WAVE as shown:

Table I.3—Behavior limits sets

| Behavior limits set | USA | Europe | Japan |
| --- | --- | --- | --- |
| 10 Wave Mode RSU/OBU | FCC CFR 47, Sections 90.375, 90.377, 90.379, 90.383, and 95.1511 | Reserved | Reserved |
| 11-255 | Reserved | Reserved | Reserved |

## I.2.3 Transmit spectrum mask

In the first subclause, change the second statement to:

For non-WAVE operation using 10 MHz channel spacing, the transmitted spectrum shall have a 0 dBr bandwidth not exceeding 9 MHz, –20 dBr at 5.5 MHz frequency offset, –28 dBr at 10 MHz frequency offset, and –40 dBr at 15 MHz frequency offset and above.

Insert the following text, table, and figures at the end of subclause I.2.3, updating figure and table numbers as needed:

For WAVE operations in the 5.85 – 5.925 GHz  frequency band in the USA, the transmit spectrum mask shall be relative to the station power class.  As with non-WAVE 10 MHz channel spacing, for all classes the transmit mask shall demonstrate a 0 dBr bandwidth not exceeding 9 MHz (±4.5 MHz).  Additional spectral falloff requirements are provided in Table pI.1.  The corresponding WAVE Class A through D spectrum masks are shown in Figures pI.1 through pI.4, respectively.   In all cases, the transmitted spectral density of the transmitted signal shall fall within the spectral mask.  This shall be accomplished by attenuating the transmitted signal by 55 + 10log(P) dBr at ±15 MHz and above, where P is the total transmitted power in watts.  The measurements shall be made using a 100 kHz resolution bandwidth and a 30 kHz video bandwidth.

Table pI.1—WAVE spectrum mask

| Station class | ± 4.5 MHz offset | ± 5.0 MHz offset | ± 5.5 MHz offset | ± 10 MHz offset | ± 15 MHz offset and above |
| --- | --- | --- | --- | --- | --- |
| Class A | 0 | -10 | -20 | -28 | -40 |
| Class B | 0 | -16 | -20 | -28 | -40 |
| Class C | 0 | -26 | -32 | -40 | -50 |
| Class D | 0 | -35 | -45 | -55 | -65 |

Reduction in Power Spectral Density, dBr

The transmitted spectrum mask for class A, B, C, and D stations are shown in Figures  pI.1, pI.2, pI.3, and  pI.4 respectively.

Note:  For WAVE operations, the transmit and receive antennas shall be either right hand circularly or vertically polarized.

Figure pI.1—WAVE Class A transmit spectrum mask

Figure pI.2—WAVE Class B transmit spectrum mask

Figure pI.3—WAVE Class C transmit spectrum mask

Figure pI.4—WAVE Class D transmit spectrum mask

# Annex J

(normative)

Country information element and regulatory classes

Delete the last row (starting with 12 – 255) in Table J.1.

Insert the following statements after Table J.1.:

The regulatory classes specified for the 5.85 – 5.925 GHz band in the USA are enumerated in Table pJ.1.  Regulatory classes 12 and 13 apply to both government (state/local) and non-government fixed and mobile station operations.  Regulatory class 14 applies to government fixed and mobile station operations.  Regulatory class 15 handles the corresponding non-government operations on this channel.  Regulatory class 16 applies to both government and non-government operations for fixed stations on channels 180 – 182 and class 17 handles operations on the same channels for mobile operations.  Regulatory class 18 applies to government fixed and mobile station operations on channel 184 and regulatory class 19 applies to non-government fixed and mobile station operations on this channel.

Add Table pJ.1 below:

Table pJ.1—5.9 GHz USA Regulatory classes

| Regulatory class | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel set | Transmit power limit (mW) | Max EIRP (dBm) | Emissions limits set | Behavior limits set |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 12 | 5 | 10 | 172, 174, 176 | 28.8 | 33.0 | 6-9 | 10 |
| 13 | 5 | 10 | 175 | 10.0 | 23.0 | 6-9 | 10 |
| 14 | 5 | 10 | 178 | 28.8 | 44.8 | 6-9 | 10 |
| 15 | 5 | 10 | 178 | 28.8 | 33.0 | 6-8 | 10 |
| 16 | 5 | 10 | 180, 181, 182 | 10.0 | 23.0 | 6-9 | 10 |
| 17 | 5 | 10 | 180, 181, 182 | 20.0 | 23.0 | 6-9 | 10 |
| 18 | 5 | 10 | 184 | 28.8 | 40.0 | 6-9 | 10 |
| 19 | 5 | 10 | 184 | 28.8 | 33.0 | 6-9 | 10 |
| 20-255 | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved |

- Motion (if technical and/or significant):

(And instructions to the editor.)

Move to accept the draft Annex I and Annex J changes as defined in section 4 of this document (1144r0)

And instruct the editor to incorporate these changes into a new draft P802.11p amendment as appropriate.

Motion by: ____________________Date: _________________

Second:  ______________________

| Approve: | Disapprove: | Abstain: |
| --- | --- | --- |

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

In response to the many comments received on Clause 20 of P802.11p D1.0 this document presents a draft of changes to Annex I and Annex J in place of the information that was contained in Clause 20.  This document presents a draft of these changes and is provided for discussion during the TGp teleconferences.

Note, this draft of changes to Annex I and Annex J includes the results of Comment Resolutions already addressed by documents:  802.11-06/ 0735r2, 0876r1, 0878r0, 1038r0, and the motions agreed to during the formal TGp sessions at the 802.11 WG meetings.