IEEE P802.11
Wireless LANs

| TGr Security Architecture – Unique PMK-R1 Names |
| --- |
| Date August 16, 2006 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Kapil Sood | Intel Corp. | 2111 NE 25th Ave JF3-206 Hillsboro OR 97124 | +1-503-264-3759 | Kapil.Sood@intel.com |
| Nancy Cam-Winget | Cisco Systems | 3625 Cisco Way, San Jose CA 95134 | +1-408-853-0532 | ncamwing@cisco.com |
| Rajneesh Kumar | Cisco Systems | 170 W Tasman Drive San Jose, Ca 95124 | +1-408-527-6148 | rajneesh@cisco.com |
| Lily Chen | NIST | 100 Bureau Dr. Gaithersburg, MD 20878 | (301) 975-6974 | llchen@nist.gov |
| Jesse Walker | Intel | 2111 NE 25th Ave JF3-206, Hillsboro OR 97124 | 503-264-3759 | Jesse.Walker@intel.com |

Updates based on TGr Draft D2.2

Update section 8.5A.4, with changes marked as follows:

8.5A.4 PMK-R0

The top level FT Key Hierarchy key, PMK-R0 binds the SPA, top level key holder (R0KH-ID), Mobility Domain Identifier, and SSID with the keying material resulting from the negotiated AKM. The PMK-R0 is the top level 256-bit keying material used to derive the next level keys (PMK-R1s):

R0-Key-Data = KDF-384(XXKey, "R0 Key Derivation", SSIDlength || SSID || MDID || R0KH-ID || 0x00 || SPA)

PMK-R0 = L(R0-Key-Data, 0, 256)

Where

- L(-) is defined in 8.5.1

- KDF-384 is the KDF function as defined in 8.5A.3 used to generate a key of length 384 bits.   PMK-R0 key shall be computed as the first 256 bits (bits 0-255) of the R0-Key-Data.  The latter 128 bits of R0-Key-Data shall be used as the PMK-R0Name-Salt to generate the PMKR0Name.

- If the AKM negotiated is 00-0F-AC:3, then XXKey shall be the second 256 bits of the MSK (MSK being derived from the IEEE 802.1X authentication), i.e., XXKey = L(MSK, 256, 256). If the AKM negotiated is 00-0F-AC:4, then XXKey shall be the PSK.

- "R0 Key Derivation" is 0x5230204B65792044657269766174696F6E.

- SSIDlength is a single octet whose value is the number of octets in the SSID.

- SSID is the service set identifier, a variable length sequence of octets, as it appears in the Beacons and Probe Responses.

- MDID is the 48-bit Mobility Domain Identifier field from the Mobility Domain information element that was used during FT Initial Mobility Domain Association.

- R0KH-ID is the 16-octet identifier of the holder of PMK-R0.

- SPA is the STA’s Supplicant’s MAC address.

The PMK-R0 is referenced and named as follows:

PMKR0Name = Truncate-128(SHA-256("R0 Key Name" || SSIDlength || SSID || MDID || R0KH-ID || 0x00 || SPA || PMK-R0Name-Salt))

where

- "R0 Key Name" is 0x5230204b6579204e616d65.

- PMK-R0Name-Salt = L(R0-Key-Data, 256, 128).  The next 128 bits (bits 256-383) of the R0-Key-Data shall be used in computing the PMK-R0Name.

- Truncate-128(-) returns the first 128 bits of its argument, and securely destroys the remainder.

The PMKR0Name is used to uniquely identify the PMK-R0 key.

In Section 8.5A.6.2, Page 29, Line 1

Remove: “The R0KH shall securely transmit the ANonce used in the calculation of PMKR0Name to the R1KH for use in the FT Initial Mobility Domain Association exchange and for PSK calculations.”

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

The document provides the text updates to make PMK-R1 names unique across different key hierarchy instantiations, by making the PMKR0Names unique.  Updates are made to TGr draft D2.2.

The text addresses a subset of changes discussed and proposed in 11-06-0566-02-000r-tgr-security-architecture.ppt (other changes are in different text submissions).  This submission addresses comments from LB82 around Security Architetcure for Fast Transitioning.