IEEE P802.11
Wireless LANs

| Normative Text Proposal for Adaptive Rate Control |
| --- |
| Date: 2006-01-10 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Feng Li | ZTE Corporation |  | +86-29-88723130 | li.feng8@zte.com.cn |
| Bin Wang | ZTE Corporation |  | +86-29-88723141 | Wang.binxa @zte.com.cn |
| Jie Li | ZTE Corporation |  | +86-29-88723148 | li.jiexa@zte.com.cn |
| Emily H. Qi | Intel Corporation | 2111 N.E 25th Ave. Hillsboro, OR 97124 | 503-264-7799 | Emily.h.qi@intel.com |
| Tim Olson | Cisco Systems | 170 W. Tasman Dr. San Jose, CA 95170 | 408-853-4527 | tolson@cisco.com |

Abstract

This document contains a normative text proposal in support of Adaptive Rate Control protocol in accordance with REQ2100 (doc:11-05/0827r3).

Contents

7. Frame formats	3

7.1 MAC frame formats	3

7.2.3.4 Association Request frame format	3

7.2.3.5 Association Response frame format	3

7.2.3.6 Reassociation Request frame format	3

7.2.3.7 Reassociation Response frame format	3

7.3.2 Information Elements	3

7.3.2.32 Wireless Network Management Capability element	3

11. MAC sublayer management entity	3

11.15 Wireless Network Management Procedures	3

11.15.1 Adaptive Rate Control	3

17. OFDM PHY specification for the 5 GHz band	3

17.3 OFDM PLCP sublayer	3

17.3.5.1 Service field (SERVICE)	3

18. High Rate direct sequence spread spectrum (HR/DSSS) PHY specification	3

18.2 High Rate PLCP sublayer	3

18.2.3.4 Long PLCP SERVICE field	3

19. Extended Rate PHY specification	3

19.3 Extended Rate PLCP sublayer	3

19.3.2.1 Long preamble PPDU format	3

# 7. Frame formats

#### 7.1 MAC frame formats

#### 7.2.3.4 Association Request frame format

Insert a new row into table 7 as shown below:

Table 7—Association Request frame body

| Order | Information | Notes |
| --- | --- | --- |
| 7 | Wireless Network Management Capability | Wireless Network Management Capability shall be present if dot11WirelessManagementImplemented is true. |

#### 7.2.3.5 Association Response frame format

Insert a new row into table 8 as shown below:

Table 8—Association Response frame body

| Order | Information | Notes |
| --- | --- | --- |
| 7 | Wireless Network Management Capability | Wireless Network Management Capability shall be present if dot11WirelessManagementImplemented is true. |

#### 7.2.3.6 Reassociation Request frame format

Insert a new row into table 9 as shown below:

Table 9—Reassociation Request frame body

| Order | Information | Notes |
| --- | --- | --- |
| 7 | Wireless Network Management Capability | Wireless Network Management Capability shall be present if dot11WirelessManagementImplemented is true. |

#### 7.2.3.7 Reassociation Response frame format

Insert new row into table 10 as follows:

Table 10—Reassociation Response frame body

| Order | Information | Notes |
| --- | --- | --- |
| 7 | Wireless Network Management Capability | Wireless Network Management Capability shall be present if dot11WirelessManagementImplemented is true. |

### 7.3.2 Information Elements

Insert Element ID x, and TBD into Table 20 and change the Reserved row accordingly:

Table 20—Element IDs

| Information Element | Element ID |
| --- | --- |
| Wireless Network Management Capability | x |
| Reserved | x+1, 255 |

Insert the following new clauses after 7.3.2.31

### 7.3.2.32 Wireless Network Management Capability element

The Wireless Network Management Capability Information element contains information about the wireless network management capabilities of a STA. The information field is two octets in length and contains the Wireless Network Management Capabilities field as shown in Figure v1.

|  | Element ID | Length | Wireless Network Management Capabilities |
| --- | --- | --- | --- |
| Octets: | 1 | 1 | 2 |

Figure v1—Wireless Management Capability Information element format

The Wireless Network Management Capabilities field is a bit field indicating the advertised management capabilities of the STA. The Wireless Network Management Capabilities field is shown in Figure v2.

|  | B0 | B1 | B15 |
| --- | --- | --- | --- |
|  | Adaptive Rate Control | Reserved |
| Bits: | 1 | 14 |

Figure v2—Wireless Network Management Capabilities

The Adaptive Rate Control bit set to 1 indicates the STA supports Adaptive Rate Control as described in 11.15.1. The Adaptive Rate Control bit set to 0 indicates that the STA does not support this service.

All other bits are reserved and shall be set to 0 on transmission and ignored on reception.

The lack of a Wireless Network Management Capability element shall be interpreted as the STA having no advertised Wireless Netork Management Capabilities.

# 11. MAC sublayer management entity

Insert 11.15 as follows:

#### 11.15 Wireless Network Management Procedures

This clause describes the management actions and the procedures for requesting and reporting wireless network management action between STAs.

#### 11.15.1 Adaptive Rate Control

Adaptive Rate Control allows a receiving STA to send a feedback rate to the sender for the next transmission with the objectives of improving performance.  A STA that supports Adaptive Rate Control shall set the Adaptive Rate Control bit in the Wireless Network Management Capabilities element to 1. A STA shall only include a feedback rate if both the transmitting STA and the receiving STA support Adaptive Rate Control.

Adaptive Rate Control applies to the case of unicast frame exchange sequences between two STAs. The initial frame of the frame exchange sequence (as defined in 9.12) is transmitted at one rate in the BSSBasicRateSet or the mandatory rate set of the PHY.  On receipt of any unicast frame, the receiving STA shall include a feedback rate in PLCP header (as defined in 17.3.5.1, 18.2.3.4, or 19.3.2.1, respectively) of the immediate response frame addressed to the sender. If a STA does not have a feedback rate available it shall set a feedback rate value indicating “No Recommendation” (as defined in 17.3.5.1, 18.2.3.4, or 19.3.2.1).

On receipt of the feedback rate in the immediate response frame, the sender shall transmit subsequent frames within the TXOP at the feedback rate.

Adaptive Rate Control supports the coexistence of different modulation types as defined in 19.1.2, but rate adaptation can only be processed with same modulation type during the TXOP.

The Adaptive Rate Control doesn’t apply to the frames with multicast and broadcast in the address1 field. The algorithm for performing rate estimate computation is beyond the scope of this standard.

# 17. OFDM PHY specification for the 5 GHz band

#### 17.3 OFDM PLCP sublayer

17.3.5 DATA field

#### 17.3.5.1 Service field (SERVICE)

Change this subclause as follows:

The IEEE 802.11 SERVICE field has 16 bits, which shall be denoted as bits 0–15. The bit 0 shall be transmitted first in time. The bits from 0–6 of the SERVICE field, which are transmitted first, are set to zeros and are used to synchronize the descrambler in the receiver. The bits from 7–10 of the SERVICE field are used by Adaptive Rate Control (as defined in 11.15.1) to indicate the feedback rate recommended for the next transmission. The Rate Identifier is specified in Table v1. The remaining 5 bits (11–15) of the SERVICE field shall be reserved for future use. All reserved bits shall be set to zero. Refer to Figure 112.

Insert the following table at the end of this subcluse:

Table v1 Rate Identifier

| B7 | B8 | B9 | B10 | Rate Identifier (Mbps) |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | No Recommendation |
| 0 | 0 | 0 | 1 | 6 |
| 0 | 0 | 1 | 1 | 9 |
| 0 | 1 | 0 | 1 | 12 |
| 0 | 1 | 1 | 1 | 18 |
| 1 | 0 | 0 | 1 | 24 |
| 1 | 0 | 1 | 1 | 36 |
| 1 | 1 | 0 | 1 | 48 |
| 1 | 1 | 1 | 1 | 54 |
| 0 | 0 | 1 | 0 | Reserved |
| 0 | 1 | 0 | 0 | Reserved |
| 0 | 1 | 1 | 0 | Reserved |
| 1 | 0 | 0 | 0 | Reserved |
| 1 | 0 | 1 | 0 | Reserved |
| 1 | 1 | 0 | 0 | Reserved |
| 1 | 1 | 1 | 0 | Reserved |

# 18. High Rate direct sequence spread spectrum (HR/DSSS) PHY specification

#### 18.2 High Rate PLCP sublayer

#### 18.2.3.4 Long PLCP SERVICE field

Change this subclause as follows:

Three bits have been defined in the SERVICE field to support the High Rate extension. The rightmost bit (bit 7) shall be used to supplement the LENGTH field described in 18.2.3.5. Bit 3 shall be used to indicate whether the modulation method is CCK <0> or PBCC <1>, as shown in Table 115. Bit 2 shall be used to indicate that the transmit frequency and symbol clocks are derived from the same oscillator. This locked clocks bit shall be set by the PHY based on its implementation configuration. Bit b1, Bit b4 and Bit b5 shall be used by Adaptive Rate Control (as defined in 11.15.1) to indicate the feedback rate recommended for the next transmission. The Rate Identifier is specified in Table v2. The SERVICE field shall be transmitted b0 first in time, and shall be protected by the CRC-16 FCS described in 18.2.3.6. An IEEE 802.11-compliant device shall set the values of the bits b0 and b6 to 0.

Change the following rows in Table 97:

Table 97—SERVICE field definitions

| b0 | b1 | b2 | b3 | b4 | b5 | b6 | b7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Reserved | Feedback rate | Locked clocks bit 0 = not 1 = locked | Mod. selection bit 0 = CCK 1 = PBCC | Feedback rate | Feedback rate | Reserved | Length extension |

Insert the following tableat the end of subcluse 18.2.3.4:

Table v2 Rate Identifier

| B1 | B4 | B5 | Rate Identifier (Mbps) |
| --- | --- | --- | --- |
| 0 | 0 | 0 | No Recommendation |
| 0 | 0 | 1 | 1 |
| 0 | 1 | 1 | 2 |
| 1 | 0 | 1 | 5.5 |
| 1 | 1 | 1 | 11 |
| 0 | 1 | 0 | Reserved |
| 1 | 0 | 0 | Reserved |
| 1 | 1 | 0 | Reserved |

# 19. Extended Rate PHY specification

#### 19.3 Extended Rate PLCP sublayer

#### 19.3.2.1 Long preamble PPDU format

…

Change this subclause as follows:

Table 123C shows graphically the assignment of the bits within the SERVICE field. The bits b0, b1, and b4 shall be used to by Adaptive Rate Control (as defined in 11.15.1) to indicate the feedback rate recommended for the next transmission. The Rate Identifier is specified in Table v3. Bit b2 is used to indicate that the transmit frequency and symbol clocks are derived from the same oscillator. For all ERP systems, the Locked Clock Bit shall be set to 1. Bit b3 is used to indicate if the data are modulated using the optional ERP-PBCC modulation. Bit b3 is defined in 18.2.3.4 with the caveat that the ERP-PBCC mode now has the additional optional rates of 22 and 33 Mbit/s as defined in 19.3.3.2. Bits b5, b6, and b7 are used to resolve data field length ambiguities for the optional ERP-PBCC-11 through ERP-PBCC-33 modes. These bits are fully defined in 19.6. Bit b7 is also used to resolve data field length ambiguities for the CCK 11 Mbit/s mode and is defined in 18.2.3.5. Bits b3, b5, and b6 are set to 0 for CCK.

Change Table123C as following:

Table 123C.SERVICE field bit definitions

| b0 | b1 | b2 | b3 | b4 | b5 | b6 | b7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Feedback rate | Feedback rate | Locked clocks bit 0 = not 1 = locked | Modulation Selection 0 = Not ERP-PBCC 1 = ERP-PBCC | Feedback rate | Length Extension Bit (ERP-PBCC) | Length Extension Bit (ERP-PBCC) | Length extension |

Insert the following table at the end of this subcluse:

Table v3 Rate Identifier

| b0 | b 1 | b4 | Rate Identifier for ERP-OFDM （Mbps） | Rate Identifier for DSSS-OFDM （Mbps） | Rate Identifier for ERP-DSSS （Mbps） | Rate Identifier for ERP-CCK （Mbps） | Rate Identifier for ERP-PBCC （Mbps） |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | No Recommendation | No Recommendation | No Recommendation | No Recommendation | No Recommendation |
| 0 | 0 | 1 | 9 or below | 9 or below | 1 | Reserved | Reserved |
| 0 | 1 | 0 | 12 | 12 | 2 | 5.5 | 5.5 |
| 0 | 1 | 1 | 18 | 18 | Reserved | 11 | 11 |
| 1 | 0 | 0 | 24 | 24 | Reserved | Reserved | 22 |
| 1 | 0 | 1 | 36 | 36 | Reserved | Reserved | 33 |
| 1 | 1 | 0 | 48 | 48 | Reserved | Reserved | Reserved |
| 1 | 1 | 1 | 54 | 54 | Reserved | Reserved | Reserved |

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.