IEEE P802.11
Wireless LANs

| Neighborhood Congestion Element |
| --- |
| Date: 2006-08-09 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Junping Zhang | Huawei Technologies Co., Ltd. | Huawei Longgang Production Base, Shenzhen 518129 P.R.China | +86-135-9023-1349 | zhjunping@huawei.com |

This text provides a resolution to Comments 12 and 231

CID: 12

Comment: It is not clear what the use of the expiration timer is. If an MP is at a certain congestion level (say congested), it cannot predict beforhand how long this condition would last. Congestion levels don't usualy time out.

Proposed Change: Delete expiration timer

Resolution: Defer-NS

CID: 231

Comment: Congestion Level should be defined.

Proposed Change:	A submission will be provided.

Resolution: Defer-RPS

Proposed resolution:

Make the following changes to the second and third paragraph of Clause 7.3.2.45 “Neighborhood Congestion Element”to  P802.11s/D0.02:

The congestion level is TBD.

Expiration timer indicates the valid period of congestion information provided in this element. Expiration Timer is represented in TU.

The expiration time should be set with the statistical time period (T) .The experimental value of T is 0.2s.

The congestion level indicate the level of congestion of the local node.When a node detects congestion, it sets the congestion level with “0” at first. If the node detects congestion again at the next period of statistic time, the congestion level will be set with“1”. That means that the congestion level will be increased with one if the congestion control announcement occurs again after a T period .When the congestion disappear, the level will reset

If the neighboring MPs received the “Neighborhood Congestion Announcement” message.Each AC of those nodes should adjust the local rate through adjusting the AIFSN parameter.The increment of AIFSN[AC] as follows:

(AIFSN[AC]=a[AC](2n                       (1)

In Eq.1, a[AC] is specified for each AC, and it is a constant. In order to meet the QoS requirement of delay-sensitive (such as voice traffic), the inequation

a[VO]<a[VI]<a[BK]=a[BG]                       (2)

should be guaranteed. n denotes the congestion level. The initial congestion level is 0.

Table1: the experimental parameter for a[AC]

| a[VO] | 0.3 |
| --- | --- |
| a[VI] | 0.4 |
| a[BK] | 0.6 |
| a[BG] | 0.6 |

References:

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

Proposed resolution text for Comments 12 and 231