IEEE P802.11
Wireless LANs

| TGr Security Architecture – Single key hierarchy instantiation per MD |
| --- |
| Date August 16, 2006 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Kapil Sood | Intel Corp. | 2111 NE 25th Ave JF3-206 Hillsboro OR 97124 | +1-503-264-3759 | Kapil.Sood@intel.com |
| Nancy Cam-Winget | Cisco Systems | 3625 Cisco Way, San Jose CA 95134 | +1-408-853-0532 | ncamwing@cisco.com |
| Rajneesh Kumar | Cisco Systems | 170 W Tasman Drive San Jose, Ca 95124 | +1-408-527-6148 | rajneesh@cisco.com |
| Lily Chen | NIST | 100 Bureau Dr. Gaithersburg, MD 20878 | (301) 975 - 6974 | llchen@nist.gov |
| Jesse Walker | Intel | 2111 NE 25th Ave JF3-206, Hillsboro OR 97124 | 503-264-3759 | Jesse.Walker@intel.com |

Updates based on TGr Draft D2.2

Section 8.5A.1, Page 25, Line 4.  Modify first paragraph as indicated below:

As depicted in Figure 160A, R0KH generates the first level key (PMK-R0) of the key hierarchy, from either the PSK or from the MSK resulting (per RFC 3748) from a successful IEEE 802.1X Authentication between the AS and the Supplicant, within a mobility domain.  Upon a successful authentication, the Supplicant and the R0KH shall delete the prior PMK-R0 key and  all PMK-R1 keys which were created between the Supplicant and the same mobility domain.  The second level keys (PMK-R1 keys) of the key hierarchy are generated by the R0KH as well. The PMK-R1 keys are delivered from the R0KH to the R1KHs within the same Mobility Domain. The PMK-R1 keys are used for PTK generation. Upon receiving a new PMK-R1 key for a STA, an R1KH shall delete the prior PMK-R1 key as well as PTKs derived from the same PMK-R1 key.

Section 8.5A.1, Page 25, Line 17.  Modify third paragraph as indicated below:

When the key lifetime expires, or when a new key hierarchy is instantiated after a successful authentication within the same mobily domain, the supplicant and each key holder within that mobility domain shall delete their respective PMK-R0, PMK-R1 or PTK SA.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

The document provides the text updates to ensure that at any time, only one PMK-R0 key hierarchy exists between a Supplicant and the mobility domain.  This is needed to avert attacks as described in 11-06-0624-00.  Updates are made to TGr draft D2.2.

This submission addresses comments from LB82 around Security Architetcure for Fast Transitioning.