IEEE P802.11
Wireless LANs

| TGr Security Architecture – Integrity Key (KCK11) for Protecting FT Management Messages |
| --- |
| Date August 16, 2006 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Kapil Sood | Intel Corp. | 2111 NE 25th Ave JF3-206 Hillsboro OR 97124 | +1-503-264-3759 | Kapil.Sood@intel.com |
| Nancy Cam-Winget | Cisco Systems | 3625 Cisco Way, San Jose CA 95134 | +1-408-853-0532 | ncamwing@cisco.com |
| Rajneesh Kumar | Cisco Systems | 170 W Tasman Drive San Jose, Ca 95124 | +1-408-527-6148 | rajneesh@cisco.com |
| Lily Chen | NIST | 100 Bureau Dr. Gaithersburg, MD 20878 | (301) 975 - 6974 | llchen@nist.gov |
| Jesse Walker | Intel | 2111 NE 25th Ave JF3-206, Hillsboro OR 97124 | 503-264-3759 | Jesse.Walker@intel.com |

Updates based on TGr Draft D2.2

Section 8.5A.7, Page 29, Update Line 47.

- PTKlen is the total number of key material bits to derive, e.g., number of bits of the PTK. PTKLen is 512 for CCMP and 640 for TKIP.

Section 8.5A.7, Page 29, Line 50.

Replace: “Each PTK has three associated keys, KCK, KEK, and TK, derived as follows:”

With: “Each PTK has four associated keys, KCK1X, KCK11, KEK, and TK, derived as follows.”

Section 8.5A.7, Page 29, Lines 52-56.

Replace all occurances of KCK with KCK1X

Section 8.5A.7, Page 29, Line 60 – Update line 60.

The KCK1X is used by IEEE 802.1X to provide data origin authenticity in the EAPOL-Key messages, in the 4-Way Handshake in FT Initial Association and Group Key Handshake messages.

Section 8.5A.7, Page 29, Line 61 – Insert the following after line 61.

The KCK11 shall be computed as bits 128-255 of the PTK:

KCK11 = L(PTK, 128, 128)

where L(-) is defined in 8.5.1.

The KCK11 is used to provide data origin authenticity in the FT management messages in the FT Base Mechnanism and in FT Reservation Mechanism (MIC generation and verification).

Update Section 8.5A.7, Page 29, lines 62-65 as follows.

The KEK shall be computed as bits 256-383 of the PTK

KEK = L(PTK, 256, 128)

Update Section 8.5A.7, Page 30, Line 4-8 as follows.

Temporal keys (TK) shall be computed as bits 384-511 (for CCMP) or bits 384-639 (for TKIP) of the PTK:

TK = L(PTK, 384, 128), or

TK = L(PTK, 384, 256)

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

The document provides the text updates to create a new Integrity protection key (called, KCK11) which will be used to provide authentication protection for FT management messages.  This is necessitated to prevent key sharing and key re-use of the EAPOL-Key confirmation Key (KCK, now called KCK1X), which protects EAPOL-Key messages in FT Initial Assoc and for TKIP countermeasures..

This submission addresses comments from LB82 around Security Architetcure for Fast Transitioning.