IEEE P802.11
Wireless LANs

| FT Protocol Refinement |
| --- |
| Date: 2006-08-22 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Michael Montemurro | RIM | 5090 Commerce Blvd, Mississauga, ON. L4W 5W4 | +1-416-804-3380 | mmontemurro@rim.com |

NOTE: THIS DOCUMENT ASSUMES THAT SUBMISSION 11-06/792r2 HAS BEEN ACCEPTED.

7.3.2.42 Mobility domain information element

Modify the first paragraph of this section as follows:

The Mobility Domain information element contains the Mobility Domain Identifier, Fast BSS Transition Capability and the Resource Policy. The Access Point uses the Mobility Domain information element to advertise that it is included in the group of APs that constitute a Mobility Domain, to advertise its support for Fast BSS Transition capability, and to advertise its resource policy information. The STA uses the Mobility Domain information element in the FT Transition Request message to signal the FT Protocol Mechanism that it will use. The format for this information element is given in Figure 112K.

8A.4 Fast BSS Transition reservation mechanism

Modify clause 8A.4, modifying the second paragraph with the following:

Availability of the reservation mechanism is advertised by the target AP in the MDIE, by setting the FT Protocol Option to 1. If the FT Protocol Option is set to one, then the STA shall use the FT Reservation mechanism. In this case, a STA that is not reserving resources may signal the use of the FT Base Mechanism using the FT Protocol Option as described in 8A.5.1. If a STA attempts to use the FT Base Mechanism when the FT Protocol Option is set to 1, the AP shall respond with status code set to 38 ("The request has not been successful as one or more parameters have invalid values"), unless the STA is not reserving resources and has signalled the FT Base Mechanism in the FT request message[#803, #1244]. If a STA attempts to use the FT Reservation Mechanism when the FT Protocol Option is set to 0, the AP shall respond with status code set to 38 ("The request has not been successful as one or more parameters have invalid values").

8A.5.1 FT authentication sequence: contents of fast BSS transition request

Add the following paragraph after the paragraph above:

The STA shall use the FT Protocol Option to indicate whether is will use the FT Base or FT Reservation mechanism. The FT Protocol Option chosen by the STA will be based on the FT Protocol Option advertised by the AP. If the FT Protocol Option advertised by the AP requires the FT Reservation mechanism but the STA does not need to reserve resources, the STA may use the FT protocol Option to indicate that it will use the FT Base Mechanism (i.e. will not be reserving resources) during the FT.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This submission addresses a use case where a STA using an FT mechanism tries to transition in the case where the AP advertises a FT Protocol option of reservation and the STA tries to FT without reserving resources.