IEEE P802.11
Wireless LANs

| LB84-CID-1177-text-proposal |
| --- |
| Date: 2006-07-28 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Matthew Fischer | Broadcom | 190 Mathilda Place, Sunnyvale, CA 94086 | 1 408 543 3370 | mfischer@broadcom.com |

CID 1177 (A)

TGn Editor: Insert, on page 33, near line 36, of TGn D1.03, before the line “Insert the following new subclause after 7.3.2.20:” the text and accompanying editor instructions as follows:

7.3.2.2 Supported Rates element

Change the first paragraph of this subclause as follows:

The Supported Rates element specifies up to eight rates in the Operational-Rate-Set parameter, as described in the MLME-JOIN.request and MLME-START.request primitives and zero or more BSS membership selector values. The information field is encoded as 1 to 8 octets, where each octet describes a single Supported Rate or BSS membership selector. If the combined total of the number of rates in the Operational Rate Set and the number of BSS membership selectors exceeds eight, then an Extended Supported Rate element shall be generated to specify the remaining supported rates and BSS membership selectors. The use of the Extended Supported Rates element is optional otherwise. If the BSSBasicMembershipSelectorSet parameter contains at least one BSS membership selector, then at least one BSS membership selector value from the BSSBasicMembershipSelectorSet parameter shall be included in the Supported Rates element.

Add a new paragraph to follow the exsiting second paragraph as follows:

Within Beacon, Probe Response, Association Response, and Reassociation Response management frames, each BSS membership selector contained in the BSSBasicMembershipSelectorSet parameter is encoded as an octet with the MSB (bit 7) set to 1, and bits 6 through 0 are set to the encoded value for the selector as found in table n99 in subclause x.y.z. (e.g., a xxxxx BSS membership selector contained in the BSSBasicMembershipSelectorSet parameter is encoded as X'xx'). BSS membership selectors not contained in the BSSBasicMembershipSelectorSet parameter are encoded with the MSB set to 0, and bits 6 through 0 are set to the appropriate value for the selector as found in table n99 in subclause x.y.z. (e.g., a yyyyy BSS membership selector not contained in the BSSBasicMembershipSelectorSet parameter is encoded as X'yy'). The MSB of each Supported Rate octet in other management frame types is ignored by receiving STAs.

Change the pre-existing third paragraph of this subclause as follows:

The Supported Rate and BSS membership selector information in Beacon and Probe Response management frames is delivered to the management entity in a STA via the BSSBasicRateSet parameter in the MLME-SCAN.confirm primitive. It is used by the management entity in a STA to avoid associating with a BSS if the STA cannot receive and transmit all the data rates in the BSSBasicRateSet parameter (see Figure 56) or cannot satisfy all of the membership requirements of the BSSBasicMembershipSelectorSet parameter. A STA which was implemented before the existence of the BSSBasicMembershipSelectorSet parameter will interpret each BSS membership selector in the Supported Rates element which is contained in the BSSBasicMembershipSelectorSet of the transmitting STA as though it were a rate from the BSSBasicRateSet parameter. The value will not match a rate which is known to the STA and therefore, the management entity in such a STA will avoid associating with the BSS because it determines that the STA cannot receive or transmit at what appears to be a required rate. A STA which is implemented after the existence of the BSSBasicMembershipSelectorSet parameter will interpret each BSS membership selector that it recognizes and determine if can meet the basic membership requirements before attempting to join the network. If there are some unknown requirements, this STA too, will avoid joining the network.

7.3.2.14 Extended Supported Rates element

Change the first paragraph of this subclause as follows:

The Extended Supported Rates element specifies the rates in the OperationalRateSet as described in the MLME_JOIN.request and MLME_START.request primitives and zero or more BSS membership selector values that are not carried in the Supported Rates element. The information field is encoded as 1 to 255 octets where each octet describes a single supported rate or BSS membership selector.

Add a new paragraph to follow the exsiting second paragraph as follows:

Within Beacon, Probe Response, Association Response, and Reassociation Response management frames, each BSS membership selector contained in the BSSBasicMembershipSelectorSet parameter is encoded as an octet with the MSB (bit 7) set to 1, and bits 6 through 0 are set to the encoded value for the selector as found in table n99 in subclause x.y.z. (e.g., a xxxxx BSS membership selector contained in the BSSBasicMembershipSelectorSet parameter is encoded as X'xx'). BSS membership selectors not contained in the BSSBasicMembershipSelectorSet parameter are encoded with the MSB set to 0, and bits 6 through 0 are set to the appropriate value for the selector as found in table n99 in subclause x.y.z. (e.g., a yyyyy BSS membership selector not contained in the BSSBasicMembershipSelectorSet parameter is encoded as X'yy'). The MSB of each octet in the Extended Supported Rate element in other management frame types is ignored by receiving STAs.

Extended Supported Rate information in Beacon and Probe Response management frames is used by STAs in order to avoid associating with a BSS if they do not support all the data rates in the BSSBasicRateSet parameter or all of the BSS membership requirements in the BSSBasicMembershipSelectorSet parameter.

For stations supporting a combined total of eight or fewer data rates and BSS membership selectors, this element is optional for inclusion in all of the frame types that include the supported rates element. For stations supporting more than a combined total of eight data rates and BSS membership selectors, this element shall be included in all of the frame types that include the supported rates element. If the BSSBasicMembershipSelectorSet parameter contains at least one BSS membership selector, then at least one BSS membership selector value from the BSSBasicMembershipSelectorSet parameter shall be included in the Supported Rates element.

References:

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document includes proposed text for modification of the TGn 1.01 draft. The text is intended to provide a resolution for CID 1177 from LB84. CID 1177 suggests the use of some mechanism to allow legacy STA to determine that a restrictive AP is restricting associations to those with a basic rate set which includes rates which are not visible to the legacy STA because they are not included in the traditional rate element. This causes the legacy STA to not realize that it is not a candidate for membership in the BSS and so it attempts to associate even though the association is doomed to failure.