IEEE P802.11
Wireless LANs

| Proposed Resolution to CIDs 3468 and 12162 |
| --- |
| Date: 2006-09-13 |
| Author(s): |
| Name | Company | Address | Phone | email |
| John Ketchum | Qualcomm Incorporated | 9 Damonmill Square Suite 2A Concord MA 01742 | 781-276-0915 | johnk@qualcomm.com |

# Introduction

## Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGn Draft.  This introduction, is not part of the adopted material.

CID 3468 and 12162

TGn Editor:  Make the changes indicated below to 21.3.7 (Mathematical description of signals) on page 165 lines 37 through 56.

Each baseband waveform  is defined via the discrete Fourier transform as

(21-4)

This general representation holds for all fields.  A suggested definition of the windowing function, , is given in 17.3.2.4.  The frequency domain symbols  represent the output of any spatial processing in subcarrier  for Tx chain  required for the field.

The   scale factor in Equation (21-4) ensures that the total power of the time domain signal as summed over all transmit chains is either 1 or lower than 1 when required.  Table n67 summarizes the various values of.

Submission Note: The factor of  is required in the denominator of (21-4) to ensure that the total power summed over the transmit chains is 1, as noted in the text.  This was was the point of CID 3468, so this change implements acceptance of that CID.  The change requested in 12162 is less clear, but the above text changes, with a note stating that  represents the composite output of any spatial processing for Tx chain , is a counter.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document contains proposed changes to the IEEE P802.11n Draft to address the following LB84 comments:

- 3468, 12162(C)

The changes marked in this document are based on TGn Draft version D1.03.