IEEE P802.11
Wireless LANs

| TGp Comment Resolution Summary of Changes to D1.0 as of 09/17/06 |
| --- |
| Date: 2006-09-17 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Wayne Fisher | ARINC, Inc | 2551 Riva Road, Annapolis, MD 21401 | 410-266-4958 | wfisher@arinc.com |

|  | LB81 Comment Resolution |
| --- | --- |
| CID | Commenter: | Clause: | Addressed By: | Original Date Prepared |

The following is basically a copy of the Abstracts in the associated documents that summarizes the changes to P802.11p D1.0.

1.	Clauses 5, 7, 9, 10, and 11.  (From 11-06-0890r3)

Changes to clauses 5, 7, and 9 that specify the MAC differences between the 11p WAVE mode and IBSS and infrastructure BSS (specifically, no beaconing or association, no management frames used except WAVE Announcement, Measurement Request/Report and link Measurement Request/Report, and control frames still permitted) in 802.11p.

This document uses REVma D7.0 for reference.  The specific changes to P802.11p D1.0 are proposed in document 11-06-0890r3, which also required edits to other parts of clauses 5, 7 and 9, as well as minor changes to clauses 10 and 11.  For the 802.11p draft this document essentially proposes replacing the existing clauses 5, 7, 9 and 11 with those provided herein, with a minor change to subclause 10.3.9.1. However, not all portions of these clauses were changed.

2.	Clause 20 incorporated into Clause 17  (From 11-06-1136r2)

In response to the many comments received on Clause 20 of P802.11p D1.0 this document presents a draft of changes to Clause 17 in place of the information that was contained in Clause 20.  Since so much of Clause 20 has been included in Clause 17 already by other task group amendments or has been relocated to an Annex or has been deleted it is reasonable to create changes and additions to the latest Clause 17 instead of maintaing a separate clause.  This document presents a draft of these changes and is provided for discussion during the TGp teleconferences.

Changes incorporated into Clause 17 include the results of Comment Resolutions already addressed by documents:  802.11-06/  0627r0, 0628r1, 0735r2, 0874r0, 0876r1, 0878r0, 1038r0, and the motions agreed to during the formal TGp sessions at the 802.11 WG meetings.

Updates from 8/10/06 teleconference include: Keep 64 levels of TXPWR.  Update (mostly remove) references of Slot Time, aAirPropagation Time, and aChSwitchTime. Update Table p12 and Table 152. Note, some items/issues still need to be verified and finalized.

3.	Annex A      (From 11-06-1357r0)

In response to the many comments received on P802.11p D1.0 this document presents a draft of changes to Annex A.  Note, this draft of changes to Annex A removes all references to Clause 20 which have been incorporated into Clause 17 and Annexes I and J.  The Transmit Specifications and Receiver Specifications and data rates for WAVE are addressed by the 10 MHz channel specifications already defined in Clause 17.  Only a few additional PICS are required to identify the 5.9 GHz band for WAVE and the additional temperature range to support devices operating in the automotive environment.

4.	Annex I and Annex J      (From 11-06-1144r2)

In response to the many comments received on Clause 20 of P802.11p D1.0 this document presents a draft of changes to Annex I and Annex J in place of the information that was contained in Clause 20.

Note, this draft of changes to Annex I and Annex J includes the results of Comment Resolutions already addressed by documents:  802.11-06/ 0735r2, 0876r1, 0878r0, 1038r0, and the motions agreed to during the formal TGp sessions at the 802.11 WG meetings.

In Rev 1 of this document changes include:  A “Coverage Class” column was added to Table pJ.1 and a statement added to the preceeding subclause.

EDITOR Note:  This subject has been addressed by Peter Ecclesine.  He implies that this is NOT required as it is covered in other ways. The only requirement is to add a line entry into the present Table J.1 to uniquely identify the WAVE Channel set as a new Regulatory Class (12).

This is an open area that needs to be discussed and resolved by TGp.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document summarizes the changes to P802.11p D1.0 that have been incorporated into a new draft P802.11p D1.1.