IEEE P802.11
Wireless LANs

| TGn LB84 Submission for CID 7071 |
| --- |
| Date: 2006-10-16 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Eldad Perahia | Intel Corporation |  |  | eldad.perahia@intel.com |

# Introduction

## Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGn Draft.  This introduction, is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGn Draft (i.e. they are instructions to the 802.11 editor on how to merge the TGn amendment with the baseline documents).

TGn Editor:  Editing instructions preceded by “TGn Editor” are instructions to the TGn editor to modify existing material in the TGn draft.   As a result of adopting the changes, the TGn editor will execute the instructions rather than copy them to the TGn Draft.

Summission Note: Notes to the reader of this submission are not part of the motion to adopt.  These notes are there to clarify or provide context.

# Proposed Resolution

| CID | Comment | Proposed Change | Resolution |
| --- | --- | --- | --- |
| 7071 | If N_TX is derived from ANTENNA_SET, then we are limiting the number of transmit chains to 4. With spatial spreading or beamforming, the only limitation should be the number of spatial streams. What is the reason for restricting a 6x4 device? | Use ANTENNA_SET only for Antenna Selection. Create a new TX VECTOR for N_TX, separate for Antenna Selection dimension. | Accept: refer to 06/1580 |

# CID 7071

TGn Editor: In D1.04, pg 150 Table n63—TXVECTOR parameters,  add the following rows

| ANTENNA_SET_ON | Set to 1 indicates that ANTENNA_SET is valid Set to 0 indicates that ANTENNA_SET is not valid |
| --- | --- |
| N_TX | Number of transmit chains |

TGn Editor: In D1.04, pg 153 add the following at the end of 21.2.2

Insert the following new subclause:

21.2.2.XX TXVECTOR ANTENNA_SET_ON

The ANTENNA_SET_ON parameter indicates whether the ANTENNA_SET parameter contains valid

values. If the value is 1, the ANTENNA_SET parameter is valid. If the value is 0, the

ANTENNA_SET parameter is not valid.

Insert the following new subclause:

21.2.2.YY TXVECTOR N_TX

The N_TX parameter indicates the number of transmit chains.

TGn Editor: In D1.04, pg 160, line 46 modify the text as follows

Determine the number of transmit chains, , from the ANTENNA_SET N_TX of the TXVECTOR.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document contains proposed changes to the IEEE P802.11n Draft to address the following LB84 comments:

7071

The changes marked in this document are based on TGn Draft version P802 11n D1 04.pdf.