IEEE P802.11
Wireless LANs

| Proposal for resolution of comments for P802.11.2-D0.10 |
| --- |
| Date: 2006-11-3 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Alexander Tolpin | Intel | PO Box 1659, Matam Industrial Park, Haifa 31015 Israel | +972-4-865-5430 | alexander.tolpin@intel.com |
| Neeraj K. Sharma | Intel | 2111 NE 25th Avenue, Hillsboro, OR 97124 | 503-712-7458 | neeraj.k.sharma@intel.com |
| Uriel Lemberger | Intel | PO Box 1659, Matam Industrial Park, Haifa 31015 Israel | +972-4-865-5701 | uriel.lemberger@intel.com |
| Mark Kobayashi | Broadcom | 190 Mathilda Place Sunnyvale, CA 94086 | 1-408-543-3318 | mmk@broadcom.com |
| Dalton Victor | Broadcom | 190 Mathilda Place Sunnyvale, CA 94086 | 1-408-922-5824 | dvictor@broadcom.com |
| Fahd Pirzada | Dell | One Dell Way, Round Rock, TX 78682 | (512) 338 4400 | Fahd_Pirzada@dell.com |
| Pratik Mehta | Dell | One Dell Way, Round Rock, TX 78682 | (512) 338 4400 | Pratik_Mehta@dell.com |

# Resolution for Comment [2] ID# 155

Here is the text of the comment

| ID | Clause | T or E | Part of Not Ready? | Comment | Suggested Remedy | Resolution | Resolution Text |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 155 | 6.2,6.5,6.6 | T | Y | For Throughput testing, a basic procedure should be developed and then desired modifications should be pointed out to cover the various scenarios covered in section 6.2, 6.5 and 6.6 | Combine sections 6.2, 6.5 and 6.6 into one section making changes such that the one section covers the required modifications while not being redundant in other sections | Deferred | 9/21/2006 - S. Tolpin and M. Kobayashi to work together to implement comment and bring a proposed revision to the group. |

CIDs 175, 150 and 151 are similar to CID 155.

The following text introduces restructuring changes in sections 6.2, 6.5 and 6.6 by combining all these sections in the section 6.X.  It also adds the Throughput versus Received Power in a COAT Environment metric.

### 6.X Throughput measurement

This clause specifies the generic definitions for throughput measurement that referenced later in clauses 6.2, 6.5 and 6.6

### 6.X.1 Introduction and purpose

The throughput is measured as the average data payload successfully transferred from the MAC SAP of the DUT to the MAC SAP of the WLCP, or to the MAC SAP of the DUT from the MAC SAP of the WLCP, for a specific test condition.

This test is applicable to wireless clients, and provides the basic measure of their ability to transmit and receive frames without loss across their wireless interface. This test is applicable to IBSS (Independent BSS) as well as infrastructure BSS client configurations. If an IBSS client is being tested, the results determine the ability of the client to exchange data traffic with another IBSS client. In infrastructure mode, the results determine the ability of the client to exchange data with an AP.

The setup comprises the DUT and a WLCP. The WLCP is a reference AP for infrastructure BSS configurations, or a reference client for IBSS configurations.

### 6.X.1.1 Throughput versus attenuation in a conducted environment

The purpose of this test is to determine the throughput of a DUT at different attenuation levels (which implies different received signal power, as measured at the antenna connector of the DUT), when handling unicast WLAN data frames that are confined to the wireless medium.

The DUT and the WLCP are connected by means of a controllable attenuator, using cables. Both the DUT and the WLCP are isolated by a shielded enclosure (or enclosures). A test controller is connected to the DUT, the WLCP and the controllable attenuator for purposes of traffic generation, analysis and control of received power using attenuation.

Two additional metrics may also be measured: the retry rate and the non-acknowledged rate.

### 6.X.1.2 Throughput versus receive power in a COAT environment

The purpose of this test is to determine the throughput performance of the DUT at various values of received power at the DUT’s antenna in an Calibrated Over the Air Testing (COAT) environment when handling unicast WLAN data frames. The attenuation reduces the received power level of the communication test signal at the DUT. Thus this test enables the throughput versus received power of the DUT to be represented in a real-life OTA scenario.

### 6.X.1.3 Throughput versus attenuation in an OTA environment

The purpose of this test is to determine the throughput performance of the DUT at various values of attenuation (which implies various levels of received power of the communication test signal at the DUT) in an OTA shielded test enclosure, when handling unicast WLAN data frames. The attenuation reduces the received power level of the communication test signal at the DUT. Thus this test enables the throughput versus range performance of the DUT to be represented in a real-life scenario.

This test is also usable for comparing the performance of different wireless APs (in infrastructure BSS mode), or different wireless clients (in IBSS mode), if the same reference DUT is used for the tests.

The WLCP is connected by means of cables to an external antenna through a controllable attenuator. The WLCP is enclosed in a shielded enclosure to minimize interference from extraneous signals. The DUT and the external antenna are placed in another shielded enclosure to allow LOS transmission of communication test signals from the external antenna to the DUT.

The communication test signal is generated by the WLCP when measuring downlink throughput performance. The communication test signal is generated by the DUT when measuring uplink throughput performance. The throughput performance is then measured for various levels of attenuation provided by the controllable attenuator.

### 6.X.1.4 Throughput versus range in an OTA environment

The purpose of this test is to determine the throughput performance of the DUT, when handling unicast WLAN data frames, at different ranges in various OTA test environments: indoor LOS, indoor non-LOS, and outdoor LOS. This test provides the best representation of an end-user experience with the performance of a wireless device.

This test is also usable for comparing the performance of different wireless APs (for BSS), or different wireless clients (for IBSS), if the same reference DUT is used for the tests.

The communication test signal is generated by the WLCP when measuring downlink throughput performance. The communication test signal is generated by the DUT when measuring uplink throughput performance.

### 6.X.2 Test configuration

This subclause describes test configurations of throughput tests for different environments.

### 6.X.2.1 Throughput versus attenuation in a conducted environment

< from this point include test from [2] 6.3.2, 6.3.2.1, 6.3.2.2, 6.3.2.3 and 6.3.2.4 >

### 6.X.2.2 Throughput versus receive power in a COAT environment

< from this point include test from [2] 5.2.2.1>

### 6.X.2.3.1 Throughput versus attenuation in an OTA environment

< from this point include test from [2] 6.6.2, 6.6.2.1, 6.6.2.2,  6.6.2.3 and 6.6.2.4 >

### 6.X.2.4.1 Throughput versus range in an OTA environment

< from this point include test from [2] 6.7.2, 6.7.2.1, 6.7.2.2,  6.7.2.3 and 6.7.2.4 >

### 6.X.3 Approach

### 6.X.3.1 Configuration parameters

This subclause provides a list of DUT setup parameters applicable to throughput measurement

### 6.X.3.1.1 Baseline configuration

The baseline DUT setup that should be configured, measured and reported whenever this test is performed is as follows:

a)	Maximum transmit power setting for the DUT and the WLCP.

b)	RTS threshold set to maximum MAC frame size.

c)	Fragmentation threshold set to maximum MAC frame size.

d)	MAC QoS and service priority disabled.

e)	No security (Open System authentication).

f)	No power management (i.e., active mode).

g)	Periodic scanning disabled if possible.

### 6.X.3.1.2 Modifiers

The baseline DUT setup parameters may be modified as follows to enable additional trials to be performed for this test.

a)	Transmit power settings: 25%, 50% and 75% of maximum.

b)	RTS threshold: 256, 512, 1024, 1528 and 2048 octets.

c)	Fragmentation threshold: 256, 512, 1024, 1528 and 2048 octets.

d)	MAC QoS and service priority enabled.

e)	Security usage: WEP-40, WEP-104, TKIP, CCMP.

f)	Power save mode

Only one variation should be tested at a time.

### 6.X.3.2 Test conditions

The test conditions used while performing this test are as follows:

a)	Frame sizes used in test traffic: 128, 256, 512, 1024, 1528 and 2048 octets.

b)	Attenuation values: minimum, maximum and step (typical: minimum 0 dB, maximum 100 dB, step 1 dB), or Range values: minimum, maximum and step (typically: minimum 1 meter, maximum 150 meters, step 10 meters

c)	 Duration of measurement for each range or attenuation: minimum 1 minute, maximum 3 minutes.

d)	Traffic directions: either unidirectional to/from the DUT, or bidirectional.

e)	Traffic type: TCP or UDP.

f) 	The turn table, if available, is operated at a specified speed (measured in revolutions per minute).

### 6.X.3.3 Calibration Procedure for Throughput in a COAT Environment

The calibration and setup requirements for COAT throughput measurements are as described in 5.2.3.3.1, 5.2.3.3.2 and 5.2.3.3.3.

### 6.X.3.4 Measurement procedure

The DUT is first set up according to the baseline configuration, using an initial combination of test conditions, and is associated with the WLCP. The following steps are then performed:

a)	The current attenuation or range value is set to the minimum value as per 6.X.3.

b)	The traffic generation device generates data traffic at a rate higher than or equal to the maximum theoretical throughput for specific frame sizes during the required duration. The downlink throughput is measured at the DUT and recorded.

c)	The DUT generates data traffic at a rate higher than or equal to the maximum theoretical throughput for specific frame sizes during the required duration. The uplink throughput is measured at the traffic generation device and recorded.

d)	The attenuation or range value is increased by the step amount, thereby decreasing received power.

e)	Steps a) through d) are repeated until the attenuation or range value exceeds the maximum value as per 6.X.3.2

The measurements are repeated for each combination of frame size and test traffic direction. Each trial represents a different set of test conditions and is reported separately.

After the baseline DUT configuration has been tested, the tester may repeat the process with a new configuration, until the desired number of different DUT configurations has been exercised.

### 6.X.3.5 Reported results

This clause describes reported results of throughput tests for different environments.

### 6.X.3.5.1 Throughput versus attenuation in a conducted environment

< from this point include test from [2] 6.3.3.4 >

### 6.X.3.5.2 Throughput versus receive power in a COAT environment

Test results for a throughput vs received power in a COAT environment should be in the form of a table and/or plot of throughput vs received power.  Power should be reported or plotted in dBm and throughput should be plotted in Mbits/sec.  The report should also provide DUT and traffic generation device details such as the manufacturer and type, BIOS type and version, OS type and version, WLAN driver, etc.  When possible, one should also report the PHY rate being used at each measurement point.  Direction of data traffic flow should also be noted for each test.

### 6.X.3.5.3 Throughput versus attenuation in an OTA environment

< from this point include test from [2] 6.6.3.4 >

### 6.X.3.5.4 Throughput versus range in an OTA environment

< from this point include test from [2] 6.7.3.4 >

# References

- P802.11.2-D0.10. Draft Recommended Practice for the Evaluation of 802.11 Wireless Performance.

- 7IEEE 802.11-06-0872r15. Comments from TGT Internal Review.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document contains the proposal for resolution of the comments to draft P802.11.2-D0.10. The comments are referenced in the document IEEE 802.11-06-0872r15 CID 155, 151,150,175.