IEEE P802.11
Wireless LANs

| Proposal for resolution of comments for P802.11.2-D0.10 |
| --- |
| Date: 2006-11-3 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Neeraj K. Sharma | Intel | 2111 NE 25th Avenue, Hillsboro, OR 97124 | 503-712-7458 | neeraj.k.sharma@intel.com |
| Uriel Lemberger | Intel | PO Box 1659, Matam Industrial Park, Haifa 31015 Israel | +972-4-865-5701 | uriel.lemberger@intel.com |
| Alexander Tolpin | Intel | PO Box 1659, Matam Industrial Park, Haifa 31015 Israel | +972-4-865-5430 | alexander.tolpin@intel.com |

# Resolution for Comment [2] ID# 243, 262, and 250

Clause 5.4.1.2.2 Test setup

Replace the sentence”

“The WLCP is placed on a test stand and the DUT on a motorized turntable on top of a test station cart. A traffic generator is used to generate data traffic from the WLCP to the DUT above the Layer 2 (MAC) protocol layer.”

With:

“In the case where either the WLCP or the DUT is an AP, the AP is placed on a test stand (fixed) and the DUT on a motorized turntable (rotated) on top of a test station cart.  In the case where both the WLCP and the DUT are STAs, the STA which is the DUT is placed on the motorized turntable. A traffic generator is used to generate data traffic from the WLCP to the DUT above the Layer 2 (MAC) protocol layer.”

Clause 5.4.1.2.3 Test parameters - Table 1

Items 1 and 2: Replace the word “DUT” by “STA” everywhere.

Item 4

Replace the test parameter:

“DUT spinning”

With”

“STA spinning”

Replace the requirement:

“At all test locations at which the DUT is more than 3 meters distant from the WLCP, the DUT should be spun clockwise about its geometric center point at a fixed rate of 1 - 10 RPM, within a run accuracy of ± 10%. This requirement is intended to track any fading or antenna angle effects.”

With:

“At all test locations at which the DUT is more than 3 meters distant from the WLCP, the STA should be spun clockwise about its geometric center point at a fixed rate of 1 - 10 RPM, within a run accuracy of ± 10%. This requirement is intended to track any fading or antenna angle effects.”

Item 5:

Replace:

“WLCP test height and antenna orientation”

With:

“AP test height and antenna orientation”

Clause 5.5.1.2.2 Test setup

Replace the sentence:

“The WLCP may be either placed on a test stand, or mounted to a wall or ceiling. The DUT is placed on a motorized turntable on top of a test station cart. A traffic generator is used to generate data traffic from theWLCP to the DUT above the Layer 2 (MAC) protocol layer.”

With:

“In the case where either the WLCP or the DUT is an AP, the AP is placed on a test stand, or mounted to a wall or ceiling (fixed) and the DUT on a motorized turntable (rotated) on top of a test station cart.  In the case where both the WLCP and the DUT are STAs, the STA which is the DUT is placed on the motorized turntable. A traffic generator is used to generate data traffic from the WLCP to the DUT above the Layer 2 (MAC) protocol layer.”

Clause 5.5.1.2.3 Test parameters - Table 3

Items 1 and 2: Replace the word “DUT” by “STA” everywhere.

Item 4

Replace the test parameter:

“DUT spinning”

With:

“STA spinning”

Replace the requirement:

“At all test locations at which the DUT is more than 3 meters distant from the WLCP, the DUT should be spun clockwise about its geometric center point at a fixed rate of 1 - 10 RPM, within a run accuracy of ± 10%. This requirement is intended to track any fading or antenna angle effects.”

With:

“At all test locations at which the DUT is more than 3 meters distant from the WLCP, the STA should be spun clockwise about its geometric center point at a fixed rate of 1 - 10 RPM, within a run accuracy of ± 10%. This requirement is intended to track any fading or antenna angle effects.”

Item 5:

Replace:

“WLCP test height and antenna orientation”

With:

“AP test height and antenna orientation”

# Resolution for Comment [2] ID# 244

Clause 5.4.1.2.3 Test parameters - Table 1, Item 5

Replace:

“APs used for performance testing should be placed such that their antennas are pointing up (straight) and perpendicular to the ground, with the base of the antennas at a fixed height (e.g. 150cm ± 1.5 cm) above the ground.”

With:

“APs used for performance testing should be placed as shown in Figure 8 with the base of the antennas at a fixed height h above the ground. The AP height is according to the test purpose and must be recorded with the results.”

Replace:

“This requirement is intended to define a consistent antenna orientation, and to adhere to the WLCP manufacturers recommendation to mount the WLCP as high as possible. Fixturing is recommended to provide consistent WLCP placement.”

With:

“This requirement is intended to define a consistent antenna orientation and location. Fixturing is recommended to provide consistent AP placement.”

Clause 5.5.1.2.3 Test parameters - Table 3, Item 5

Replace:

“APs used for performance testing should be placed such that their antennas are pointing up (straight) and perpendicular to the ground, with the base of the antennas at a fixed height (e.g. 275cm ± 1.5 cm) above the ground.”

With:

“APs used for performance testing should be placed as shown in Figure 8 with the base of the antennas at a fixed height h above the ground. The AP height is according to the test purpose and must be recorded with the results.”

Replace:

“This requirement is intended to define a consistent antenna orientation, and to adhere to the WLCP manufacturers recommendation to mount the WLCP as high as possible. Fixturing is recommended to provide consistent WLCP placement.”

With:

“This requirement is intended to define a consistent antenna orientation and location. Fixturing is recommended to provide consistent AP placement.”

Replace Figure 8 with:

Clause 5.5.1.2.3 Test parameters, Table 3

Figure 11: Delete figure 11 (this is the same as Figure 8 as the height is no longer being specified but rather the parameter h) and in Item 5, column Applicable figure, replace “Figure 11” with “Figure 8.”

# Resolution for Comment [2] ID# 249

Clause 5.5.1.2.3 Test parameters, Table 3, item 2

Replace the sentence:

“This requirement is not applicable to devices whose 802.11 antenna(s) are not in the lid/LCD, or are base-mounted (such as DUTs with Cardbus or PCMCIA adapters with integrated antennas), or to 802.11 device configurations with external antennas.”

With:

“This requirement is applicable only to devices that have an integral display whose viewing angle is adjustable.”

# Resolution for Comment [2] ID# 251 and 255

Clause 5.4.1.2.3 Test parameters, Table 1

Replace Figure 5 with:

Appropriate changes also made to Figure 8 as shown in Resolution for Comment ID# 244.

# Resolution for Comment [2] ID# 146

Figure 7 (Figure 8 in the new draft [1]) caption has already been changed in the draft 10 [1]. Figure 11 in the new draft (Figure 10 in the old draft) has been deleted as per comment ID# 144.

# Resolution for Comment [2] ID# 54

Clause 5.5.1.2.1 Resource requirements

Replace:

“e) An optional spectrum analyzer.”

With:

“e) Spectrum analyzer.”

Clause 5.6.2.1 Resource requirements

Replace:

“e) An optional spectrum analyzer.”

With:

“e) Spectrum analyzer.”

Annex B.3 Test equipment minimum capabilities in draft 10 [1] does contain the sentence "Test equipment should be calibrated as per manufacturer's specifications"

# Resolution for Comment [2] ID# 70

Clause 5.6.5 Special reporting requirements

In the new draft 10 [1], the contents of this clause has been changed with “The composition of the floor, ceiling, and walls should be recorded.”

Clause 5.5.1.5 Special reporting requirements (Page 34)

Replace:

“No special requirements are associated with this environment.”

With:

“The composition of the floor, ceiling, and walls should be recorded.”

This will make it consistent with clause 5.6.5.

# Resolution for Comment [2] ID# 261

Clause 5.6.2.1 Resource requirements

Replace:

“c) The test area should be flat, with a linear distance of approximately 70 meters.”

With:

“c) The test area should be flat and allow placing the DUT at a distance of at least 70 meters from the WLCP.”

Clause 5.4.1.2.1 Resource requirements

Replace:

“c) A flat test area with a linear distance of approximately 300 meters.”

With:

“c) A flat test area that allows placing the DUT at a distance of at least 300 meters.”

# Correction – 1

Clause 5.6.3 Procedure (Page 39)

The sentence “The test setup should be configured as shown in Figure 10” should read as “The test setup should be configured as shown in Figure 4.

# Correction – 2

Figure 4 – Typical outdoor LOS setup shown below indicates that the WLCP can be on a test stand or wall/ceiling. In outdoor LOS, you will not have wall or ceiling and therefore the labelling “Test Stand or wall/ceiling needs to be corrected.

Figure 4 (shown above) should be replaced by figure shown below:

# Correction – 3

Clause 6.18.2.3 Test Setup

In this clause, the distance between DUT and Client_Jammer is specified as 2 meters ± 1cm but it is not specified how this distance is measured. Figure 57 shows this distance is measured from center of the DUT to the center of the Client_Jammer. This makes the distance between the two devices dependent on the size of the DUT and client_Jammer.

“The distances between the test devices are as follows:

- Distance between WLCP and AP_Jammer = 40 meters ± 1cm

- Distance between DUT and Client_Jammer = 2 meters ± 1cm

- Distance between WLCP and DUT = Distance between the AP_Jammer and Client_Jammer.”

“The positioning of the DUT and Client_Jammer should be as follows:

- For laptops, DUT and Client_Jammer are placed back-to-back as shown in Figure 1.

- For desktops with external antennas, the DUT’s and Client_Jammer’s antennas are placed on top of their respective test station carts.

- For desktops with internal antennas, the desktops are placed on top of their respective test station carts.”

First sentence above should be replaced by:

“The distances between the test devices are as follows:

- Distance between WLCP and AP_Jammer = 40 meters ± 1.5cm

- Distance between DUT and Client_Jammer = 2 meters ± 1.5cm

- Distance between WLCP and DUT = Distance between the AP_Jammer and Client_Jammer.”

The second sentence above should be replaced by:

“The positioning of the DUT and Client_Jammer should be as follows:

- For laptops, DUT and Client_Jammer are placed back-to-back and the distance between the DUT and the Client_Jammer is measured from the back base of the DUT to the back base of the Client_Jammer as shown in Figure 57.

- For desktops with external antennas, the DUT’s and Client_Jammer’s antennas are placed on top of their respective test station carts and the distance between the DUT and the Client_Jammer is measured from the center of the antenna of the DUT to the center of the antenna of the Client_Jammer.

- For desktops with internal antennas, the desktops are placed on top of their respective test station carts and the distance between the DUT and the Client_Jammer is measured from inside edge of the DUT to the inside edge of the Client_Jammer.

Figure 57 (above) should be replaced by:

# Correction – 4

The lid angle should be 110o and not 120o. This effects the following text and figures in the draft:

Table 1, item 2 and Table 3, item 2, Table 6, item 2:

Replace:

The DUT’s lid/LCD should be positioned such that it is at 120 degrees ± 1 degree relative to a level ground.

With:

The DUT’s lid/LCD should be positioned such that it is at 110 degrees ± 1 degree relative to a level ground.

Replace Figure 6 as below:

With:

# Replace figure 10 shown below:

With:

# References

- P802.11.2-D0.10. Draft Recommended Practice for the Evaluation of 802.11 Wireless Performance.

- IEEE 802.11-06-0872r15. Comments from TGT Internal Review.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document contains the proposal for resolution of some comments to draft P802.11.2-D0.10 and some corrections. The comments referenced to are listed in the document IEEE 802.11-06-0872r15 and the comments addressed are as follows: 243, 244, 262, 249, 250, 251, 255, 146, 54, 70, and 261. There are four other corrections.

Test Controller/Traffic Generator

Distance Between WLCP and AP_Jammer

Test Controller/Traffic Generator

1200

1200

Test Stand or wall/ceiling

Distance Between

Client_Jammer

and AP_Jammer

Distance Between WLCP and AP_Jammer

Test Controller/Traffic Generator

1100

1100

Test Stand or wall/ceiling

Distance Between

Client_Jammer

and AP_Jammer

Distance Between WLCP

and DUT

DUT

Client_Jammer

WLCP

Distance Between DUT and Client_Jammer

h +/- 1.5cm

h +/- 1.5cm

Distance Between WLCP

and DUT

DUT

Client_Jammer

WLCP

Distance Between DUT and Client_Jammer

Test Controller/Traffic Generator

Spectrum Analyzer

Test Station Cart

AP_Jammer

Wired LAN Cable

Test Stand or wall/ceiling

WLCP

Obstructions

1200

Measurement Distance

Test Controller/Traffic Generator

Spectrum Analyzer

DUT capable of Rotating

Test Station Cart

Wired LAN Cable

Test Stand or wall/ceiling

WLCP

AP wall mounted

AP ceiling mounted

AP placed on a stand

h +/- 1.5cm

Obstructions

1100

Measurement Distance

Test Controller/Traffic Generator

Spectrum Analyzer

DUT capable of Rotating

Test Station Cart

Spectrum Analyzer

Test Station Cart

AP_Jammer

1100

Measurement Distance

Test Controller/Traffic Generator

Spectrum Analyzer

DUT capable of Rotating

Test Station Cart

Wired LAN Cable

Test Stand (for indoor LOS, wall/ceiling)

WLCP

1200

Measurement Distance

Test Controller/Traffic Generator

Spectrum Analyzer

DUT capable of Rotating

Test Station Cart

Wired LAN Cable

Test Stand or wall/ceiling

WLCP