IEEE P802.11
Wireless LANs

| Generation and transmission of BlockAck |
| --- |
| Date: 2006-12-31 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Solomon Trainin | Intel Corporation | POB 1659, Haifa 31015, Israel | +97248655738 | solomon.trainin@intel.com |
| Matthew Fischer | Broadcom | 190 Mathilda Place, Sunnyvale, CA 94086 | 1 408 543 3370 | mfischer@broadcom.com |

# Introduction

## Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGn Draft.  This introduction is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGn Draft (i.e. they are instructions to the 802.11 editor on how to merge the TGn amendment with the baseline documents).

TGn Editor:  Editing instructions preceded by “TGn Editor” are instructions to the TGn editor to modify existing material in the TGn draft.   As a result of adopting the changes, the TGn editor will execute the instructions rather than copy them to the TGn Draft.

Summission Note: Notes to the reader of this submission are not part of the motion to adopt.  These notes are there to clarify or provide context.

TGn Editor: Change the entire text of subclause “9.10.7.5 Generation and transmission of BlockAck during partial-state operation and full-state operation” on pages 109 and 110 of TGn D1.07 as follows:

When responding with a BlockAck frame to either a received BlockAckReq frame or a received A-MPDU with ACK Policy set to Normal Ack (i.e. implicit Block Ack request) during either full-state operation or partial-state operation, any adjustment to the value of WinStart_R according to the procedures defined within 9.10.7.3 Scoreboard context control in full state and 9.10.7.4 Scoreboard context control in partial state shall be performed before the generation and transmission of the response BlockAck frame. The Starting Sequence Number of the Block Ack Starting Sequence Control field of the BlockAck frame shall be set to any circular modulo 2^12 value in the range from (WinEnd_R - 63) to WinStart_R inclusive. The values in the recipient’s record of status of MPDUs beginning with the MPDU for which the Sequence Number field value is equal to WinStart_R and ending with the MPDU for which the Sequence Number field value is equal to WinEnd_R shall be included in the bitmap of the BlockAck frame.

When responding with a BlockAck frame to either a received BlockAckReq frame or a received A-MPDU with ACK Policy set to Normal Ack (i.e. implicit Block Ack request) during either full-state or partial-state operation, if the adjusted value of WinStart_R is greater than the value of the SSN of the BlockAck frame, then within the bitmap of the BlockAck frame, the status of MPDUs with sequence numbers that are less than the adjusted value of WinStart_R (using a circular modulo 2^12 comparison) may be set to any value.

When responding with a BlockAck frame to either a received BlockAckReq frame or a received A-MPDU with ACK Policy set to Normal Ack (i.e. implicit Block Ack request) during either full-state or partial-state operation, if the adjusted value of WinEnd_R is less than the value of the SSN of the BlockAck frame plus 63, then within the bitmap of the BlockAck frame, the status of MPDUs with sequence numbers that are greater than the adjusted value of WinEnd_R (using a circular modulo 2^12 comparison) shall be reported as unsuccessfully received (i.e., the corresponding bit in the bitmap shall be set to 0).

If a BlockAckReq is received and no matching partial state is available, the recipient shall send a “null” BlockAck with an all 0 bitmap.

NOTE—The sequence number space is considered divided into two parts, one of which is “old” and one of which is

“new” by means of a boundary created by adding half the sequence number range to the current start of receive window

(modulo 2^12). (Ed: CID 4765)

References:

11-06-1345-10-000n-lb84-cid-1264-text-proposal

IEEE P802.11n/D1.07, December 2006

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart@ok-brit.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

This submission reopens the CID 1264 in relation to subclause 9.10.7.5 Generation and transmission of BlockAck during partial-state operation and full-state operation

Definition of Starting Sequence Number has been fixed to solve controversy between first and fifth paragraph in the submission 11-06-1345-10-000n-lb84-cid-1264-text-proposal and draft D1.07. The presented definition of BA unifies response to BlockAckReq frame and response to received A-MPDU with ACK Policy set to Normal Ack.

This change refers to IEEE P802.11n/D1.07, December 2006