IEEE P802.11
Wireless LANs

| Make the MDID Two Octets |
| --- |
| Date: 2007-01-16 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Dan Harkins | Tropos Networks | 555 Del Rey ave., Sunnyvale, CA. USA | +1 408 470 7372 | dharkins@tropos.com |

The Mobility Domain identifier is used to uniquely identify a Mobility Domain. It is currently six octets which is excessive. A two octet Mobility Domain identifier would serve the same purpose since a rational, static configuration of mobility domains would be able to take advantage of the entire range (65536) of values. Given the limitations of 802.11 it is unlikely that there would be even more than a handfull of overlapping mobility domains in any given geographic area. In that sense one octet could servee this purpose. But not every configuration is necessarily rational. So with two octets even a randomly chosen Mobility Domain identifier would have a statisticly insignificant probability of collision.

3.86b Mobility Domain Identifier

Change to:

A 16-bit value that identifies a Mobility Domain.

7.3.2.45 Mobility domain information element

Change Figure 112s – octet size indicator in Mobility Domain information element for the Mobility Domain Identifier from

6

to:

2

Change the two sentences following Figure 112s to:

The Length field is set to 3

The Mobility Domain Identifier is a 2-octet value, following the ordering conventions from 7.1.1.

8.5a.4 PMK-R0

Change:

MDID is the 48-bit Mobility Domain Identifier field from the Mobility Domain Information element that was used during FT Initial Mobility Domain Association.

To:

MDID is the Mobility Domain Identifier field from the Mobility Domain Information element that was used during FT Initial Mobility Domain Association.

Annex D

Change  dot11FTMobilityDomainID object from:

SYNTAX OCTET STRING (SIZE(6))

to

SYNTAX OCTET STRING (SIZE(2))

References: 11-06-1895-07-000r-d4-comments.xls and comment #60 therein.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart@ok-brit.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This submission addresses comment number sixty by making the MDID two octets.