IEEE P802.11
Wireless LANs

| Comment Resolutions for CID 169, 191, 199 |
| --- |
| Date: 2007-01-02 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Emily Qi | Intel Corp. | 2111 NE 25th Ave Hillsboro OR 97229 | 503-264-7799 | Emily.H.Qi@intel.com |

Change 7.3.2.27 as follows:

7.3.2.27 Extended Capabilities information element

The Extended Capabilities information element carries information about the capabilities of an 802.11 STA, intended to augment the Capability Information Field (CIF) when these bits are fully allocated. The format of this information element is shown in Figure 93.

|  | Element ID Length | Length | Capabilities |
| --- | --- | --- | --- |
| Octets: | 1 | 1 | n |

Figure 93 - Extended Capabilities information element

The Element Identifier of this information element is 127.

The Value of the Length field is equal to the number of octets in the Capabilities field.

The Capabilities field is a bit field indicating the capabilities being advertised by the STA transmitting the information element. There are no capabilities defined for this field in this revision of the standard. The Capabilities field is shown in Table x-1.

Table x-1 The Capabilities field

| Bit | Information | Notes |
| --- | --- | --- |
| 0 | Reserved |  |
| 1 | Wireless Network Management | A STA shall set the Wireless Network Management bit field in the Extended Capabilities Information field to 1 if the STA’s dot11WirelessManagementImplemented is true; otherwise, it shall be set to 0. |
| 2-n | Reserved |  |

TGv Editor: Change 7.3.2.46 as marked with Microsoft Word’s “track changes”:

7.3.2.46 FBMS Response element

The FBMS Response defines information about the broadcast and multicast status. The format of the FBMS Response element is shown in 0.

|  | Element ID | Length | FBMS Status Element 1 | FBMS Status Element n |
| --- | --- | --- | --- | --- |
| Octets: | 1 | 1 | 5 | 5 |

Figure v80—FBMS Response element format

The Length field is set to 1+n, where n indicates the total length of all FBMS Status Elements contained in the IE.

The format of the FBMS Status Element is shown in 0.

|  | Element Status | Delivery Interval |  | FBMSID | FBMS Counter ID | Multicast Rate | Multicast Address | Multicast Diagnostic Interval |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Octets: | 1 | 1 |  | 1 | 1 | 1 | 6 | 4 |

Figure v81—FBMS Status Element format

The Element Status field defines the following values, as inidcated in 0.

Table v44—Element Status Definition

| Value | Description |
| --- | --- |
| 0 | Accept |
| 1 | Deny, due to malformed request or ambiguous classifier. |
| 2 | Deny, due to lack of resources on AP. |
| 3 | Deny, due to requested classifier(s) matching 2 or more existing streams on different intervals |
| 4 | Deny, by policy, requested stream is not permitted to participate in FBMS |
| 5 | Override, due to existing stream with different delivery interval |
| 6 | Override, due to policy limits on AP. |
| 7 | Override, due to AP changed the delivery interval. |
| 8 | Override, due to AP multicast rate policy |
| 9-255 | Reserved |

A status value of Accept is transmitted by the AP when the requested delivery interval is supported by the AP.

A status value of Deny is transmitted by the AP when the AP denies the STA’s requested delivery interval and TCLAS completely.

A status value of Override is transmitted by the AP when the AP denies the requested delivery interval but can support an alternate delivery interval for the requested TCLAS. The STA must comply with the AP’s override value. If the STA does not accept this overridden rate, then the STA must send a new request with the TCLAS IE removed.

The Delivery Interval defines the number of DTIMs that the stream is transmitted as defined by the AP.

The FBMSID is assigned by the AP and provides a unique identifier for this stream within the BSS.

The FBMSID Counter ID provides a unique identifier for this stream counter within the BSS.

The Multicast Rate specifies the data rate to be used for the multicast service.

The Multicast Address specifies the multicast MAC address for the multicast service.

The Multicast Diagnostic Interval specifies the number of beacon intervals for which the AP keeps multicast service traffic counts. The STA uses the Multicast Diagnostic Interval to determine how frequently to send Multicast Diagnostic Reports.

TGv Editor: Change Table v25 as marked with Microsoft Word’s “track changes”:

Table v25—Client Report for Group Type Operating Parameters contents

| Order | Information |
| --- | --- |
| 1 | MAC Address |
| 2 | Radio channels |
| 3 | Tx Power |
| 4 | Data Rates |
| 5 | SSID |
| 6 | Cipher Suite |
| 7 | AKM Suite |
| 8 | EAP Method |
| 9 | Profile ID |
| 10 | Power Save Mode |

TGv Editor: Change 7.3.2.38.5.21 as marked with Microsoft Word’s “track changes”:

          - Power Save Mode

The format for the Power Save Mode is shown in 0.

|  | Power Save Mode |
| --- | --- |
| Octets: | 1 |

Figure v58—Power Save Mode format

The Power Save Mode field indicates the STA’s current power save mode and is set to one of the values in 0.

Table v21—Power Save Mode definition

| Power Save Mode | Value |
| --- | --- |
| Awake | 0 |
| Normal Power Save | 1 |
| U-APSD | 2 |
| S-APSD | 3 |
| Reserved | 4–254 |
| Unknown | 255 |

# Text boxes

Abstract

This document is a normative text proposal to provide comment resolution for TGv Internal Review comment 169, 191 and 199.

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.