IEEE P802.11
Wireless LANs

| TGp LB 92 Comment Resolution Form |
| --- |
| Date: 2007-01-17 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Rick Noens | Motorola | 1301 E. Algonquin Rd. Schaumburg, IL 60196 | 847-576-1163 | Rick.Noens@Motorola.com |

|  | LB92 Comment Resolution |
| --- | --- |
| CID | Commenter: | Clause: | Addressed By: | Original Date Prepared |
| 438 | Parameswaran | 10.3.9.1.4 | Noens | 01/16/07 |

- COMMENT:  [From Spreadsheet]

"If the MIB attributes are not being set to their default values, WAVE mode MAC operation shall resume in less than 2 TUs after changing the value of the locally administered MAC address.". Why is there a 2 TU requirement. What is the time specification, when MIB attributes are not set to their default value?

- Commenter’s Suggested Remedy (If appropriate):  [From Spreadsheet]

Clarify why there is a  2TU time requirement. State what happens if the MIB attributes are not set to default values.

- Background, Explanation, Discussion, etc.:

The reason for a 2 TUs requirement was to facilitate channel switching and guarantee that operation will not be interrupted.  It may be advisable to include an explanation for this requirement within the informative section in the introduction to in the next draft.

- Recommended Resolution of the Comment:

Accept with modification.  Include explanation in for this requirement in the introduction portion of the next draft.

- Motion (if technical and/or significant):

(And instructions to the editor.)

Move to accept CID 438 with modification by including an explanation for the “2 TUs requirement” within the introducation section of the next draft of 11p.

Motion by: Rick Noens__________Date: _01/17/07________

Second:  ______________________

| Approve: | Disapprove: | Abstain: |
| --- | --- | --- |

References:

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart@ok-brit.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document describes proposed resolution to CID 438 resulting from LB92.