IEEE P802.11
Wireless LANs

| LB93 CID5628 Resolution |
| --- |
| Date: 2007-01-16 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Hui Ma | Huawei Technologies Co., Ltd | No.9 Shangdi Xinxi Rd., Haidian, Beijing, China | +86 10 82836437 | mah@huawei.com |

This text provides a resolution to CID5628 [1].

CID: 5628

Comment:

MPs in Power Save mode use the IBSS parameter to indicate traffic, however the description of the IBSS parameter Set in 802.11 draft9.0 is not available for MPs.

Proposed Change:

Recommended to add a description of the IBSS parameter Set in Beacon frame body

Resolution: Defer-NS

Proposed resolution

Corresponding changes in the text should be made in the following subclauses:

7.2.3.1 Beacon frame format

Change the contents of Table 8 as shown:

Table 8: Beacon frame body

| Orders | Information | Notes |
| --- | --- | --- |
| 4 | Service Set Identifier (SSID) | When dot11WLANMeshService is true but the interface on which the beacon is being sent is not configured as an Access Point, the SSID IE shall be set to the wildcard value. [Note: the SSID is a required IE in beacon frames. To avoid having non- mesh STAs send association requests to non-MAP Mesh Points, a valid SSID should not be included in beacons sent by non-MAP Mesh Points. To avoid backward compatibility issues, rather than removing the SSID IE from MP (non-MAP) beacons the wildcard value is used.] |
| 9 | IBSS Parameter Set | When dot11WLANMeshService is true, the IBSS Parameter Set informatin element is present only within Beacon frames generated by STA in an IBSS or MPs in Power Save mode. |
| (Ed: insert unchanged table entries for completeness) |
| 26 | OFDM Parameter Set | The OFDM Parameter Set information element is present within Beacon frames generated by STAs using Clause 17 PHYs. |
| 27 | Mesh ID | The Mesh ID information element shall be present within Beacon frames only when dot11WLANMeshService is true. |
| 28 | WLAN Mesh Capability | The WLAN Mesh Capability information element shall be present within Beacon frames only when dot11WLANMeshService is true. |
| 29 | Neighbor List | The Neighbor List information element shall be present within DTIM Beacon frames generated when dot11WLANMesh Service is true and MP is supporting Transmission to MP in power save mode. |
| 30 | DTIM | The DTIM IE shall be present in beacon frames generated by when dot11WLANMesh Service is true and MP is supporting Transmission to MP in power save mode. |
| 31 | Mesh Portal Reachability | The Mesh Portal Reachability information element shall be present within Beacon frames only when dot11WLANMeshService is true. |
| 32 | Beacon Timing | The Beacon Timing information element shall be present within Beacon frames only when dot11WLANMeshService is true. |
| 33 | MDAOP Advertisements | The MDAOP Advertisements information element shall be present within Beacon frames only when dot11WLANMeshService is true. |
| 34 | MDAOP Set Teardown | The MDAOP Set Teardown information element shall be present within Beacon frames only when dot11WLANMeshService is true. |
| 35 | MKDDIE | The MKDDIE element shall be present only when dot11WLANMeshService is true |

References:

[1] Draft Amendment: ESS Mesh Networking.  doc.: IEEE P802.11s/D1.0, November 2006.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

Proposed resolution text for CID5628