IEEE P802.11
Wireless LANs

| Protected Management Frames and Fast Roaming sync-up |
| --- |
| Date: 2007-01-30 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Kapil Sood | Intel Corporation | 2111 NE 25th Ave JF3-206 Hillsboro OR 97124 | +1-503-264-3759 | kapil.sood@intel.com |
| Nancy Cam-Winget | Cisco Systems | 190 W Tasman, San Jose CA 95134 | +1-408-853-0532 | ncamwing@cisco.com |
| Jesse Walker | Intel | 2111 NE 25th Ave JF3-206 Hillsboro OR 97124 | +1-503-712-1849 | jesse.walker@intel.com |
| Dorothy Stanley | Aruba | 1322 Crossman Ave, Sunnyvale, CA 94089 | +1-630-363-1389 | dstanley@arubanetworks.com |
| Abhijit Choudhury | Cisco Systems | 3625 Cisco Way, San Jose CA 95134 | +1-408-525-8682 | Abhijitc@cisco.com |

Remove the following from Clause 5.4.3.7

Management frame protection protocols apply to robust management frames after the RSNA PTK key establishment for protection of unicast frames is completed and after the GTKs to protect tbroadcast/multicast frames have been delivered.   All management frames sent or received by a STA before keys are installed shall be unprotected.

Insert the following as a new Clause 8.4.12

8.4.12 Robust Management Frame Selection procedure

If the AKM suite selected in the RSN IE is Suite Type 1 or 2, then Robust Management frame protection  shall apply to Robust Management frames after the RSNA PTK key establishment is completed and after the GTK and IGTK have been delivered.   All management frames sent or received by a STA before the keys are installed shall be unprotected.

If the AKM suite selected in the RSN IE is Suite Type 3 or 4, then Robust Management frame protection shall apply to Robust Management frames after the Fast BSS Transition protocol has completed, and the GTK and IGTK have been delivered.  All management frames sent or received by a STA before the keys are installed shall be unprotected.

Change Clause 6.1.2, Page 7 Lines 12

During the authentication exchange, both parties exchange authentication information as described in Clause 8 and 8A.

Change Clause 7.3.2.25, Page 8 Lines 31

03 40 // Robust Management frame protection is enabled

Change Clause 8.4.1.1, Page 17 Lines 7

- IGTKSA: A result of a successful Group Key Handshake, successful 4-Way Handshake, or the (Re) association Response message of the Fast BSS Transition protocol

Change Clause 8.4.1.1.3A, Page 17 Lines 14

The IGTKSA is unidirectional and is created by the 4-way Handshake, Fast BSS Transition protocol handshake, or the Group Key Handshake.  A Supplicant’s SME creates an IGTKSA when it receives Message 3 of the 4-Way Handshake, the (Re) association Response message of the Fast BSS Transition protocol, or Message 1 of the Group Key Handshake. The Authenticator’s SME creates an IGTKSA when it changes the IGTK with all STAs to which it has a valid PTKSA.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart@ok-brit.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document contains proposed changes to the TGw draft D1.0 to address comments (#452, 455, 467 – in Group 18).  This text proposes to sync-up the TGw draft D1.0 with Fast BSS Transition handshakes being developed by Task Group r.  It is expected (based on IEEE timeline) that TGr will complete before TGw, and hence, all changes from TGr must be rolled into TGw.

The diagrams for FT handshakes will be updated in a separate submission.