IEEE P802.11
Wireless LANs

| Proposed IBSS Comment Resolutions |
| --- |
| Date: 2007-01-30 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Jesse Walker | Intel Corporation | JF3-206, 2111 NE 25th Avenue, Hillsboro, OR | +1-503-712-1849 | jesse.walker@intel.com |
| Nancy Cam-Winget | Cisco Systems | 190 W Tasman, San Jose CA 95134 | +1-408-853-0532 | ncamwing@cisco.com |
| Abhijit Choudhury | Cisco Systems | 3625 Cisco Way, San Jose CA 95134 | +1-408-525-8682 | abhijitc@cisco.com |
| Kapil Sood | Intel Corporation | 2111 NE 25th Ave JF3-206 Hillsboro OR 97124 | +1-503-264-3759 | kapil.sood@intel.com |
| Dorothy Stanley | Aruba | 1322 Crossman Ave, Sunnyvale, CA 94089 | +1-630-363-1389 | dstanley@arubanetworks.com |

# Introduction

This submission proposes resolutions to CIDs 261, 265, 272, 273, and 604 from LB88.

# Proposed change of 8.4.4.2

Replace the text in clause 8.4.3 of P802.11w D1.01 with the following, renumbering the table as appropriate:

An RSNA-capable AP may choose to accept, as set in the policy variable dot11RSNALegacyManagementFrames, RSNA STAs with or without the capability for management frame protection set in the RSN IE. A STA may choose not to associate with an AP that does not advertise protection of Robust management frames in the RSN capabilities. In the case where an RSNA STA tries to associate without Robust Management frame protection, the AP shall reject the (Re)association if dot11RSNALegacyManagementFrames is set to false. Table XX details all the possibilities.

| AP’s State | Non-AP STA’s State | AP Action | STA/Supplicant Action |
| --- | --- | --- | --- |
| dot11RSNAProtectedManagementFramesEnabled = true | RSN IE Robust Mgmt Frame protection subfield = 1 | if STA’s RSN IE advertises a different Management Group Ciphersuite then AP shall reject (re)association request with Reason Code TBD else AP may accept (re)association request. The AP shall transmit and receive unicast Robust Management frames protected by the data pairwise ciphersuite, and broadcast/multicast Robust Management frames protected by the Management Group Ciphersuite. | if AP’s RSN IE advertises a different Management Group Ciphersuite then STA shall not (re)associate with this AP else STA may (re)associate with this AP. The STA shall transmit unicast Robust Management frames protected by the data pairwise ciphersuite, and broadcast/multicast Robust Management protected by the Management Group Ciphersuite. |
| dot11RSNAProtectedManagementFramesEnabled = true AND dot11RSNALegacyManagementFrames = true | RSN IE Robust Mgmt Frame protection subfield = 0 | AP may (re)associate with this STA. The AP shall transmit and receive unicast Robust Management frames unprotected; the AP shall protect broadcast/multicast Robust Management frames using the Management Group Ciphersuite. | The STA ignores all Robust Management frame protection. |
| dot11RSNAProtectedManagementFramesEnabled = true AND dot11RSNALegacyManagementFrames = false | RSN IE Robust Mgmt Frame protection subfield = 0 | AP shall reject any (Re)associate Request from this STA with reason code TBD | The STA may reassociate with this AP. |
| RSN IE Robust Mgmt Frame protection subfield = 0 | dot11RSNAProtectedManagementFramesEnabled = true AND dot11RSNALegacyManagementFrames = true | The AP ignores all Robust Management frame protection | The STA may reassociate with this AP. The STA shall transmit and receive unicast Robust Management frames unprotected. |
| RSN IE Robust Mgmt Frame protection subfield = 0 | dot11RSNAProtectedManagementFramesEnabled = true AND dot11RSNALegacyManagementFrames = false | The AP ignores all Robust Management frame protection | The STA shall not (Re)associate with this AP |

Table XX: Robust Management Frame selection in an ESS

Replace the text in clause 8.4.4.2 of P802.11w D1.01 with the following, renumbering the table as appropriate:

Robust Management frame protection is valid only if RSNA is selected to protect data messages and dot11RSNAProtectedManagementFramesEnabled is set to true.

In an IBSS two 4-Way Handshakes exchange RSN information elements to establish the security of the link between two STAs. The Robust Management frame capabilities are determined by the RSN information elements exchanged in the 4-Way Handshake initiated by the Authenticator of the STA with the larger MAC address.  Table XX details all of the possibilities.

| Local STA’s State | Peer STA’s State | Local STA’s Action |
| --- | --- | --- |
| dot11RSNAProtectedManagementFramesEnabled = true | RSN IE Robust Mgmt Frame protection subfield = 1 | if Peer STA’s RSN IE advertises a different Management Group Ciphersuite then The Local STA shall abort 4-Way Handshakes with the Peer STA else 4-Way Handshakes with the Peer STA may complete successfully. The Local STA shall transmit and receive unicast Robust Management frames protected by the data pairwise ciphersuite, and broadcast/multicast Robust Management frames protected by the Management Group Ciphersuite. |
| dot11RSNAProtectedManagementFramesEnabled = true AND dot11RSNALegacyManagementFrames = true | RSN IE Robust Mgmt Frame protection subfield = 0 | The Local STA may complete 4-Way Handshake with the Peer STA. The Local STA shall transmit and receive unicast Robust Management frames unprotected; the Local STA shall transmit broadcast/multicast Robust Management frames protected using the Management Group Ciphersuite, but receive broadcast/multicast Robust Management frames from the Peer STA unprotected. |
| dot11RSNAProtectedManagementFramesEnabled = true AND dot11RSNALegacyManagementFrames = false | RSN IE Robust Mgmt Frame protection subfield = 0 | The Local STA shall abort any 4-Way Handshakes with this Peer STA |

Table XX: Robust Management Frame selection in an IBSS

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart@ok-brit.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This submission proposes resolutions to CIDs 261, 265, 272, 273, and 604 from LB88.