IEEE P802.11
Wireless LANs

| Emergency Services Public Credentials Format |
| --- |
| Date: 2007-03-13 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Matthew Gast | Trapeze Networks | 5753 W. Las Positas Blvd Pleasanton, CA 94588 | +1 925 474 2273 | msg@trapezenetworks.com |

# Introduction

The current TGu draft uses the Emergency Services Realm to indicate to STAs how to associate to a network using the public credential method to place an emergency call.  Only the realm is specified by the current draft.  This submission changes the realm to a full NAI to allow the TGu-enabled network to supply the user name in addition to the realm.

## Changes to TGu draft 0.03:

## 3. Definitions

Remove the definitions for "Realm" and "Realm-based routing"

## 7.2 Format of individual frame types

### 7.2.3 Management frames

#### 7.2.3.1 Beacon frame format

Change the following row in table 8 as indicated:

Table 8—Beacon frame body

| Order | Information | Notes |
| --- | --- | --- |
| 29 | Default Emergency Services RealmNAI | Optional (present if configured) |

#### 7.2.3.8 Probe Request frame format

Change the following row in table 14 as indicated:

Table 14—Probe Request frame body

| Order | Information | Notes |
| --- | --- | --- |
| 6 | Default Emergency Services RealmNAI | Optional (present if configured) |

#### 7.3.2.44	Default Emergency Services RealmNAI Information element

Replace the existing text of this section and figure as follows:

The Default Emergency Service RealmNAI information element defined in Figure u14 provides a STA with information on which directly connected SSPN is configured as the default provider of emergency services for the BSS.  A STA using this field may be able to speed up the emergency call setup process when using the public credentials method.

|  | Element ID | Length | RealmNAI |
| --- | --- | --- | --- |
| Octets: | 1 | 1 | Variable |

Figure u14 - Default emergency services realm element description

The Length field shall be set to the length in octatesoctets of the RealmNAI field.

The RealmNAI field is a variable length field defined as the realm portion of the that contains user credentials that can be used to obtain emergency services.  It is formatted as a Network Access Identifiedr (NAI) as defined in RFC-4282.

## Annex P

## P.1.2 System Aspects for Emergency Call Support

Change the first bullet point on page 72 (lines 3-10) as follows:

- Using public user credentials (described further in P.1.5). In this situation, a STA uses the defined network selection method to query candidate SSPNs to determine which one (or several) support VoIP, end-to-end QoS and emergency services. Once this has been determined, the STA associates to the SSID corresponding to the chosen SSPN using public user credentials. Optionally, the AP may have been configured with a default realm (part of the NAI) user name and realm, present as the Emergency Services NAI, from which emergency services may be obtained. This information, if present/configured by the hotspot provider, may be used to speed up the emergency call setup process.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart@ok-brit.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This submission modifies the public credentials advertised for emergency services access to be a user name plus realm, rather than just a realm.