IEEE P802.11
Wireless LANs

| Clause 5 Comment Resolution to 802.11u-D0.03 |
| --- |
| Date: 2007-03-08 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Hong Cheng | Panasonic Singapore Laboratories | BLK1022 TaiSeng Ave #06-3530 TaiSeng Ind. Est. Singapore 534415 | +65 65505477 | hong.cheng@sg.panasonic.com |
| Necati Canpolat | Intel | 2111 NE 25th Ave, Hillsboro, OR 97124 | +1 503 264 8014 | necati.canpolat@intel.com |
| Srinivas Sreemanthula; | Nokia | 6000 Connection Drive, Irving, TX 75039 U.S.; | +1 972 8945000 | Srinivas.Sreemanthula@nokia.com; |

5. MAC sublayer functional description

5.2.7 Interworking basic service set: Interworking with external network

An Interworking capable AP can interact with external networks via a logical Interworking Interface. As shown in Figure u1, the Interworking Interface is a logical point that is distributed between AP and the SSPN. The information exchange over this interface provides means for AP to provision specific interworking services to the non-AP STA.. For example, this interface allows the AP to reach any SSPN for exchange of authentication, authorisation and accounting information for a specific non-AP STA in the pre-association and post-association states. The interworking information may be exchanged transparently through the Portal connecting the 802.xLAN.

Figure u1 IEEE802.11 interworking architecture

The Interworking interface allows the non-AP STA to transparently access the services provisioned in the SSPN via the currently associated BSS. However, certain interworking services also allow the non-AP STA to access services in networks other than the SSPN.

5.3.2 DSS

Insert the new service into the DSS service list below: f) QoS traffic scheduling (QoS facility only)

g) Interworking Serivce (Interworking capable network only)

Insert the following new sub-section in section 5.4 Overview of the services

5.4.7 Wireless LAN Interworking with External Networks

An interworking capable IEEE 802.11 STA may have a subscription relation with an external network, e.g. the SSPN. The establishment of such a relation is out of scope of this standard. For example, it could be part of a subscription plan of the user using the STA. With the interworking function, the IEEE802.11 AN allows the STA to access the services provided by the SSPN according to the subscription relation.

An overview of the interworking functions addressed in this specification is provided below:

- network selection of the current IEEE 802.11 network by consulting the SSPN

- emergency service provisioning at the IEEE 802.11 network level

- QoS map distribution

- Backend interface services between AP and the SSPN

In order to support the service provisioning, interactions between the IEEE802.11 AN and SSPN are necessary over the Interwork interface.

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@ok-brit.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document describes proposed text changes to resolve comments #20 to 25 of the TGu internal comment resolution summary 11-06-1857r8.

This document is based on P802.11u-d0.03 and P802.11ma-d9.