IEEE P802.11
Wireless LANs

| Report of Teleconference May 2nd for Comment Resolution of Beamforming in LB97 |
| --- |
| Date: 2007-05-02 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Joonsuk Kim | Broadcom | 190 Mathilda Place, Sunnyvale, CA94086 | 408-543-3455 | joonsuk@broadcom.com |

# CID 2728

| 2728 | 282.42 | 20.3.11.1 | I'm not sure the notation TX(RX) is clear. | Say: "of the form A_TX,k and A_RX,k" |
| --- | --- | --- | --- | --- |

Resolution: Counter.

Replace" A_TX(RX), k" with "A_TX,k and A_RX,k at STA A"

# CID 1814

| 1814 | 282.19 | 20.3.11.1 | error in formula |  |
| --- | --- | --- | --- | --- |

Resolution:  COUNTER. See CID#1604 and its resolution. Already resolved in Editorial comment with D2.01.

# CID 2371

| 2371 | 148.27 | 9.17.1 | "When using implicit feedback, the beamformer receives long training symbols, which allow the MIMO channel between the beamformee and beamformer to be estimated" The important aspect is that these are transmitted by the beamformee. | . insert "sent by the beamformee," after "long training symbols" |
| --- | --- | --- | --- | --- |

Resolution:  ACCEPT.

.

# CID 2372

| 2372 | 148.33 | 9.17.1 | "Generally, reciprocity requires calibrated radios in MIMO systems" This statement is too broad and awkward. | Reword thus: "Generally, the assumption of reciprocity of the channel between two radios in a MIMO system is only true if they are calibrated." |
| --- | --- | --- | --- | --- |

Resolution:  COUNTER.

Replace "Generally, reciprocity requires calibrated radios in MIMO systems" with "Generally, calibrated radios in MIMO systems may improve reciprocity."

# CID 2375

| 2375 | 149.64 | 9.17.2.1 | "If the STA is capable of implicit TxBF and the requesting STA is capable of receiving implicit TxBF, the sounding PPDU may be steered." There may be some confusion about which STA is which. | Reword thus: "If the beamformee is capable of implicit TxBF and the beamformer is capable of receiving implicit TxBF, the sounding PPDU may be steered." |
| --- | --- | --- | --- | --- |

Resolution:  COUNTER.

Replace quoted sentence with  "If the beamformee is capable of implicit TxBF and the beamformer is capable of receiving implicit TxBF, the sounding PPDU from the beamformee may be steered.".

# CID 2376

| 2376 | 150.09 | 9.17.2.1 | "In this case, response with NDP is allowed only when RDG/More PPDU subfield is set to 1 in the HT Control field that also contains TRQ= 1, as specified in 9.19.1 (NDP Rules)." This was changed in January. RDG is no longer required. | Remove the quoted sentence. |
| --- | --- | --- | --- | --- |

Resolution:  ACCEPT.

# CID 2380

| 2380 | 151.56 | 9.17.2.3 | PPDUs are either wholly steered or unsteered. Calling out unsteered or steered for the preamble and data parts is unnecessary. Same comment on figure n56 in the next subclause. | Use a device (e.g. cross-hatching) to indicate steered packets, and add a key to the diagram. Then remove the separate unsteereds from text and cross-hatch the steered PPDUs. |
| --- | --- | --- | --- | --- |

Resolution:  Withrawn by Adrian

# CID 2381

| 2381 | 152.24 | 9.17.2.3 | What this subclause doesn't say is under what conditions you can obtain bidirectional training. Clearly you can train bidirectionally whenever a sequence of frame exchanges occurs. But is it only worth training the reverse direction if STA B wants to send data? If so, then under what conditions can it sent date? The obvious answer is using reverse direction protocol. Are there any non-obvious answers - e.g. using QoS CF-Poll, or using a non-QoS CF-Poll? | It might help clarify matters to add the following note: "NOTE-The TRQ protocol is only used to manage the beamforming training process. By itself, it is not sufficient to permit STA B to transmit data. STA B can send data, for example, following the reverse direction protocol. Under this protocol, in the example shown in figure n56, all +HTC MPDUs transmitted by STA A also have the RDG/More PPDU field set to 1." |
| --- | --- | --- | --- | --- |

Resolution: COUNTER - Add a note "NOTE-The TRQ protocol used with the beamforming training process is not sufficient to permit STA B to transmit data frames in the reverse direction. In this example, shown in Figure n56, STA A would additionally have to follow the rules of the Reverse Direction Protocol (see 9.14 (Reverse Direction Protocol)).

# CID 3219

| 3219 | 148.54 | 9.17.2.1 | No matter whether it is unidirectional or bidirectional implicit beamforming, only the beamformer sends beamformed transmission | Replace "phi axis" and "psi axis" with "quantized phi" and "quantized psi", respectively. |
| --- | --- | --- | --- | --- |

Resolution:  Withdrawn by Joonsuk

# CID 2086

| 2086 | 46.38 | 7.3.1.30 |  |  | The second H in this sentence probably should be H_eff | Change to H_eff |
| --- | --- | --- | --- | --- | --- | --- |

Resolution:  Accept

# CID 2733

| 2733 | 288.15 | 20.3.11.2.3 |  |  | "‘s such as." What is the 's doing? Also "as" is not a good way to end a sentence. | replace with: "such as:". |
| --- | --- | --- | --- | --- | --- | --- |

Resolution:  Counter – remove [‘s] in line 15. The same for line 35 and 52, line 64.

# CID 3194,3195

| 3194 | 285.33 | 20.3.11.2.1 |  |  | Equation (20-75) is not fully correct. Variable k in the max{..} should be replaced with another variable name, for example z. | write max{ m_H(z) } z = -Nsr z = Nsr |
| --- | --- | --- | --- | --- | --- | --- |
| 3195 | 285.44 | 20.3.11.2.1 |  |  | Equation (20-76) is not fully correct. Variable k in the max{..} should be replaced with another variable name, for example z. | write max{ m_H(z) } z = -Nsr z = Nsr |

Resolution:  Accept – Replace “k” in max function to “z” < numerator in equation (20-75)> – three in total. And Replace “k” in max function to “z” numerator in equation (20-76)>– three in total.

Line 44, colon needs to be removed.

# CID 3203

| 3203 | 281.65 | 20.3.11 |  |  | For Non-Compressed & Compressed Beamforming feedback, the receiver does not generate Qk | Replace the following sentence "on whether the transmitter or the receiver generates Qk" with "on whether the beamformer generates Qk or the beamformee provides feedback information for the beamformer to generate Qk." |
| --- | --- | --- | --- | --- | --- | --- |

Resolution:  Accept

# CID 3212

| 3212 | 288.09 | 20.3.11.2.3 |  |  | In compressed feedback, the angles shall be found as described in 20.3.11.2.3 | Replace "may be found …" with "shall be found…" |
| --- | --- | --- | --- | --- | --- | --- |

Resolution:  Counter - Replace "may be found to make the first column of D1*V to all be .." with "shall satisfy the constraint that all elements in the first column of D1*V are .."

# CID 3213

| 3213 | 288.00 | 20.3.11.2.3 |  |  | In compressed feedback, the angles shall be found as described in 20.3.11.2.3 | Replace "may be applied" with "shall be applied" in line 27 and "may be found …" with "shall be found…" in line 30. |
| --- | --- | --- | --- | --- | --- | --- |

Resolution:  Counter - Replace "may be found to make the second column of D2* x diag(1,V2) to be all .." with "shall satisfy the constraint that all elements in the second column of D2* x diag(1,V2) are .." in line 30. And, Replace "this process may be applied" with "this process is applied" in line 27.

# CID 3214

| 3214 | 288.47 | 20.3.11.2.3 |  |  | In compressed feedback, the angles shall be found as described in 20.3.11.2.3 | Replace "This process may continue …" with "This process shall continue…" |
| --- | --- | --- | --- | --- | --- | --- |

Resolution:  Counter - Replace "This process may continue …" with "This process continues .."

# CID 3217

| 3217 | 50.04 | 7.3.1.32 |  |  | Table n21, the name of tables sounds strange. | Replace "phi axis" and "psi axis" with "quantized phi" and "quantized psi", respectively |
| --- | --- | --- | --- | --- | --- | --- |

Resolution:  Accept

Reference: 11-07-0580-00-000n-proposed-comment-resolutions-implicit-transmit-beamforming.doc

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart@ok-brit.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document reports resolutions to LB97 comments on Beamforming adhoc teleconference call on May 2nd, 2007. These resolutions are agreed in the Beam adhoc teleconference call.

Attendee:

Joonsuk Kim		Broadcom

Paul Feinberg		Sony

Bjorn Andre Bjerke		Qualcomm

Adrian			Intel

Eldad			Intel

Vinko			Broadcom

Doug			Cisco

Sanjiv			Qualcomm

Solomon			Intel

Mike			Metalink

Jim			Conexant

Bruce			Marvell