IEEE P802.11
Wireless LANs

| TGy LB106 Submission for misc PHY CIDs |
| --- |
| Date: 2007-07-02 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Vinko Erceg | Broadcom Corporation |  |  | verceg@broadcom.com |

# Proposed Resolutions

| 2024 | 17.3.6 | 29 | 58-61 | "For improved spectrum sharing in some bands, an optional Clear Channel Assessment-Energy Detect (CCAED) may be used. The behavior class indicating CCA-ED is given in Table I.3. The regulatory classes requiring the corresponding CCA-ED behavior class are given in Annex J." In this paragraph optional CCA-ED is defined that actually becomes mandatory for the 3.65 GHz band in Annex I and J. I don't think that this is a good way of writing a spec: optional that is actually mandatory is very confusing. | In some way relate CCA-ED to only regulatory classes in Annex I and J that are required to have CCA-ED, i.e. 3.65 GHz band. Wording "optional CCA-ED" is very confusing. Avoid using optional in the text. I understand that this may be a tricky task but I believe that it has to be done. |
| --- | --- | --- | --- | --- | --- |

| 2025 | 17.3.10.5 | 32 |  | In this subclause new CCA-ED definition should be related only to the 3.65 GHz frequency band. One may interpret that the new CCA-ED definition is for all clause 17 devices, text is not clear. Also it seems like that the "optional CCA-ED" is actually mandatory for 3.65 GHz based on Annex I and J. How can "optional CCA-ED" be actually mandatory? Wording "optional" is quite confusing. | Relate CCA-ED to only regulatory classes in Annex I and J that are required to have CCA-ED, i.e. 3.65 GHz band. Wording "optional CCA-ED" is very confusing. Avoid using optional in the text. |
| --- | --- | --- | --- | --- | --- |

Proposed Resolution to CIDs 2024 and 2025:

Option A: Withdrawn by the commenter (Vinko Erceg)

Option B:

- Introduce Regulatory Enabled (RE) CCA-ED instead of Optional CCA-ED.

- Regulatory classes requiring the RE CCA-ED are given in Annex J.

- The above removes “optional” CCA-ED for other frequency bands that was inserted by TGy into Clause 17.

| 2026 | 17.3.10.5 | 32 | 32-42 | "For the optional CCA-ED, the OFDM PHY shall provide the additional capability to perform CCA-ED. The CCA shall indicate BUSY if there is any energy above the ED threshold or CS." In these sentence there is a "shall" statement for "optional". If something is "optional" then usage of "shall" seems to be incorrect. | Change the sentence to: "For the optional CCA-ED, the OFDM PHY provides the additional capability to perform CCA-ED. The CCA indicates BUSY if there is any energy above the ED threshold or CS." |
| --- | --- | --- | --- | --- | --- |

Proposed Resolution: Accept

TGy Editor: In D3.0,  pg 32, ln 32-4, modify the sentences as follows:

"For the optional CCA-ED, the OFDM PHY shall provides the additional capability to perform CCA-ED. The CCA shall indicates BUSY if there is any energy above the ED threshold or CS."

| 2027 | A.4.8 | 35 | 15 | Is "CCA-ED energy detect with OFDM CS" needed? | If not required, please remove "CCA-ED energy detect with OFDM CS" from the table. |
| --- | --- | --- | --- | --- | --- |

Proposed Resolution: Accept

TGy Editor: In D3.0,  pg 35, ln 15, delete the following row from the Table that includes the following sentence:

"CCA-ED energy detect with OFDM CS"

| 2071 | 17.3.9.2 |  |  | I remember the discussion in the group about what "more stringent" means. As I remember it, the intent of the resolution was to require the actual mask to be the more stringent of regulatory and default masks at all frequency points. The outcome in D3.0 is different. Provided that one of the regulatory mask points is more stringent than the default, the entire regulatory mask will be used, even if all its other points are more relaxed. | Replace with something like: "In the absence of a regulatory mask, use the mask defined here. In presence of a regualtory mask, the device shall meet both the requirements of the regulatory mask and the mask defined here -i.e., its emissions shall be no higher at any frequency offset than the minimum of the values specified in the regulatory and default masks." |
| --- | --- | --- | --- | --- | --- |

Proposed Resolution: Accept

TGy Editor: In D3.0,  pg 30, ln 35, add the following paragraph:

In the absence of a regulatory mask, use the mask defined here. In presence of a regualtory mask,  the device shall meet both the requirements of the regulatory mask and the mask defined here -i.e.,  its emissions shall be no higher at any frequency offset than the minimum of the values specified in the regulatory and default masks.

TGy Editor: In D3.0,  pg 30, ln 36, modify the text as follows:

“In the absence of a more stringent transmit spectrum mask by regulatory domain in Annex I, Ffor operation using 10 MHz channel spacing, the transmitted spectrum shall have a 0 dBr bandwidth not exceeding 9 ..”

TGy Editor: In D3.0,  pg 30, ln 44, modify the text as follows:

In the absence of a more stringent transmit spectrum mask by regulatory domain in Annex I, Ffor operation using 5 MHz channel spacing, the transmitted spectrum shall have a 0 dBr bandwidth not exceeding 4.5 MHz, –20 dBr at 2.75 MHz frequency ..”

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart@ok-brit.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document contains proposed changes to the IEEE P802.11y Draft to address the following LB106 comments:

CIDs: 2024, 2025, 2026, 2027, and 2071.

The changes marked in this document are based on TGy Draft version P802.11y D3.0.pdf.